## Slide 1
CYB530
Computer Networks
Dr. Khaled ELMenshawy
Lecture (01)
Introduction to Computer Networks and the Internet

## Slide 2
Objectives
Lecture (01)
Understand the meaning of network.
Recognize the different types of network.
Understand the network topologies.
Recognize the different types of network devices and their functions.
Understand the Internet evolution.
Define network protocols.
Understand the different types of Internet connection and their properties.

## Slide 3
What is Computer Networks?
Lecture (01)
A collection of computers, servers, mainframes, network devices, or other devices connected to one another allowing for data to be shared and used.

## Slide 4
Network Types
Lecture (01)
Personal Area Network (PAN):
PAN is a computer network organized around an individual person within a single building. This could be inside a small office or residence. A typical PAN would include one or more computers, telephones, peripheral devices, video game consoles and other personal entertainment devices.
Local Area Network (LAN):
LAN is a computer network that connects servers and personal computers within the same building.

## Slide 5
Network Types
Lecture (01)
Campus Area Network (CAN):
CAN is a group of LANs that connects (more than one building) within the same property.
Metropolitan Area Network (MAN):
MAN is a group of LANs or CANs that connects buildings in multiple properties but within the same city (Metropolitan).

## Slide 6
Network Types
Lecture (01)
Wide Area Network (WAN):
WAN is a LANs, CANs, or MANs that connects all within the same country or countries.
Virtual Private Network (VPN):
VPN allows a secure connection to the WAN, thus protecting your data and device from attack.

## Slide 7
Network Types
Lecture (01)
Enterprise Private Network (EPN):
EPN is a computer network that is entirely controlled by one organization, and it is used to connect multiple locations.
Storage Area Network (SAN):
SAN is a dedicated network of storage devices used to provide a pool of shared storage that multiple computers and servers can access. Storing data in centralized shared storage architecture allows organizations to manage storage and apply consistent policies for security, data protection, and disaster recovery.

## Slide 8
Network Topologies
Lecture (01)
What is a network topology?
Networks topology is the shape of a local area network (LAN) or other communications system, or in other words, the ways of connecting computers.

## Slide 9
Network Topologies
Lecture (01)
Bus topology:
All computers are connected to a single wire (the bus) that has two endpoints.
A single break to the cable would take down the entire network. The broken ends on a bus topology network do not have the necessary termination, which causes reflection between computers that are still connected.
Terminators should be used at each end of a bus segment to prevent a signal from bouncing.

## Slide 10
Network Topologies
Lecture (01)
Ring topology:
All computers are connected on the network with a ring of cable.
Data is passed around the ring from computer to another in the same direction, with no end to the cable, ring networks require no termination. A break in a ring topology network breaks the circuit, stopping the data flow.

## Slide 11
Network Topologies
Lecture (01)
Star topology:
All computers are connected through a central control unit. A single break to a cable would only take down communication to one computer. A central control unit failure would take down the entire network.

## Slide 12
Network Topologies
Lecture (01)
Hybrid topology:
Any form of networking technology that combines a physical topology with a signaling topology is called a hybrid topology.
There are only two hybrid topologies, star-ring topology, and star-bus topology.
Star-Ring topology:
Shrinking the ring into a small box.
Star-Bus topology:
Shrinking the bus into a small box.

## Slide 13
Network Topologies
Lecture (01)
Mesh topology :
All computers are connected to all other computers. If all computers are directly connected to other computers without any routes between them, this called a fully meshed topology network. if every computer connects to every other computer via two or more routes, this called a partially meshed topology network.

## Slide 14
Network Topologies
Lecture (01)
Point-to-Multipoint topology:
A single system acts as a common source through which all members of the Point-to-Multipoint network converse. The Point-to-Multipoint topology is physically similar to the star topology, but the difference is that a point-to-multipoint topology requires an intelligent device in the center.

## Slide 15
Network Topologies
Lecture (01)
Point-to-Point topology:
Two computers connect directly together with no need for a central device of any kind. Point-to-Point topology implemented in both wired and wireless networks.

## Slide 16
Network Devices
Lecture (01)
Modem:
Used in dial-up connections over standard analog telephone lines. It can be internal or external device.

## Slide 17
Network Devices
Lecture (01)
Network Interface Card (NIC):
Used to connect system to physical network media. It can be integrated into the system motherboard or as expansion card. Also, it can be wired or wireless NIC.

## Slide 18
Network Devices
Lecture (01)
Hexadecimal | 7 | D | E
Order | 2 | 1 | 0
Weight | (162) =256 | (161) =16 | (160) =1
Values | 7 × 256 = 1792 | 13 × 16 =208 | 14 × 1 = 14
An overview of Hexadecimal numeral system:
Hexadecimal system consists of ten numbers (0,1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, and F), where A=10, B=11, C=12, D=13, E=14 and F=15, Thus:
Digits: 0,1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F, Base: Sixteen (16), since there are sixteen digits to represent this numeral system.
The decimal value of this hexadecimal number equals the summation of all values for each position within this number set (7DE)16= 1792 + 208 + 14 = (2014)10
Weight= (Base)order, Values= (The number that exist in this position) X (Weight of this position).

## Slide 19
Network Devices
Lecture (01)
Inside every NIC, burned onto some type of ROM chip, is special firmware containing a unique identifier with a 48-bit value called the Media Access Control address, or MAC address.
MAC address is 12 hexadecimal characters. Because each hex character represents 4 bits, it takes 12 hex characters to represent 48 bits (6 Byte).
The MAC address E0-69-95-90-8B-C3, The first six digits, E0-69-95; represent the number of the NIC manufacturer, no other manufacturer may use them. The last six digits, 90-8B-C3, are the manufacturer’s unique serial number for that NIC.

## Slide 20
Network Devices
Lecture (01)
Repeater:
It deals with attenuation issues. It takes the signal in one port and transmitted out the other.
HUB:
It is a multi-port repeater. It takes the signal in one port and transmitted out to all other ports.

## Slide 21
Network Devices
Lecture (01)
Bridge:
It connects two systems, or two segments of the same LAN that use the same protocol.
Switch:
It is basically a multi-port bridge that can connects more than one system to each other.

## Slide 22
Network Devices
Lecture (01)
Router:
It can connect two or more different networks to each other

## Slide 23
Network Devices
Lecture (01)
Wireless access point:
It is basically the same thing as HUB, but the connection is made via airwaves rather than cable.

## Slide 24
What is the Internet?
Lecture (01)
The Internet is a worldwide collection of separate, but interconnected, networks accessed daily by millions of people using a variety of devices to obtain information, disseminate information, access entertainment.
The Internet (Capital “I”) is a specific name given to the communication network comprised of hundreds of thousands of inter-connected networks.
Network A
Network B
Network C
Connection between networks

## Slide 25
What is the Internet?
Lecture (01)
The roots of the Internet began with an experimental project called ARPANET stands for (Advanced Research Projects Agency Network) created by The U.S. Department of Defense in 1969 associated with Massachusetts Institute of Technology (MIT), after the Russian’s launched Sputnik, the first satellite.

## Slide 26
What is the Internet?
Lecture (01)
In 1974 Bob Kahn and Vint Cerf invented the Transmission Control Protocol (TCP) which moves data on the modern Internet which became the standard networking protocol on the ARPANET.
Hi, I would like to talk, here is the information that you need to communicate with me.
Thanks, I got it, here is the information that you need to communicate with me.
Ok, I got it, let's being talking.
PC 1
PC 2
PC 1
1
2
3

## Slide 27
What is the Internet?
Lecture (01)
What is a Protocol?
A protocol is a set of rules and instructions used for transmitting data between two devices. The protocol determines the following:
The type of error checking to be used.
Data compression method, if any.
How the sending device will indicate that it has finished sending a message.
How the receiving device will indicate that it has received a message.
What is a Port?
A port is a location where information is sent through. For example, http connection uses port no. 80.

## Slide 28
What is the Internet?
Lecture (01)
Examples of protocols:
Transmission Control Protocol (TCP): One to One connection, Connection-Oriented, and segment sequencing, and Reliable communication, acknowledgement.
User Datagram Protocol (UDP): Connectionless, No acknowledgement, and Unreliable communication, and no sequencing.
Hyper Text Transfer Protocol (HTTP): HTTP is used to transfer web pages from web server to client web browser.
File Transfer Protocol (FTP): used to download a file from a server using the Internet or to upload a file to a server.

## Slide 29
What is the Internet?
Lecture (01)
In 1971 Ray Tomlinson developed the first email programs called SNDMSG and READMAIL .

## Slide 30
What is the Internet?
Lecture (01)
1973-1975: Robert Metcalfe develops a system which replaces radio transmission of network data with a cable that provides a larger amount of bandwidth, enabling the transfer of millions of bits of data per second in comparison with the thousands of bits per second when using a radio channel transmission. This system is originally known as the Alto Aloha network, but which was later known as Ethernet.

## Slide 31
What is the Internet?
Lecture (01)
1982-1983: ARPANET is split into two separate entities: MILNET to serve the needs of national defense and the military community and ARPANET which is primarily utilized by academics and researchers. This is the first step toward the commercialization of the Internet.

## Slide 32
What is the Internet?
Lecture (01)
In 1984: computer scientists (Paul Mockapetris, Jon Postel, and Craig Partridge) begin to consider new methods of naming and addressing users and networks. The Domain Name System (DNS), first defined to divide Internet names between host names (x.com) and usernames (user@x.com).

## Slide 33
What is the Internet?
Lecture (01)
1988: Internet Assigned Numbers Authority (IANA) established to distribute IP number to Internet users.
In 1998: Internet Corporation for Assigned Names and Numbers (ICANN) which is responsible for coordinating the management of the technical elements of the DNS to ensure universal resolvability so that all users of the Internet can find all valid addresses.
ICANN is the institution which runs IANA.

## Slide 34
Types of connections
Lecture (01)
Internet service providers (ISPs):
ISPs are businesses or other organizations that provide Internet access to others. In 1990 the first Internet service provider (ISP) was “World.Std.com”.
Internet service providers (ISPs)

## Slide 35
Types of Internet connection
Lecture (01)
Dial-up connection:
This type of connection uses dial-up modem connected to a standard telephone jack with regular telephone cabling.
Advantages:
It is including inexpensive hardware, ease of setup and use, and widespread availability.
Disadvantages:
It is slow connection speed (a maximum of 56 Kbps) and cannot make or receive phone calls while connecting to the Internet.

## Slide 36
Types of Internet connection
Lecture (01)
Cable connection:
A Cable is a dedicated connection between the user's premises and the local exchange. It is fixed bandwidth and offers identical upload and download speeds up to 100 Mbps and requires a cable modem.
Advantages:
Faster download and upload speed, it does not require any phone service to operate.
Disadvantages:
During peak hours, the data transfer speed gets low, and it is a bit expensive.

## Slide 37
Types of Internet connection
Lecture (01)
Broadband over Fiber (BoF):
Fast direct connection available to homes and businesses in areas where there is fiber-optic cabling available. download speeds for BoF service typically range between 15 Mbps and 150 Mbps.
Advantages:
Extremely High Bandwidth. The volume of data that fiber optic cables transmit per unit time is far great than copper cables, enables signals can be transmitted to a longer distance than copper cables, and resistance to Electromagnetic Interference.
Disadvantages:
Optical fiber cables are made of glass, which lends to they are more fragile than electrical wires, Difficult to Install, and as transmission distance getting longer, light will be attenuated and dispersed.
.

## Slide 38
Types of Internet connection
Lecture (01)
DSL/ADSL connection:
DSL (Digital Subscriber Line) and ADSL (Asymmetric Digital Subscriber Line) Internet access is a type of direct connection that transmits via standard telephone lines. DSL/ADSL modem is available only to users who are relatively close (within 5 kilometers) to a telephone switching station (Central).
Advantages:
Deliver download speed up to 100 Mbps, widely used since it depends on telephone landline, and reasonable cost depend on required speed.
Disadvantages:
Slow speed at peak times, the quality of the copper cables can affect the performance of the DSL/ADSL, and the quality of the service is dependent on the distance from a telephone switching station (Central).

## Slide 39
Types of Internet connection
Lecture (01)
Satellite :
Satellite Internet access uses a direct connection, but it is slower and more expensive than leased line or DSL/ADSL access (around 10 Mbps). It requires a satellite modem and a transceiver satellite dish mounted outside the home or building .
Advantages:
It has a higher availability rate than DSL or cable, easily used in areas where other internet options are not available.
Disadvantages:
It is difficult to troubleshoot the system, it delivers poor quality internet during bad weather conditions, and it suffer from Latency which is a delay in service caused by the amount of time it takes to transfer a signal to and from a satellite.

## Slide 40
Types of Internet connection
Lecture (01)
Mobile Internet :
It used with smartphones and media tablets to keep them connected to the Internet via a cellular network. The speed of mobile wireless depends on the cellular standard being used, 3G networks have speeds between 1 and 4 Mbps; 4G networks are often between 3 and 15 Mbps and sometimes more.
Advantages:
Using internet while moving from one place to the other, and it does not need any extra hardware or software to connect to the Internet.
Disadvantages:
weak mobile network signal leads to poor connection, and extra cost for data plane provided by mobile network provider.

## Slide 41
Thank you
Lecture (01)