## Slide 1
Static Routing & Router Basic Configuration
CCNA (200-301) Cisco Certified Network Associate
Prepared by Eng. Taghreed Elsayed
Lecture 5

## Slide 2
Chapter
03
Static Routing
General Role of the Router
Functions of a Router
  Best Path Selections
  Forwarding packets to destination
Introducing the Topology
  3 1800 series routers connected via WAN links
  Each router connected to a LAN represented by a switch and a PC

## Slide 3
Chapter
03
General Role of the Router
Connections of a Router for WAN
  -A router has a DB-60 port that can support 5 different cabling standards
Connections of a Router for Ethernet
  -2 types of connectors can be used: Straight through and Cross-over
  Straight through used to connect:
    -Switch-to-Router, Switch-to-PC, Router-to-Server, Hub-to-PC, Hub-to-Server
  Cross-over used to connect:
    -Switch-to-Switch, PC-to-PC, Switch-to-Hub, Hub-to-Hub, Router-to-Router
Static Routing

## Slide 4
Chapter
03
Interfaces
Examining Router Interfaces
  -Show IP router command – used to view routing table
  -Show Interfaces command – used to show status of an interface
  -Show IP Interface brief command – used to show a portion of the interface information
  -Show running-configuration command – used to show configuration file in RAM
Static Routing

## Slide 5
Chapter
03
Interfaces
Configuring a Serial interface
  -Enter interface configuration mode
  -Enter in the ip address and subnet mask
  -Enter in the no shutdown command
Example:
  -R1(config)#interface serial 0/0
  -R1(config-if)#ip address 172.16.2.1 255.255.255.0
  -R1(config-if)#no shutdown
Static Routing

## Slide 6
Chapter
03
Interfaces
Examining Router Interfaces
  -Physically connecting a WAN Interface.
  -A WAN Physical Layer connection has sides:
    Data Circuit-terminating Equipment (DCE) – This is the service provider. CSU/DSU is a DCE device.
    Data Terminal Equipment (DTE) – Typically the router is the DTE device.
    #show controller s0/0/1
Static Routing

## Slide 7
Chapter
03
Interfaces
Configuring serial links in a lab environment
  One side of a serial connection must be considered a DCE
  This requires placing a clocking signal – use the clock rate command.
  Example:
    -R1(config)#interface serial 0/0
    -R1(config-if)#clock rate 64000
  Serial Interfaces require a clock signal to control the timing of the communcations.
Static Routing

## Slide 8
Chapter
03
Routing Table and CDP Protocol
When a router only has its interfaces configured & no other routing protocols are configured then:
  -The routing table contains only the directly connected networks
  -Only devices on the directly connected networks are reachable
Static Routing

## Slide 9
Chapter
03
Routing Table and CDP Protocol
Static Routing

## Slide 10
Chapter
03
Routing Table and CDP Protocol
Purpose of CDP
  A layer 2 cisco proprietary tool used to gather information about other directly connected Cisco devices.
Concept of neighbors
  -2 types of neighbors
    Layer 3 neighbors
    Layer 2 neighbors
Static Routing

## Slide 11
Chapter
03
Routing Table and CDP Protocol
CDP(cisco discovery protocol) show commands
  Show cdp neighbors command
    -Displays the following information:
      Neighbor device ID
      Local interface
      Hold time value, in seconds
      Neighbor device capability code
      Neighbor hardware platform
      Neighbor remote port ID
  Show cdp neighbors detail command
    -Useful in determining if an IP address configuration error
Static Routing

## Slide 12
Chapter
03
Routing Table and CDP Protocol
Disabling CDP
  To disable CDP globally use the following command
    Router(config)#no cdp run
Static Routing

## Slide 13
Chapter
03
Routing : the process of selecting best path to forward the packets
Purpose of a static route
  A manually configured route used when routing from a network to a stub network
Static Routing
Dynamic Routing
Routing Types
Static Routing

## Slide 14
Chapter
03
Static Routes with Exit Interfaces
Purpose of a static route
  A manually configured route used when routing from a network to a stub network
Static Routing

## Slide 15
Chapter
03
Static Routes with Exit Interfaces
IP route command
  To configure a static route use the following command: ip route
  Example:
    -Router(config)# ip route network-address subnet-mask {ip-address of next hop | exit-interface }
Static Routing

## Slide 16
Chapter
03
Static Routing

## Slide 17
Chapter
03
Static Routing

## Slide 18
Chapter
03
Static Routing