## Slide 1
Prepared by
Dr. Rasha B. AL Jerd
Project Cost Management
Lecture 5
PMG 213

## Slide 2
Project Cost Management
Lecture 5
PMG 213

## Slide 3
Cost Estimating
Project Cost
Management
PMG 213
Prepared by
Dr. Rasha B. AL Jerd

## Slide 4
Cost Estimating Outlines:
3.2 OPERATING COST ESTIMATION
3.2.1 Definitions
3.2.2 Purposes of Operating Cost Estimates
3.2.3 Raw Materials and Utilities
3.2.4 Operating Labor
3.2.5 Maintenance
3.2.6 Indirect Payroll Cost
3.2.7 Operating Supplies
3.2.8 Laboratory and Other Service Costs
3.2.9 Royalties and Rentals
3.2.10 Indirect Costs
3.2.11 Distribution Costs
3.2.12 Avoidance of Nuisances
3.2.13 Contingencies
3.2.14 Shortcut Methods
3.2.15 Components of Total Product Cost
3.3 SUMMARY

## Slide 5
3.2 OPERATING COST ESTIMATION
3.2.1 Definitions
Operating Cost (or manufacturing cost): the expenses incurred during the normal operation of a facility, or component, including labor, materials, utilities, and other related costs.
Overhead: a cost or expense inherent in the performing of an operation, i.e., engineering, construction, operating or manufacturing, which cannot be charged to or identified with a part of the work, product or asset and, therefore, must be allocated on some arbitrary base believed to be equitable, or handled as a business expense independent of the volume of production. Plant overhead is also called factory expense.
Direct Costs: the portion of the operating costs that is generally assignable to a specific product or process area.
Indirect Costs: costs not directly assignable to the end product or process, such as overhead and general purpose labor, or costs of outside operations, such as transportation and distribution.

## Slide 6
Examples:
Operating Cost:
The plant spends $1,500,000 annually on raw materials, utilities, and labor to run the facility
Overhead: Plant security, general facility lighting, and administrative salaries total $150,000/year. These cannot be linked to a single batch of product
Direct Costs: $800,000 spent directly on purchasing raw material.
Indirect Costs: $60,000 paid to an external trucking logistics provider to deliver final products to regional distributors

## Slide 7
3.2.2 Purposes of Operating Cost Estimates:
Operating cost estimates can be important from several standpoints:
They are necessary in order to determine the potential profitability of a product or process, and are very useful for screening alternative project possibilities.
Frequently they can act as a guide to pinpoint potential areas in which to conduct research and to evaluate the commercial viability of research results. And they provide a tool for sensitivity analysis for individual components. It is very important to remember to perform operating cost estimates at both full and reduced capacities for the operating system in question.

## Slide 8
3.2.2 Purposes of Operating Cost Estimates (continued):
It is not uncommon for a system to be highly efficient at full capacity, but very inefficient when operating at less than design capacity. The important question to be answered is what range of operations can a plant operate over and still make a profit. Such costs can be calculated either as stand-alone estimates or as incremental costs for specified projects. Depending upon the situation, these different viewpoints could result in different decisions.

## Slide 9
-Capacity Example:
At 100% capacity (5,000 tons), total operating cost is $1,500,000, making the unit cost $300 per ton.
At 50% capacity (2,500 tons), fixed expenses remain high, so the operating cost only drops to $1,125,000, driving the unit cost up to $450 per ton.
This demonstrates why estimating at reduced capacity is vital to finding the true profit range.

## Slide 10
Commonly, three differing bases for comparison are used, although others may be used for special applications. The most common three are:
• Daily cost
• Cost per unit-of-production
• Annual cost
Using our previous 100% capacity data:
Annual Cost: $1,500,000 per year (capturing summer peak utility rates and scheduled winter maintenance shutdowns)
Daily Cost: $1,500,000 divided by 300 operating days = $5,000 per day.
Cost per Unit-of-Production: $1,500,000 divided by 5,000 tons = $300 per ton

## Slide 11
For some manufacturing considerations, a cost-per-unit analysis can be valuable.
When making comparisons, it is very important to make sure each calculation is made using the same techniques and assumptions. Otherwise, comparisons may not be valid.
All other factors being equal, making comparisons using an annualized basis instead of on shorter time increments has a number of advantages:

## Slide 12
• Seasonal variations are evened out.
• On-stream time factors are considered.
• More accurate analysis of less-than-full capacity situations is obtained.
• Infrequently occurring large expenses are factored in (scheduled maintenance, vacation shutdowns, catalyst changes, etc.).
• The output is in a form easily used in standard profitability analysis.
• The annual basis is readily convertible to the other bases, daily cost and unit-of-production, yielding mean annual figures rather than a potentially high or low figure for an arbitrarily selected time of year.

## Slide 13
Lecture 5
3.2.3 Raw Materials and Utilities
Raw materials and/or utilities are frequently the largest operating cost being considered in an estimation. The estimations involving raw materials are not always straightforward, as the following list of considerations shows:
• Raw materials frequently are the largest operating cost.
• By-products and scrap may be a debit or credit.
• Prices may be obtained either from suppliers or from published data.
• Raw materials costs may vary significantly depending upon the quality required (concentration, acceptable impurity levels, etc.).

## Slide 14
Lecture 5
3.2.3 Raw Materials and Utilities (continued):
• Raw materials costs entail quantity discounts in many cases leading to a trade-off of lower prices for purchase of large quantities vs. storage and inventory cost for raw materials that cannot be used immediately.
• Raw materials costs vary significantly depending upon the mode of purchase and transport (bulk quantities, truck lots, rail car lots, pipeline delivery, bags, boxes, etc).
• Supplies and catalysts are sometimes considered to be raw materials.
• Fuels may be either raw materials or utilities.
• Freight and handling costs must be included in pricing raw materials.

## Slide 15
As this list illustrates, accepted local practice can have a large impact on the operating cost estimate.
The cost of utilities can vary widely with the location, with the size of the service required, with the national and local economy, and even with the season.
Utilities must be examined closely on a local basis, especially if they form a major part of the operating costs.
Generally utility pricing is regulated and the approved tariffs are readily available from the utility company or the cognizant regulatory agency.
However, if the utilities are internally generated within a process, a separate estimate of the utility cost must be performed.

## Slide 16
Raw Materials: Buying raw chemical elements in small bags costs $150/ton. However, the plant utilizes a quantity discount by ordering rail car lots, dropping the price to $120 per ton
Freight and Handling: $10 per ton is added for rail transport and unloading labor
Utilities: Local regulated industrial electricity tariff is $0.10 per kWh during regular seasons but rises to $0.14 per kWh during the peak summer season

## Slide 17
3.2.4 Operating Labor
The best estimates of operating labor are based on a complete staffing table. This table should indicate the following: • The particular craft or skill required in each operation • Labor rates for the various types of operations • Supervision required for each process step • Maintenance personnel required • Overhead personnel required.
In the absence of a staffing table, an order-of-magnitude approximation of labor requirements can be made using the Wessell equation. The Wessell equation is
Supervision costs may vary from 10% to 25% of operating labor cost. On average, an allowance of 15 to 20% of operating labor cost is usually satisfactory for early-on estimates.

## Slide 18
Staffing Table: The plant requires 4 operators per shift ($25/hour) plus 1 shift supervisor
Total Operating Labor (Base): Let's assume the total base operating labor is $200,000 per year
Supervision Cost: Applying a standard 15% allowance of the operating labor cost adds $30,000 per year ($200,000 × 0.15) for supervisors

## Slide 19
Lecture 5
3.2.5 Maintenance
Few published data on maintenance data are available. Maintenance cost can vary from 1 or 2% to over 15% of the project capital cost per year. For simple plants with relatively mild, noncorrosive conditions, an allowance of 3 to 5% should be adequate. For complex plants and severe corrosive conditions, this factor can be 10 to 12% or even higher.
Maintenance costs consist of labor and material components with the total maintenance cost divided 50 to 60% labor and 40 to 50% material.

## Slide 20
Lecture 5
3.2.5 Maintenance (continued)
For most early-on estimates, it is sufficient to assume a 50:50 split. Maintenance varies with rate of operation, but not linearly. When operating at less than 100% of capacity, maintenance costs generally increase per unit of production as follows:

## Slide 21
Lecture 5
Adequate Allowance:
For this standard plant operating under mild, non-corrosive conditions, maintenance is estimated at 4% of the capital cost per year
Calculation: $10,000,000 × 4% = $400,000 per year
Labor/Material Split: This $400,000 is split 50:50, meaning $200,000 for maintenance labor and $200,000 for replacement materials
Reduced Capacity Effect: If the plant operates at 50% capacity, the maintenance cost does not drop by half. As the table, it stays at 75% of the full capacity cost ($400,000 × 0.75 = $300,000)

## Slide 22
3.2.6 Indirect Payroll Cost
Indirect payroll cost includes workers’ compensation, pensions, group insurance, paid vacations and holidays, social security, unemployment taxes, fringe benefits, and so on. It is generally based on labor cost, usually at about 30 to 45% of the labor cost in the United States. In other countries, this percentage may vary greatly and should be verified locally.
3.2.7 Operating Supplies
Operating supplies include lubricants, instrument charts, brooms, and so on, and may be generally assumed to be 6% of the operating labor or as 0.5% to 1% of the capital investment per year. For highly automated, complex operations these costs can increase substantially as a percentage of labor costs.
3.2.8 Laboratory and Other Service Costs
Laboratory and other service costs can be based on one or more of the following:
1. Experience
2. Workhours required
3. A percentage of operating labor cost (3 to 10% is common, but it may be as high as 20%).

## Slide 23
Indirect Payroll, Operating Supplies, & Laboratory :
Indirect Payroll Cost Calculated at 35% of the labor cost to cover workers' compensation and medical insurance
Calculation: $200,000 labor × 35% = $70,000/year.
Operating Supplies: Lubricants, tools, and charts estimated at 6% of operating labor: Calculation: $200,000 × 6% = $12,000/year.
Laboratory Costs: Quality testing of chemical batches estimated at 10% of operating labor:
Calculation: $200,000 × 10% = $20,000/year

## Slide 24
3.2.9 Royalties and Rentals
Royalties and rentals are generally an operating expense but may be part of capital investment. Single-sum payments for royalties, rental, or license payments are properly considered as capital investment items, whereas payments in proportion to production or fixed payments per annum are treated as direct operating costs. Royalty payments may range between 1% and 5% of product sales price.
3.2.10 Indirect Costs
Factory overhead is the indirect cost of operating a plant. It is dependent upon both investment and labor. Some data on the allocation for new plants follow (Black, 1991). The figures represent what percentage of the investment and labor, respectively, can be used for estimating the factory overhead.

## Slide 25
Royalties: The plant pays a proportional cost of 3% of the product sales price to use a patented chemical blending technique, If the selling price is $500/ton, the royalty is $15 per ton
Factory Overhead: Using the table on next Slide for a "Heavy chemical plant, small capacity"
Investment factor: 4.0% of capital per year → 4.0% × $10,000,000 = $400,000/year
Labor factor: 45% of labor per year → 45% × $200,000 = $90,000/year

## Slide 27
3.2.11 Distribution Costs
Distribution costs include handling and transportation costs. These costs vary with the types of containers and with methods of shipment. Cost without distribution cost is called bulk cost.
3.2.12 Avoidance of Nuisances
Nuisances include waste disposal and pollution control costs. Each case must be calculated individually. The topic is becoming increasingly more expensive and includes such items as product liability. These cost are mounting rapidly.
3.2.13 Contingencies
As is true for the capital cost estimate, an operating cost estimate should include a contingency allowance to account for those costs that cannot readily be determined or are too small to be readily determined or defined, but may be significant in the aggregate. The contingency allowance applies to both direct and indirect costs and ranges from 1% to 5% or more in some cases.

## Slide 28
Distribution Costs: Specialized shipping containers cost $15 per unit, plus freight carrier fees.
Avoidance of Nuisances: Environmental waste compliance and wastewater filtration cost $45,000 annually
Contingencies: Following Hackney’s guidelines for an installation common to the industry with reliable data, a 2% contingency is applied to the total operating estimate

## Slide 29
Hackney (1971) has suggested the following guidelines for operating cost contingency:
1. Installations similar to those currently used by the company and for which standard costs are available: 1%
2. Installations common to the industry for which reliable data are available: 2%
3. Novel installations that have been completely developed and tested: 3%
4. Novel installations that are in the development stage: 5%
3.2.14 Shortcut Methods
Table 3.10 will help in making preliminary operating cost estimates.
Table 3.10 Preliminary Operating Cost Estimate

## Slide 38
Applying the Table 3.10 formulas for indirect costs quick calculations:
Depreciation (10-year straight-line): $10,000,000 ÷ 10 = $1,000,000/year.
Real Estate Taxes (1% of investment): $10,000,000 × 1% = $100,000/year
Insurance (0.5% of investment): $10,000,000 × 0.5% = $50,000/year

## Slide 39
Summarizing and aggregating the values into the formal structure :
Operating / Manufacturing Cost: Sum of raw materials, utilities, labor, maintenance, and depreciation = $2,500,000
II. General Expense:
Marketing/Sales costs: Advertisements and sales team travel = $50,000
Administrative Expense: Executive salaries and legal fees = $80,000.
Research & Development (R&D): Creating new product lines = $40,000.
Total Product Cost: $2,500,000 + $170,000 = $2,670,000 per year

## Slide 40
3.3 SUMMARY
The basic cost estimating procedure is as follows:
Scope the job or problem.
2. Establish the estimate format; use a code of accounts.
3. Prepare your estimate area by area and category by category.
4. Check your work; verify your data.
5. Review and adjust.
6. Finalize.
7. Complete the documentation.
8. File.
In general, • Understand the overall picture.
• Document well.
• Analyze your figures.
• Tailor your estimate to the job.
• Plan ahead.

## Slide 41
3.3 SUMMARY
Applying the 8-step estimation lifecycle to our plant :
Scope: Estimate the operating cost of the new 5,000-ton plastic production line.
Format: Organize costs into the Table 3.11 ledger structure.
Prepare: Calculate step-by-step raw materials first, then labor, then utilities.
Check: Cross-verify calculated electricity tariffs against current regulatory approved rates.
Review: Adjust the raw materials budget upward by 4% to account for winter supply chain risks.

## Slide 42
3.3 SUMMARY
Applying the 8-step estimation lifecycle to our plant : (continued)
Finalize: Approve the finalized operating cost of $2.67M.
Document: Save all calculation logs and vendor quote sheets.
File: Store the document in the central PMO directory for future historical benchmarking.

## Slide 43
Thank You