## Slide 1
Social Media and Mobile Forensics
Prepared by Dr. Nermin Hamza
Lecture 9
CYB 770
IT Forensics

## Slide 2
Main Topics
Lecture 9
Social Media Forensic
Mobile Forensics
  Phones Devices
  Service provider
  Sim Card

## Slide 3
Lecture 9
Social Media Forensic

## Slide 4
Social media
Lecture 9
What is social media?
Social media is the use of applications or programs that a user can use to create and share information, forms of expression, opinions, ideas, and so on through virtual communities through the global internet.
Users can access social media through web-based technology such as a mobile device application.

## Slide 5
Social media
Lecture 9
The majority of the social media that the artifacts will not be saved to the user system.
The applications store the data in the service provider's cloud, which is a fancy way of saying the data will be on the service provider's servers.

## Slide 6
Social media
Lecture 9

## Slide 7
Social media
Lecture 9
The following is a short description of some popular social media applications you make come across during your investigations:
Facebook: The most extensive social media application with nearly 2,000,000,000 users. It combines commercial advertisers and consumer users with their content. It is easy to use. Users can upload images, recorded videos, live videos, and chat via the messenger application.
Instagram: A photo and video sharing social media application. Users can share photos and recorded videos and live videos. Users can also chat and comment with other users via the app.

## Slide 8
Social media
Lecture 9
Snapchat: A video/photo-sharing social media application. Initially, when a user sent a "snap" after the recipient viewed the image, it would be deleted from the system. Now, users have the option of saving "snaps."
Twitter: Social media application used for news, politics, sports, entertainment, and so on. Twitter allows 280-character tweets, with longer tweets being linked in the following messages.
WhatsApp: A messaging application with the ability to send pictures/videos.

## Slide 9
Social media
Lecture 9
Telegram: is a popular cross-platform messaging app that is widely used because it offers some enhanced privacy and encryption features as well as support for large group chat features.
Tumblr: A blogging/social networking application. Users can post pictures/videos to a blog page.
Tinder: A location-based social media application used as a dating service. Users "swipe right" or "swipe left" on profiles they like/dislike. If both parties "like" each other, then they can chat using the app.

## Slide 10
Social Media Forensics
Lecture 9
The application of computer investigation and analysis techniques to gather evidence from online sources suitable for presentation in a court law

## Slide 11
Social Media Forensics
Lecture 9
Social media investigators have a variety of strategies for collecting and analyzing social media information, such as:
Manually visiting social media account pages.
Printing or taking screenshots.
Downloading copies of photos or files.
Accessing open source or other software programs to collect and preserve information.
Subpoenaing or obtaining a court order for production of additional information and documents.

## Slide 12
Social Media Forensic
Lecture 9
Here are tools designed to make your online investigations more successful and efficient:
WebPreserver: Collect and preserve social media evidence in defensible format
Makeawebsitehub: Identify the latest social media apps and platforms
Pipl Search: Find public records, online data, and other information related to an individual
TinEye: Use reverse image search to find the source of an online picture
TweetBeaver: Use Twitter analytics to understand an account and identify connections

## Slide 13
Social Media Forensic
Lecture 9
WebPreserver
https://youtu.be/gNLHue6TydM

## Slide 14
Lecture 9
Mobile Forenics

## Slide 15
Mobile forensic
Lecture 9
Mobile devices perform an array of functions ranging from a simple telephony device to those of a personal computer.
Designed for mobility, they are compact in size, battery-powered, and lightweight.
Most mobile devices have a basic set of comparable features and capabilities.

## Slide 16
Mobile forensic
Lecture 9
Depending on your phone’s model, the following information might be stored on it:
Incoming, outgoing, and missed calls
Multimedia Message Service (MMS; text messages) and Short Message Service (SMS) messages
E-mail accounts
Instant messaging (IM) logs
Photos, videos, and music files
Calendars
Social media account information
GPS data
Web pages
address books
Voice recordings and voicemail
Access to your home
Bank account logins

## Slide 17
Mobile forensic
Lecture 9
Different mobile devices have different technical and physical characteristics (e.g., size, weight, processor speed, memory capacity)
Mobile Devices have a microprocessor, read only memory (ROM), random access memory (RAM), a radio module, a digital signal processor, a microphone and speaker, a variety of hardware keys and interfaces and a liquid crystal display (LCD).
The operating system (OS) of a mobile device may be stored in either NAND or NOR memory while code execution typically occurs in RAM.

## Slide 18
Mobile Forensic
Lecture 9
Phone category | Smart Phone features
Processor | Superior speed (~1GHz dual-core)
Memory | Superior capacity (~128GB)
Display | Large size color, 16.7 million (~24-bit)
Card Slots | MicroSD MicroSDXC
Camera | Still, Panoramic, and Video (HD)
Text | Input Numeric Keypad, QWERTY-style keyboard Touch Screen, Handwriting Recognition, QWERTY-style keyboard
Voice Input | None Voice Recognition (Dialing and Control)
Cell Interface | Voice and Limited Data Voice and High Speed Data (4G LTE)
Positioning | GPS receiver GPS receiver
Wireless | IrDA, Bluetooth, WiFi, and NFC
Battery | Fixed/Removable, Rechargeable Li-Ion Polymer
Mobile Hardware

## Slide 19
Mobile Forensic
Lecture 9
OS | Android, BlackBerry OS, iOS, Symbian, WebOS and Windows Phone
PIM (Personal Information Management) | Phonebook, Calendar and Reminder List
Applications | Applications (e.g., games, office productivity and social media)
Call | Voice, Video
Messaging | Text, Enhanced Text, Full Multimedia Messaging
Chat | Enhanced Instant Messaging
Email | Via POP or IMAP Server
Web | Direct HTTP
Mobile Software

## Slide 20
Mobile Forensic
Lecture 9

## Slide 21
Mobile Storage Evidence Locations
Lecture 9

## Slide 22
Mobile Evidence Analysis
Lecture 9

## Slide 23
Lecture 9
Phone

## Slide 24
Set Of Switching for On/Off
Lecture 9
On State
If The device is “On” , do Not turn it “OFF” , turning it “Off” could activate lockout feature.
Write down all information on display (photography, if possible)
OFF State
If the device is “OFF”, leave it “OFF”
Turning it on could alter evidence on device (same as computer

## Slide 25
Mobile Forensic
Lecture 9
Mobile device should be protected from signal Interruption, data overwriting
Use signal Containment devices and bags to achieve and maintain network isolation

## Slide 26
Mobile Forensic
Lecture 9
Faraday Bag : prevent any signal from being sent to or reaching the mobile phone.
Signal Disruption Bag/Wireless StrongHold Bag : It Prevents any type of signal from reaching mobile device.

## Slide 27
Mobile Forensic
Lecture 9
Arson Cans : are mainly used in the mobile investigative process to prevent someone connected to the crime from hitting the with a text or email ‘bomb’ that floods the phone’s memory with message that crowd out all other previous calls from the log.

## Slide 28
Mobile Forensic
Lecture 9
Aluminum Foil : the mobile devices is wrapped with three layers of aluminum foil to prevent an incoming signal and making data secure.
RF-shielded box: it preserve the mobile device against radio frequency (RF) inerferences resulting form noisy environmen

## Slide 29
Mobile Forensic
Lecture 9
A forensic investigator should not directly work on the original evidence. He/she should instead create ta forensic image of the mobile device obtained at the crime scene
File carving and forensic analysis is conducted on forensic image in order to leave the actual evidence intact

## Slide 30
Mobile Forensic
Lecture 9
Forensic imaging is an accepted standard of every company for the preservation of mobile-based evidences. The forensic investigator should not directory work on the actual evidence.
The investigator need to create image of the mobile internal or external memory.
Creating forensic image is difficult since the data may change due to continuous mobile updates.
Investigator may copies the content onto separate hard device.
The image tool such as : FTKImager, EnCase and Smart used to create forensic image.

## Slide 31
Mobile Forensic
Lecture 9
AccessData FTK Imager is a forensics tool whose main purpose is to preview recoverable data from a disk of any kind. It can also create perfect copies, called forensic images, of that data.
This powerful tool can create forensic images of local hard drives, floppy disks, Zip disks, CDs, and DVDs, entire folders, or even of individual files from various places within the media storage device.
The fact that it can export files and folders from the created image means that this application can also recover data on its own (in some circumstances).

## Slide 32
Mobile Forensic
Lecture 9
File carving is a process used in computer forensics to extract data from a disk drive or other storage device without the assistance of the file system that originality created the file.
It is a method that recovers files at unallocated space without any file information and is used to recover data and execute a digital forensic investigation.
It also called “carving,” which is a general term for extracting structured data out of raw data, based on format specific characteristics present in the structured data.
File carving

## Slide 33
Mobile Forensic
Lecture 9
The IMEI (International Mobile Equipment Identity) is a unique number to identify GSM, WCDMA, and iDEN mobile phones, as well as some satellite phones.
Mostly phone have one IMEI number, but in dual SIM phones are two.
The IMEI number is a unique 15-digit code that precisely identifies the device.
This number is an individual number assigned to each and every phone all over the world.

## Slide 34
Mobile Forensic
Lecture 9
How to find this number:
Dial *#06# on your keypad and press call or send button, your IMEI number will be retrieved and displayed on your screen.
On the back or bottom of the device or under, IMEI number can be found printed.
IMEI numbers can also be printed on the original packaging of your device.

## Slide 35
Mobile Forensic
Lecture 9
*#06#
IMEI CHECK - Free Online IMEI Number Checker | IMEI.info

## Slide 36
Mobile Forensic
Lecture 9
Why would you need to check the IMEI Number?
The number is useful when you would like to send the device for service to fill out warranty forms.
Besides that, if you want to report a stolen or a lost phone at the police or network operator you should use the IMEI Number as well.
After that, you can block your phone and it will make the device unusable, regardless of whether the SIM card is changed or removed.
What is also really important is that IMEI contains a few secret information about the product but also sometimes allows you to locate the smartphone.

## Slide 37
Mobile Forensic
Lecture 9
The Structure of an IMEI Number:
First 8 digits of IMEI number are TAC (Type Allocation Code) which will give you the mobile phone brand and model. Other 7 digits are defined by manufacturer (6 are serial number and 1 is check digit).
For example a IMEI number: 354230061155201
Here TAC: 354230 | FAC: 06 | SNR: 115520 | CD: 1

## Slide 38
Lecture 9
Service Provider Data

## Slide 39
Mobile Forensic
Lecture 9
Service Provider Data contains information such as call history and text message, including the date and time.
It can act as backup evidence when the user deletes the content from his mobile.
The mobile forensic investigator should request the service provider to release data at the time of incident .

## Slide 40
Mobile Forensic
Lecture 9
This helps investigators pinpoint the exact location of the mobile device at the time of the incident in a situation where a user turns off the Geo location feature in the mobile.
Investigators should investigate both the service provider data and the data found on the mobile phone, to find potential evidence.

## Slide 41
Mobile Forensic
Lecture 9
Call Detail Record (CDR): contains information about user activities with the mobile phone.
The service providers records and store this information in their database.
The call data record contains several categories of information such as :
Call telephone number or numbers
Name and addresses of the subscribers or registered users
Date and time of the start and end of the communication
Telephone service used , e.g. voice, conference call , Short Message Service (SMS) Multimedia Service(MMS)
Location label (Cell ID) at the start and end of the communication

## Slide 42
Mobile Forensic
Lecture 9

## Slide 43
Lecture 9
SIM Card

## Slide 44
Mobile Forensic
Lecture 9
Mobile chips

## Slide 45
Mobile Forensic
Lecture 9
ICCID : Integrated Circuit Card IDentification
Integrated Circuit Card ID (ICCID) is the unique identifier of a Subscriber Identity Module (SIM card) on a mobile device.
ICCIDs are stored in the SIM cards and printed on the SIM card body.
The ICCID is defined by the ITU-T recommendation E.118 as the Primary Account Number.
A full ICCID is 19 or 20 characters containing the Industry Identifier (ISO), country code, issuer identity, account ID, and other data which allows the network operator to identify the card.

## Slide 46
Mobile Forensic
Lecture 9
19 to 20 digit
Industry identifier : 89
Counter code : 94
Issuer identifier

## Slide 47
Mobile Forensic
Lecture 9
What is a SIM cloning?
SIM cloning is the process in which a legitimate SIM card is duplicated. When the cloning is completed, the cloned SIM card’s identifying information is transferred onto a separate, secondary SIM card.
The secondary card can then be used in a different phone while having all calls and associated charges attributed to the original SIM card.

## Slide 48
Mobile Forensic
Lecture 9
SIM Cloning as attack
An attacker gaining physical access to your SIM card and then cloning it onto a new SIM card controlled by the hacker.
Once the hacker has a clone of the SIM card, they can then use this in a device they control to access the victim’s texts, phone calls and location data.

## Slide 49
How to Clone SIM Card -- Tenorshare

## Slide 50
Lecture 9