## Slide 2
Outlines
Module
2
(Sockets/Part 3_ Computer Networks Protocols(UDP_TCP_ICMP))
    Various topics: (UDP broadcast, Using TCP Streams Like Files)
    2. Handlling errors: (Socket Exceptions, Missed Errors, Errors with File-like Objects)
    3. ICMP protocol (Definition, Packet, Header, Messages types)
    4. ICMP in Python and raw sockets
      Ping
      Broadcast Ping
      Multi-Ping
      Traceroute
      Verbose Ping
      Verbose traceroute

## Slide 3
UDP Broadcast
Module
2
UDP broadcast is a technique that allows sending UDP datagram from a single source to all computers in a LAN/ entire subnet. (sent to a special address called the Broadcast address).
IPv6 doesn't even have a concept of broadcast (multicast is used, instead).

## Slide 4
Network Masks
Module
2
A network mask, or ``netmask'', is used to divide an IP address into a network address and a host address. When you set up a network, the network mask must be common to all network interfaces on that network. The default network masks are 255.0.0.0 for class A, 255.255.0.0 for class B, and 255.255.255.0 for class C networks.

## Slide 5
How to Find the Broadcast Address?
Module
2
A broadcast IP address is only assigned once in each network. It is always the last IP address of the subnet.
The network address and the broadcast address are not used as computer IP addresses.
In a network, the first address field is reserved for the network and the last for the broadcast address.

## Slide 6
UDP Broadcast Application
Module
2
def client(network, port): sock = socket.socket(socket.AF_INET, socket.SOCK_DGRAM) sock.setsockopt(socket.SOL_SOCKET, socket.SO_BROADCAST, 1) text = 'Broadcast datagram!' sock.sendto(text.encode('ascii'), (network, port))

## Slide 7
Using TCP Streams Like Files
Module
2
File objects can read() and write(), sockets can send() and recv(), and no kind of object can do both.
Sometimes you will want to treat a socket like a normal Python file object—often because you want to pass it into code like that of the many Python modules such as pickle, json, and zlib that can read and write data directly from a file. For this purpose, Python provides a makefile() method on every socket that returns a Python file object that is really calling recv() and send() behind the scenes.

## Slide 8
Using TCP Streams Like Files
Module
2
conn, addr = sock.accept() print('socket accepted, got connection object') sockFile = conn.makefile() message = sockFile.readline() print('received and read by socket: ' + str(message)) conn.close()
(Server side)
(Client side)
sock.connect((HOST, PORT))
print('socket connected') sockFile = sock.makefile(mode='w') message = 'Hi this is my msg Number = ' + str(myCounter) + ' ***' + '\r\n' print('*** ' + message) sockFile.write(message)

## Slide 9
Handling Errors
Module
2
In Python, the socket code raises exceptions when network errors occur.
Virtually every function call that touches the network in any way can and does raise exceptions for various reasons, for example: servers being down, connections dropped, and so on.
Socket Exceptions
  socket. error for general I/O and communication problems
  socket.gaierror for errors looking up address information
  socket. herror for other addressing errors (This exception is thrown when there is a problem with gethostbyname () and gethostbyaddr())
  socket. timeout for handling timeouts that occur after settimeout () has been called on a socket (Python 2.3 and higher)

## Slide 10
Handling Errors
Module
2
Missed Errors
    There are certain situations in which communication problems could occur but no exception would be raised because no error was passed back from the operating system.
    One such problem could occur if the remote server drops the connection between the time the client connects and the time it writes out its request. In this case, the later call to recv() will receive no data (since the server closed its connection) and the program will terminate successfully.
Errors with File-like Objects
    It's possible to use the makefile () function to get a file-like object from a socket.
    This file-like object actually makes calls to the real socket, so the exceptions raised by the file-like object are the same as the ones raised by the socket's own send () and recv () functions.

## Slide 11
Handling Errors with File-like Objects
Module
2
while 1: try: buf = fd.read(2048) except socket.error as e: print('Error receiving data:', e) sys.exit(1) if not len(buf): break sys.stdout.write(buf)
fd = s.makefile('rw', 2048) print('sleeping :') time.sleep(5) print('Continuing ...') try: fd.write("GET %s HTTP/1.1" % filename) print('fd has this info: ', fd) except socket.error as e: print('Error sending data:', e) sys.exit(1)

## Slide 12
ICMP Protocol
Module
2
      Definition of ICMP protocolICMPv4
      Redirect message
      ICMP (Packet/ Header)
      ICMP messages types
      ICMP Protocol in Python
      Raw Sockets
      ICMP Functions (Ping, Traceroute, …)

## Slide 13
Definition: ICMP Protocol
Module
2
The Internet Control Message Protocol (ICMP) is a supporting protocol in the Internet protocol suite.
It is used by network devices, including routers, to send error messages and operational information indicating success or failure when communicating with another IP address, for example:
    An error is indicated when a requested service is not available or that a host or router could not be reached.
ICMP is not typically used to exchange data between systems, nor is it regularly employed by end-user network applications (with the exception of some diagnostic tools like ping and traceroute).
ICMP for IPv4 is defined in RFC 792.
ICMPv6, defined by RFC 4443, is used with IPv6.

## Slide 14
Definition: ICMP Protocol
Module
2
ICMP is a network-layer protocol. There is no TCP or UDP port number associated with ICMP packets as these numbers are associated with the transport layer above (It does not have source and destination port numbers because it was designed to communicate network-layer information between hosts and routers, not between application layer processes).
ICMP messages are typically used for diagnostic or control purposes or generated in response to errors in IP operations (as specified in RFC 1122). ICMP errors are directed to the source IP address of the originating packet.

## Slide 15
Definition: ICMP Protocol
Module
2
ICMP uses the basic support of IP as if it were a higher-level protocol, however, ICMP is actually an integral part of IP. Although ICMP messages are contained within standard IP packets, ICMP messages are usually processed as a special case, distinguished from normal IP processing.
In many cases, it is necessary to inspect the contents of the ICMP message and deliver the appropriate error message to the application responsible for transmitting the IP packet that prompted the ICMP message to be sent.

## Slide 16
An example of how an ICMPv4
redirect message works
Module
2

## Slide 17
ICMP & T T L
Module
2
For example, every device (such as an intermediate router) forwarding an IP datagram first decrements the time to live (TTL) field in the IP header by one. If the resulting TTL is 0, the packet is discarded and an ICMP time exceeded in transit message is sent to the datagram's source address.
Many commonly used network utilities are based on ICMP messages. The traceroute command can be implemented by transmitting IP datagrams with specially set IP TTL header fields, and looking for ICMP time exceeded in transit and Destination unreachable messages generated in response. The related ping utility is implemented using the ICMP echo request and echo reply messages.

## Slide 18
ICMP in Network
Module
2

## Slide 19
Module
2
ICMP messages:
  Are encapsulated in IP packets so most people would say that it’s a layer 4 protocol like UDP or TCP.
However, since ICMP is a vital part of the IP protocol it is typically considered a layer 3 protocol.
ICMP in Network

## Slide 20
Module
2
ICMP Header

## Slide 21
ICMP Packet at Network Layer
Module
2
IP header | ICMP header | ICMP payload size | MTU (1500)
20 bytes | 8 bytes | 1472 bytes (maximum) | 20 + 8 + 1472 = 1500
ICMP is actually a user of the IP protocol--in other words, ICMP messages must be encapsulated within IP packets. However, ICMP is implemented as part of the IP layer. So ICMP processing can be viewed as occurring parallel to, or as part of, IP processing.
According to MTU the size of the ICMP packet cannot be greater than 1500 bytes.

## Slide 22
ICMP (Checksum)
Module
2

## Slide 23
ICMP Messages
Module
2
What is the difference between ICMP and ping?
    Ping is a tool commonly used to find the status of a device on a network. Ping is based on the ICMP protocol. When a Ping process request is sent out as an ICMP echo to the target device, it replies with an ICMP echo reply if the device is available.
ICMP uses unicast routing for error detection and notification messages.

## Slide 24
Module
2
Error-reporting messages
  The error-reporting message means that the router encounters a problem when it processes an IP packet then it reports a message.
Query messages
  The query messages are those messages that help the host to get the specific information of another host. For example, suppose there are a client and a server, and the client wants to know whether the server is live or not, then it sends the ICMP message to the server.
ICMP Messages

## Slide 25
ICMP Message Format
Module
2

## Slide 26
Module
2
Type: the number 3 specifies that the destination is unreachable.
Code (0 to 15): It is a 4-bit number which identifies whether the message comes from some intermediate router or the destination itself.
Sometimes the destination does not want to process the request, so it sends the destination unreachable message to the source. A router does not detect all the problems that prevent the delivery of a packet.
Error Message : Type 3

## Slide 27
Module
2
ICMP Query Messages

## Slide 28
Module
2
ICMP Query Messages
(Timestamp) Type 13/14

## Slide 29
Module
2
ICMP Query Messages
(Timestamp) Type 13/14

## Slide 30
Module
2
ICMP always reports error messages to the original source.
No ICMP error message will be generated in response to a datagram carrying an ICMP error message.
No ICMP error message will be generated for a fragmented datagram that is not the first fragment.
No ICMP error message will be generated for a datagram having a multicast address.
No ICMP error message will be generated for a datagram having a special address such:
      127.0.0.0
      0.0.0.0
ICMP Messages (Notes)

## Slide 31
ICMP & Raw sockets
Module
2
Raw IP packet manipulation

## Slide 32
ICMP & Raw sockets
Module
2

## Slide 33
ICMP & Raw sockets
Module
2
The biggest problem with RAW-sockets (also the PACKET-sockets) is that there is no uniform API for using RAW-sockets under different operating systems.

## Slide 34
ICMP & Raw sockets
Module
2
Raw socket is a type of network socket which allows a software application on the computer to send and obtain packets of information from the network without using the computer's operating system as a middleman. In other words, A raw socket provides an express tunnel between an application and an external source. Neither the operating system nor any other program on the computer has the ability to interfere with a raw connection. (Need root privilege/ Administrator ).
The primary advantage to using raw socket network handling is that it cuts out the middle man. Since the operating system doesn't handle the data specifically:
    It reduces overhead on the network.
    Saving central processing unit (CPU) cycles.
    Decreasing stress on the system hardware.

## Slide 35
ICMP & Raw sockets
Module
2
Raw socket network interfaces do have a downside. though. Hackers commonly use raw socket connections to stage transmission control protocol (TCP) attacks on a network. During a TCP attack, a hacker sends a forged bit of data onto the network through a raw socket connection. This forged data contains a reset signal for the TCP connection, which in turn interrupts and crashes the current network connections on the computer.
For this reason, some operating systems have withdrawn support for raw sockets.
Software companies can restrict users' ability to use raw.
With modern processors coming in dual-, quad-, and even six-core varieties, the chances of regular network socket connections lagging the computer are negligible. For this reason, unless there is a specific justification for using a raw socket connection over a standard network socket, the risk posed by hackers and TCP attacks on the network outweighs any advantages.

## Slide 36
ICMP Protocol in Python
Module
2
icmplib 3.0.3
The power to form ICMP packets and do ping and traceroute. https://pypi.org/project/icmplib/
icmplib is a brand new and modern implementation of the ICMP protocol in Python.
Latest version : Released: Feb 6, 2022
Since icmplib 3, Python 3.7 or later is required to use the library.
If you are using Python 3.6 and you cannot update it, you can still install icmplib 2.

## Slide 37
icmplib 3.0.3
Module
2
Import basic functions
      from icmplib import ping, multiping, traceroute, resolve
Import asynchronous functions
      from icmplib import async_ping, async_multiping, async_resolve
Import sockets (advanced)
      from icmplib import ICMPv4Socket, ICMPv6Socket, AsyncSocket, ICMPRequest, ICMPReply
Import exceptions
      from icmplib import ICMPLibError, NameLookupError, ICMPSocketError
      from icmplib import SocketAddressError, SocketPermissionError
      from icmplib import SocketUnavailableError, SocketBroadcastError, TimeoutExceeded
      from icmplib import ICMPError, DestinationUnreachable, TimeExceeded

## Slide 38
ICMP Functions in Python
Module
2
      Ping
      Broadcast Ping
      Multi-Ping
      Traceroute
      Verbose Ping
      Verbose traceroute