## Slide 2
Contents
Sequential circuits
Flip-flops
Analysis of clocked sequential circuits
Design procedure

## Slide 3
The behavior of a clocked sequential circuit is determined from the inputs, the outputs, and the sate of flip-flops
A clocked sequential circuit can be analyzed by using:
  (i) The state equation obtained by replacing flip-flop input equations in its characteristic equation, or
  (ii) a state table.
A state equation (or transition equation) specifies the next state as a function of present state and inputs
Analysis of Clocked Sequential Circuits

## Slide 4
State table – a multiple variable table with the following four sections:
  Present State – the values of the state variables at time (t) for each allowed state.
  Input – the input combinations allowed.
  Next-state – the value of the state at time (t+1) based on the present state and the input
  Output – the value of the output as a function of the present state and (Mealy) the input.

## Slide 5
Procedure: Write the Boolean expression for each flip-flop input, which is, in fact, the flip-flop output right after the next active clock edge.
Consider the circuit shown in next slide
It consists of two D flip-flops A and B, an input x and an output y
Since the D input of a flip-flop determines the value of the next state, it is possible to write a set of equations for the circuit
Analysis (Contd.)

## Slide 6
Analysis (Contd.)

## Slide 7
Analysis (Contd.)
Flip-flop input equations or excitation equations (for a circuit with D flip-flops, it is the same as the state equation):
DA = Ax + Bx
DB = A’x
y = (A + B)x’
As the FF in use is the D FF:
Q(t+1) = D

## Slide 8
The state equation can be written as:
A(t+1) = A(t).x(t) + B(t).x(t)
B(t+1) = A’(t).x(t)
Or simply:
A(t+1) = Ax + Bx
B(t+1) = A’x
Similarly, the present state of output is:
y(t) = [A(t) + B(t)]x’(t),
or y = (A +B)x’
Analysis (Contd.)

## Slide 9
Analysis (Contd.)

## Slide 10
A state diagram is a graphical representation of a state table
represented by a circle, and the transitions between states are indicated by directed lines connecting the circles
Number of states = 2number of Flip Flops
The binary number inside each circle identifies the state of the flip-flops
Analysis (Contd.)

## Slide 11
Analysis (Contd.)
The directed lines are labeled with two binary numbers separated by a slash
The state diagram follows from the state table
The state diagram for the given circuit:
I/O

## Slide 12
NOTE:
Mealy model – the output values are determined by both current state and current inputs.
Moore model – the output values are determined only by current state.
State Diagrams Types

## Slide 13
1) FF Input equation:
DA = Ax + Bx
DB = A’x
2) State equation and output:
Characteristic equation:
A(t+1)= DA , B(t+1)=DB
State equation:
A(t+1) = A(t).x(t) + B(t).x(t)
B(t+1) = A’(t).x(t)
Or A(t+1) = Ax + Bx
B(t+1) = A’x
state of output is:
y = (A +B)x’
3) State table.
4) State diagram (Mealy)
Analysis of D FF: summary

## Slide 14
Analysis with JK flip-flops
The next state values of a sequential circuit that uses flip-flops such as JK can be derived using following procedure:
  Determine the flip-flop input equations in terms of the present state and inputs
  Use corresponding flip-flop characteristic equation to determine the next state values
We consider the sequential circuit with two JK flip-flops A and B, and one input x

## Slide 15
Analysis with JK flip-flops (Contd.)

## Slide 16
Analysis with JK flip-flops (Contd.)
The circuit has no outputs and, so, the state table does not need an output column
The outputs of the flip-flops may be considered as the outputs in this case
The circuit can be specified by the flip-flop input equations
JA = B KA = Bx’
JB = x’ KB = A’x + Ax’ = A ⊕ x

## Slide 17
Analysis with JK flip-flops (Contd.)
find the next state from the state equations by substituting the input equations into the flip-flop characteristic equations.
Characteristic equation for the JK flip-flop is:
A(t+1) = JAA’ + K’AA
B(t+1) = JBB’ + K’BB

## Slide 18
Analysis with JK flip-flops (Contd.)
Substituting the values of JA and KA, and JB and KB, from the input equations, we obtain state equations for A and B as:
A(t+1) = BA’ + (Bx’)’A = A’B + AB’ + Ax
B(t+1) = x’B’ + (A ⊕ x)’B = B’x’ + ABx + A’Bx’

## Slide 19
Analysis with JK flip-flops (Contd.)
A(t+1) = A’B + AB’ + Ax
B(t+1) = B’x’ + ABx + A’Bx’

## Slide 20
Analysis with JK flip-flops (Contd.)
The state diagram of the sequential circuit is shown right-side. Since the circuit has no outputs, the directed lines out of circles are marked with one binary number only to designate the value of input x.

## Slide 21
1) FF Input equation:
JA = B KA = Bx’
JB = x’ KB = A ⊕ x
2) State equation and output:
Characteristic equation:
A(t+1) = JAA’ + K’AA
B(t+1) = JBB’ + K’BB
State equation:
A(t+1) = BA’ + (Bx’)’A
= A’B + AB’ + Ax
B(t+1) = x’B’ + (A ⊕ x)’B
= B’x’ + ABx + A’Bx’
3) State table.
4) State diagram.
Analysis of JK FF: summary

## Slide 22
Analysis with T flip-flops
Similar to the analysis with JK flip-flops, the state table can be obtained by using characteristic table or the characteristic equation
Q(t+1) = T ⊕ Q = T’Q + TQ’
Consider the sequential circuit given in the next slide
It has two flip-flops A and B, one input x, and one output y

## Slide 23
Analysis with T flip-flops (Contd.)

## Slide 24
Analysis with T flip-flops (Contd.)
It can be described algebraically by two input equations and one output equation
TA = Bx, TB = x, y = AB
The characteristic equations are
A(t+1) = TA ⊕ A, B(t+1) = TB ⊕ B
Substituting the input equations with characteristic equations we get
A(t+1) = (Bx)’A + (Bx)A’ = AB’ + Ax’ + A’Bx
B(t+1) = x ⊕ B

## Slide 25
Analysis with T flip-flops (Contd.)
The state table is as follows:
A(t+1) = AB’ + Ax’ + A’Bx
B(t+1) = x ⊕ B

## Slide 26
Analysis with T flip-flops (Contd.)
The state diagram is in right-side
The output is only a function of current state, not the input, and that is why the output is written inside state circles

## Slide 27
1) FF Input equation:
TA = Bx, TB = x,
2) State equation and output:
Characteristic equation:
A(t+1) =T ‘A A + TA A’
B(t+1) = T’B B +TB B’
State equation:
A(t+1) = (Bx)’A + (Bx)A’
= AB’ + Ax’ + A’Bx
B(t+1) = x’ B +x B’
=x ⊕ B
State of the output:
y = AB
3) State table.
4) State diagram (Moore)
Analysis of T FF: summary

## Slide 28
Design Sequential circuits
The procedure for designing synchronous sequential circuit is:
  Translate the design specifications to the state diagram for the circuit
  Assign binary values to the states
  Obtain the binary coded state table

## Slide 29
Design Sequential circuits
  Choose the type of flip-flops to be used
  Derive the simplified flip-flop input equations and output equations
  Draw the logic diagram

## Slide 30
Example 1: Design 2-bit Counter using D-Flip Flops.
  Translate the design specifications to the state diagram for the circuit
  Assign binary values to the states
  Obtain the binary coded state table
Since Number of states = 2number of Flip Flops
4 = 2 Number of Flip FLOPS
So, Number of Flip[ Flops = 2
We Use D-type Flip Flop

## Slide 31
  3.Obtain the binary coded state table
Present State |  | Next State | 
A | B | A | B
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0

## Slide 32
  Choose the type of flip-flops to be used (D-type)
  Derive the simplified flip-flop input equations and output equations
  A(t+1) =A.B’ + A’.B
  B(T+1) = B’
Present State |  | Next State | 
A | B | A | B
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0

## Slide 33
5. Draw the logic diagram
Present State |  | Next State | 
A | B | A | B
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0

## Slide 34
End of lecture 9