## Slide 1
Automation and Programmability
CCNA (200-301) Cisco Certified Network Associate
Prepared by Eng. Taghreed Elsayed
Lecture 10

## Slide 2
Chapter
04
Automation and Programmability
What is Network Automation and Why We Need It?
Network automation is the process of automating the provisioning, orchestration, and management of network and their services. There are lots of benefits network automation can offer.
It allows network operations to be automated, which reduces human-to-machine interaction and, therefore, greatly reduces the chance of human error such as typos.
Network automation can also save time and manual labor because it provides Zero Touch Provisioning (ZTP) that configures network devices automatically without someone needing to configure it locally, hence reducing the operational expenditures, especially for service providers and enterprises.

## Slide 3
Chapter
04
Automation and Programmability

## Slide 4
Chapter
04
Automation and Programmability
Finally, one of the more important benefits of network automation is guarantee consistency in your configurations. With automation, you can create a script and then instruct the controller to deploy that to the devices wherein each device receives the same configuration.
This ensures that you are familiar with the configuration of each device, and it also means minimal configuration errors because the administrator is not typing the same configuration commands over and over on each device. It also greatly helps in troubleshooting and in generating reports.

## Slide 5
Chapter
04
Automation and Programmability
Traditional Network Management
With traditional networking, you can only manage network devices one at a time using SSH to the command line. This process is time-consuming, labor-intensive, and prone to human error. While this can work well in smaller networks, it does not work well in a large enterprise and does not also scale very well.
Traditional Network Monitoring Systems (NMS) such as Solar Winds , Cisco Works, and Cisco Prime Infrastructure have also been available for a long time and use protocols such as SNMP and Net flow to gather information reports on the state of the network.

## Slide 6
Chapter
04
Automation and Programmability
While SNMP uses MIB and OID to collects useful data and can also be used to push configuration to devices, it does not build for real-time programmatic access and has limited functionality.
SNMP also has security concerns and can be complex to implement and operate. These are the main challenges of traditional Networks:
Scalability Issues
Management Complexity
Slower Issue Resolution

## Slide 7
Chapter
04
Automation and Programmability

## Slide 8
Chapter
04
Automation and Programmability

## Slide 9
Chapter
04
Automation and Programmability

## Slide 10
Chapter
04
Automation and Programmability

## Slide 11
Chapter
04
Automation and Programmability

## Slide 12
Chapter
04
Automation and Programmability

## Slide 13
Chapter
04
Automation and Programmability
Cisco TCL

## Slide 14
Chapter
04
Automation and Programmability

## Slide 15
Chapter
04
Automation and Programmability

## Slide 16
Chapter
04
Automation and Programmability
Controller-Based Networks
A Controller-based network uses controller software or appliance to automate network operations. Software-defined networking uses a controller for network automation. It allows you to centrally manage your network device’s configuration and enable programs to automatically configure and operate networks through the power of Application Programming Interfaces (APIs).
Intelligent network automation through a controller-based network provides ease of management to your network than traditional networking because all of the configuration settings can be easily managed in the GUI of the controller.

## Slide 17
Chapter
04
Automation and Programmability
Controllers can also provide central aggregation points for monitoring and data analytics for more visibility and easier troubleshooting, particularly on a large network enterprise.
SD-Access is Cisco’s solution for network automation that replaces traditional network management. It offers a single point of automation, orchestration, and management of networks through the Cisco DNA Center controller. SD-Access has two key components:
Cisco Campus Fabric Solution- it is a network virtualization overlay built on top of the network underlay.
Cisco DNA Center – SDN controller for centralized management and NMS.

## Slide 18
Chapter
04
Automation and Programmability
Network Automation Tools
Multiple methods can be used to automate network management – Python scripts, NETCONF, RESTCONF, Ansible, Puppet, SDN, Cisco DNA Center, etc. However, not all methods are supported by all devices so you should choose which is most suitable for your environment.
Network configuration management tools provide an automated method to execute and monitor changes to our networks. Some tools even offer network automation frameworks wherein a library of commands and workflows are already provided

## Slide 19
Chapter
04
Automation and Programmability
If such changes do occur, it either reconfigures the device or informs the network engineers to make the change. There are two types of configuration management tools:
agent-based tools – need the installation of a code (agent) on the managed device, such as Puppet, Salt stack, and Chef.
agentless tools – does not need the installation of any code (agent) on them, such as Ansible , Salt stack SSH, and Puppet Bolt.

## Slide 20
Chapter
04
Automation and Programmability
Cisco DNA Center
The Cisco Digital Network Architecture (DNA) Center is an SDN controller that is used to support Cisco’s Software-Defined Access for network automation. The DNA Center provides centralized management on your system, automates configuration changes, and performs analysis of the devices.
Cisco DNA Center Assurance is a tool for monitoring and network management. It monitors traffic statistics, the health status of the network, and an overview of all issues in the network, It also correlates issues and provides recommendations on what may cause such network issues to help you assist in diagnosing and troubleshooting.

## Slide 21
Chapter
04
Automation and Programmability
Cisco DNA Center also enhances network visibility use that visibility to improve performance, It enables proactive prediction of network-related and security-related risks by using telemetry to improve the performance of the network.

## Slide 22
Chapter
04
Automation and Programmability

## Slide 23
Chapter
04
Automation and Programmability

## Slide 24
Chapter
04
Automation and Programmability

## Slide 25
Chapter
04
Automation and Programmability

## Slide 26
Chapter
04
Automation and Programmability

## Slide 27
Chapter
04
Automation and Programmability

## Slide 28
Chapter
04
Automation and Programmability

## Slide 29
Chapter
04
Automation and Programmability

## Slide 30
Chapter
04
Automation and Programmability

## Slide 31
Chapter
04
Automation and Programmability

## Slide 32
Chapter
04
Automation and Programmability

## Slide 33
Chapter
04
Automation and Programmability
SOAP vs REST: Comparing the Web API Services
Application Programming Interface (API) serves as an interface that enables applications or computer programs to communicate with each other directly. It is used to expose functionalities and procedures to the outside world through a service path or URL.
API plays a big part in our network by configuring and monitoring computer systems, network devices, or applications that involve programmatically interacting through software.
APIs are built for real-time programmatic access (built for computers to interact with each other without human intervention) and can be used for connecting to an individual or multiple devices on our network simultaneously.

## Slide 34
Chapter
04
Automation and Programmability
Web Services
Web services are the type of API that typically runs over HTTP/HTTPS. However, some web services, such as the Simple Object Access Protocol (SOAP), can use different transports such as Simple Mail Transfer Protocol (SMTP). Web services don’t necessarily use HTTP, but this is almost always the case and is usually assumed unless mentioned otherwise.
All web services can be considered APIs, but not all can be regarded as web services. APIs can utilize any communication protocol and aren’t limited to HTTP like web services are.
The two main types of APIs used for web service that runs over the Internet and typically use HTTP/HTTPS are SOAP and REST.

## Slide 35
Chapter
04
Automation and Programmability
Simple Object Access Protocol (SOAP) API
SOAP APIs are standard communication protocol systems that permit different operating systems like Linux and Windows to communicate. It was developed by Microsoft and is commonly used with HTTP transport with XML data format to access web services. It has three well-known characteristics.
Independent
Extensible
Neutral

## Slide 36
Chapter
04
Automation and Programmability
A more reliable way to communicate between applications is over HTTP, as it is supported by all Internet browsers and servers for web service. SOAP was created to accomplish this.
SOAP web services provide a way to communicate between applications running on different operating systems, with different technologies and programming languages.
SOAP messages are nothing but XML documents and can contain four elements.
Envelope
Header
Body
Fault

## Slide 37
Chapter
04
Automation and Programmability
Representational State Transfer (REST) API
REST API or Representational State Transfer is an architecture style for designing a distributed system that gives guidelines for the structure and organization of an API for web service. REST is protocol-independent. It supports any transport and data format like HTTP/S transport and JavaScript Object Notation (JSON) or XML data format.
Restful web services use HTTP methods to collect and manipulate data. A URL identifies every resource, and every resource should support the HTTP common operations. It offers a consistent way to interact with APIs from multiple vendors. Below are the most common HTTP “CRUD” functions and their associated use cases:

## Slide 38
Chapter
04
Automation and Programmability
Unlike SOAP protocol, REST APIs do not require a new message format. The HTTP API is CRUD (Create, Retrieve, Update, and Delete).

## Slide 39
Chapter
04
Automation and Programmability
SOAP vs REST
Use SOAP API if you are dealing with transactional operations and you already have an audience that is satisfied with this technology. Use REST web services if you’re focused on wide-scale API adoption or if your API is targeted at mobile apps.
SOAP Advantages:
Follows a formal enterprise approach
It is platform- and language-independent.
Information about objects is communicated to clients.
SOAP bypasses all firewalls.

## Slide 40
Chapter
04
Automation and Programmability
SOAP Disadvantages:
Uses high bandwidth to communicate metadata
Hard to implement
Unpopular among web and mobile developers
SOAP Use Cases:
Financial services
Payment gateways
Telecommunication services
REST Advantages:
Follows the philosophy of the Open Web
Relatively easy to implement and maintain
Separates client and server implementations
A single entity doesn’t control communication
The client can store information to prevent multiple calls
Able to return data in multiple formats (JSON, XML, etc.)

## Slide 41
Chapter
04
Automation and Programmability
REST Disadvantages:
Works on top of the HTTP protocol only
Must enforce security and authorization on top of it
REST Use Cases:
Social media services
Social networks
Webchat services
Mobile services
REST Advantages:
Follows the philosophy of the Open Web
Relatively easy to implement and maintain
Separates client and server implementations
A single entity doesn’t control communication
The client can store information to prevent multiple calls
Able to return data in multiple formats (JSON, XML, etc.)

## Slide 42
Chapter
04
Automation and Programmability
Data Serialization Formats – JSON, YAML, and XML
Data serialization is a technique that translates structured data into a format that enables storage or sharing of the digital information in a state that permits recovery of its original structure. Various computer systems have different hardware architecture, operating systems, and/or addressing mechanisms, which can be a challenge that is why serializing the data enables different users to have a standardized data serialization formats that can be easily shared across various applications.

## Slide 43
Chapter
04
Automation and Programmability
Data Serialization Formats and its Functionalities
Choosing the data serialization format for an application should depend on factors such as human readability, the complexity of data, and storage and speed limitations. Here are some of the common data serialization formats used to ease the storage and sharing of data across the Internet.
JSON – JavaScript Object Notation
This serialization format was standardized in 2013 and is considered a lightweight data-interchange format that translates data structures easier to be read and written by humans. This human-readable format has a short syntax textual format with limited data types derived from JavaScript data formats

## Slide 44
Chapter
04
Automation and Programmability
JSON data does not need a separate parser since they are referenced to JavaScript objects compared to XML.
The following are the benefits of using JSON files:
Self-describing
Simplicity and compact
Ease in learning and understanding