## Slide 1
Prepared by Dr. Mohamed Mostafa
Computer Vision,
and Digital Image
Processing
Lecture 9
AI 612

## Slide 2
Color Image Processing
Lecture 9
AI 612
Dr. Mohamed Mostafa
Prepared by
www.midocean.ae

## Slide 3
Image Morphology
Chapter
06
www.midocean.ae
Chapter 6:
Gonzalez, Rafael C. Digital image processing. Pearson education, India, 2009.
Resources for this lecture

## Slide 4: Color Image Processing
Motivations:
Color is a powerful descriptor that often simplifies object identification and extraction from a scene.
A humans can discern thousands of color shades, compared to only about two dozen shades of gray.

## Slide 5: Color Image Processing
Areas:
Pseudo-color processing:
  The process of assigning color(s) to a particular grayscale intensity or range of intensities.
Full-color processing:
  images typically are acquired using a full-color sensor, such as a digital camera, or color scanner.
Image source: Reseachgate

## Slide 6: Color Fundamentals
In 1666, Sir Isaac Newton, 24 year old, discovered white light spectrum.
The emerging light is not white, but consists instead of a continuous spectrum of colors ranging from violet at one end to red at the other (violet, blue, green, yellow, orange, and red.).

## Slide 7: Color Fundamentals
Basically, the colors that humans and some other animals perceive in an object are determined by the nature of the light reflected from the object.

## Slide 8: Color Fundamentals
Basically, visible light wavelength: from around 400 to 700 nm

## Slide 9: Color Fundamentals
For example,
green objects reflect light with wavelengths primarily in the 500 to 570 nm range, while absorbing most of the energy at other wavelengths.

## Slide 10: White Color Characteristics
1. For an achromatic (monochrome, gray scale) light source,
  there is only 1 attribute to describe the quality: intensity (Brightness)
2. For a chromatic light source (400 to 700 nm), there are 3 attributes to describe the quality:
  Radiance = total amount of energy flow from a light source (Watts)
  Luminance = amount of energy received by an observer (lumens)
    Brightness = intensity

## Slide 11: Color Models
The purpose of a color model (also called a color space or color system) is to facilitate the specification of colors in some standard way.
Colors’ models:
  Hardware oriented models:
    RGB (red, green, blue)  for monitors and cameras
    CMY (cyan, magenta, yellow)  for printing
  Image processing oriented models:
    HSI (hue, saturation, intensity)  it decouples the color and gray-scale information in an image

## Slide 12: RGB Model
In the RGB model, each color appears in its primary spectral components of red, green, and blue.
The number of bits used to represent each pixel in RGB space is called the pixel depth.
An RGB image in which each of the red, green, and blue images is an 8-bit image. Under these conditions, each RGB color pixel [that is, a triplet of values (R, G, B)] has a depth of 24 bits (3 image planes times the number of bits per plane).
The term full-color image is used often to denote a 24-bit RGB color image.
The total number of possible colors in a 24-bit RGB image is (28 )3 = 16, 777, 216.
Note :
Pixel depth (color depth): refers to the number of bits used to represent the color of each pixel in an image.
- In a grayscale image, a pixel depth of 8 bits represents 256 different shades of gray (28 = 256).

## Slide 13
(Images from Rafael C. Gonzalez and Richard E.
Wood, Digital Image Processing, 2nd Edition.
Color Gamut of Color Monitors and Printing Devices
Color Monitors
Printing devices
Human eye

## Slide 14
RGB Color Model
Purpose of color models: to facilitate the specification of colors in some standard
RGB color models:
based on Cartesian
coordinate system

## Slide 15
RGB Color Cube
R = 8 bits
G = 8 bits
B = 8 bits
Color depth 24 bits
= 16777216 colors
Hidden faces
of the cube

## Slide 16
RGB Color Model (cont.)
Red fixed at 127

## Slide 17
Safe RGB Colors
Safe RGB colors: a subset of RGB colors.
There are 216 colors common in most operating systems.

## Slide 18
RGB Safe-color Cube
The RGB Cube is divided into
6 intervals on each axis to achieve
the total 63 = 216 common colors.
However, for 8 bit color representation, there are the total 256 colors. Therefore, the remaining 40 colors are left to OS.

## Slide 19: Primary and Secondary Colors
The purpose of a color model (also called a color space or color system) is to facilitate the specification of colors in some standard way.
Primary
color
Primary
color
Primary
color
Secondary
colors
Primary and Secondary Colors

## Slide 20
Additive primary colors: RGB
use in the case of light sources
such as color monitors
Subtractive primary colors: CMY
use in the case of pigments in
printing devices
RGB add together to get white
White subtracted by CMY to get
Black
Primary and Secondary Colors

## Slide 21
CMY and CMYK Color Models
C = Cyan (G+B)
M = Magenta (R+B)
Y = Yellow(R+G)
K = Black (R+G+B)  Muddy brown instead of black

## Slide 22
The HSI Color Model
RGB, CMY models are not good for human interpreting
HSI Color model:
Hue: Dominant color
Saturation: Relative purity (inversely proportional to amount of white light added)
Intensity: Brightness
Color carrying
information

## Slide 23
Relationship Between RGB and HSI Color Models
RGB
HSI

## Slide 24
Hue and Saturation on Color Planes
1. A dot is the plane is an arbitrary color
2. Hue is an angle from a red axis.
3. Saturation is a distance to the point.

## Slide 25
HSI Color Model (cont.)
Intensity is given by a position on the vertical axis.

## Slide 26
Converting Colors from RGB to HSI

## Slide 27
Converting Colors from HSI to RGB
RG sector:
GB sector:
BR sector:

## Slide 28
Color Image Processing
There are 2 types of color image processes
1. Pseudocolor image process: Assigning colors to gray values based on a specific criterion. Gray scale images to be processed may be a single image or multiple images such as multispectral images
2. Full color image process: The process to manipulate real color images such as color photographs.

## Slide 29
Pseudocolor Image Processing
Why we need to assign colors to gray scale image?
Answer: Human can distinguish different colors better than different
shades of gray.
Pseudocolor (sometimes called false color) image processing consists of assigning
colors to gray values based on a specified criterion

## Slide 30
Intensity Slicing or Density Slicing
Formula:
C1 = Color No. 1
C2 = Color No. 2
T
Intensity
Color
C1
C2
T
0
L-1
A gray scale image viewed as a 3D surface.

## Slide 31
Intensity Slicing Example
An X-ray image of a weld with cracks
After assigning a yellow color to pixels with
value 255 and a blue color to all other pixels.

## Slide 32
Multi Level Intensity Slicing
Ck = Color No. k
lk = Threshold level k
Intensity
Color
C1
C2
0
L-1
l1
l2
l3
lk
lk-1
C3
Ck-1
Ck

## Slide 33
An X-ray image of the Picker
Thyroid Phantom.
After density slicing into 8 colors
Multi Level Intensity Slicing

## Slide 34
Color Coding Example
A unique color is assigned to each intensity value.
Gray-scale image of average
monthly rainfall.
Color coded image
Color
map
South America region

## Slide 35
(Images from Rafael C. Gonzalez and Richard E.
Wood, Digital Image Processing, 2nd Edition.
Gray Level to Color Transformation
Assigning colors to gray levels based on specific mapping functions
Red Frequencies
Green Frequencies
Blue Frequencies
Gray scale image

## Slide 36
Old Movies Coloring
Gray Level to Color Transformation

## Slide 37
Basics of Full-Color Image Processing
The two methods:
1. Per-color-component processing: process each component separately.
2. Vector processing: treat each pixel as a vector to be processed.
Example of per-color-component processing: smoothing an image
By smoothing each RGB component separately.
In order for per-component-image and vector-based processing to be equivalent, two conditions have to be satisfied:
first, the process has to be applicable to both
vectors and scalars;
second, the operation on each component of a vector (i.e., each voxel) must be independent of the other components.

## Slide 38
Example: Full-Color Image and Various Color Space Components
Color image
CMYK components
RGB components
HSI components

## Slide 39
Color Transformation
Formulation:
f(x,y) = input color image, g(x,y) = output color image
T = operation on f over a spatial neighborhood of (x,y)
When only data at one pixel is used in the transformation, we
can express the transformation as:
i= 1, 2, …, n
Where ri = color component of f(x,y)
si = color component of g(x,y)
Use to transform colors to colors.
For RGB images, n = 3

## Slide 40
Example: Color Transformation
Formula for RGB:
Formula for CMY:
Formula for HSI:
These 3 transformations give
the same results.
k = 0.7
I
H,S

## Slide 41
(Images from Rafael C. Gonzalez and Richard E.
Wood, Digital Image Processing, 2nd Edition.
Color Complements
Color complement replaces each color with its opposite color in the
color circle of the Hue component. This operation is analogous to
image negative in a gray scale image.
Color circle (color wheel)

## Slide 42
Color Complement Transformation Example

## Slide 43
Color Slicing Transformation
We can perform “slicing” in color space: if the color of each pixel is far from a desired color more than threshold distance, we set that color to some specific color such as gray, otherwise we keep the
original color unchanged.
i= 1, 2, …, n
or
Set to gray
Keep the original
color
Set to gray
Keep the original
color
i= 1, 2, …, n

## Slide 44
Color Slicing Transformation Example
Original image
After color slicing

## Slide 45
Tonal Correction Examples
In these examples, only
brightness and contrast are
adjusted while keeping color
unchanged.
This can be done by
using the same transformation
for all RGB components.
Power law transformations
Contrast enhancement
Flat (low contrast image)
light (high key) Image
dark (low key) color image

## Slide 46
Color Balancing Correction Examples
Color imbalance: primary color components in white area
are not balance. We can measure these components by
using a color spectrometer.
Color balancing can be
performed by adjusting
color components separately
as seen in this slide.

## Slide 47
Histogram Equalization of a Full-Color Image
Histogram equalization of a color image can be performed by
adjusting color intensity uniformly while leaving color unchanged.
The HSI model is suitable for histogram equalization where only
Intensity (I) component is equalized.
where r and s are intensity components of input and output color image.

## Slide 48
Histogram Equalization of a Full-Color Image
Original image
After histogram
equalization
After increasing
saturation component
Normalized

## Slide 49
Color Image Smoothing
Two Methods:
Per-color-plane method: for RGB, CMY color models
Smooth each color plane using moving averaging and
the combine back to RGB
Smooth only Intensity component of a HSI image while leaving
H and S unmodified.
Note: 2 methods are not equivalent.

## Slide 50
Color Image Smoothing Example (cont.)
Color image
Red
Green
Blue

## Slide 51
(Images from Rafael C. Gonzalez and Richard E.
Wood, Digital Image Processing, 2nd Edition.
Color Image Smoothing Example (cont.)
Hue
Intensity
Color image
HSI Components
Hue
Saturation
Intensity

## Slide 52
Color Image Smoothing Example (cont.)
Smooth all RGB components
Smooth only I component of HSI
(faster)

## Slide 53
Color Image Smoothing Example (cont.)
Difference between
smoothed results from 2
methods in the previous
slide.

## Slide 54
Color Image Sharpening
We can do in the same manner as color image smoothing:
  1. Per-color-plane method for RGB,CMY images
  2. Sharpening only I component of a HSI image
Sharpening all RGB components
Sharpening only I component of HSI

## Slide 55
Color Image Sharpening Example (cont.)
Difference between
sharpened results from 2
methods in the previous
slide.

## Slide 56
Thank You