## Slide 1
Lecture 2
ITC202
The System Unit: Processing and Memory
Dr. Eng. Youssef Ntefeh
Prepared by
Internet and Information Technology

## Slide 2
Chapter 2:
The System Unit: Processing and Memory
Data and Program Representation
Digital Data Representation
The Binary Numbering System
Coding Systems for Text-Based Data
Coding Systems for Images
Coding Systems for Audio
Representing Programs: Machine Language
Inside the System Unit
The Motherboard
The CPU
Memory
Fans, Heat Sinks, and Other Components
Expansion Slots and Expansion Cards
How the CPU Works
Typical CPU Components
Making Computers Faster and Better

## Slide 3: Learning Objectives
Understand how data and programs are represented to a computer and be able to identify a few of the coding systems used to accomplish this.
Explain the functions of the hardware components commonly found inside the system unit, such as the CPU, memory, buses, and expansion cards.
Describe how new peripheral devices or other hardware can be added to a computer.

## Slide 4: Learning Objectives
Understand how the computer system’s CPU and memory components process program instructions and data.
Name and evaluate several strategies that can be used today for speeding up the operations of a computer.
List some technologies that may be used in the future computers.

## Slide 5: Overview
This lecture covers:
  How computers represent data and program instructions.
  How the CPU, memory, and other components located inside the system unit are arranged, as well as the characteristics of the components.
  How the CPU performs processing tasks.

## Slide 6: Data and Program Representation
In order to be understood by a computer, data and programs need to be represented appropriately.
Coding systems: Used to represent data and programs in a manner understood by the computer.
Digital computers: Can only understand two states, off and on (0 and 1).
Digital data representation: The process of representing data in digital form so it can be understood by a computer.

## Slide 7: Digital Data Representation
  Bit: The smallest unit of data that a binary computer can recognize (a single 1 or 0).
Byte = 8 bits.
Byte terminology used to express the size of documents and other files, programs, etc.
Prefixes are often used to express larger quantities of bytes: kilobyte (KB), megabyte (MB) , gigabyte (GB), terabyte (TB), etc.

## Slide 8: The Binary Numbering System
Numbering system: A way of representing numbers.
Decimal numbering system:
  Uses 10 symbols (0-9).
Binary numbering system:
  Uses only two symbols (1 and 0) to represent all possible numbers.
In both systems, the position of the digits determines the power to which the base number (such as 10 or 2) is raised.

## Slide 9: The Binary Numbering System

## Slide 10: Coding Systems for Text-Based Data
ASCII and EBCDIC
  ASCII (American Standard Code for Information Interchange): coding system traditionally used with personal computers.
  EBCDIC (Extended Binary-Coded Decimal Interchange Code): developed by IBM, primarily for mainframe use.

## Slide 11: Coding Systems for Text-Based Data
Unicode: newer code (32 bits per character is common); universal coding standard designed to represent text-based data written in any ancient or modern language.
Replacing ASCII as the primary text-coding system.

## Slide 12: Coding Systems for images
Images also need to be converted into binary in order for a computer to process them so that they can be seen on our screen. Digital images are made up of pixels. Each pixel in an image is made up of binary numbers.
If we say that 1 is black (or on) and 0 is white (or off), then a simple black and white picture can be created using binary.

## Slide 13: Coding Systems for images
To create the picture, a grid can be set out and the squares colored (1 – black and 0 – white). But before the grid can be created, the size of the grid needs be known. This data is called metadata and computers need metadata to know the size of an image. If the metadata for the image to be created is 10x10, this means the picture will be 10 pixels across and 10 pixels down.
This example shows an image created in this way:
0001111000 0001001000 0001001000 1111111111 1111111111 0100000010

## Slide 14: Coding Systems for images
Adding color
The system described so far is fine for black and white images, but most images need to use colors as well. Instead of using just 0 and 1, using four possible numbers will allow an image to use four colors. In binary this can be represented using two bits per pixel:
  00 – white.
  01 – blue.
  10 – green.
  11 – red.

## Slide 15: Coding Systems for images
While this is still not a very large range of colors, adding another binary digit will double the number of colors that are available:
1 bit per pixel (0 or 1): two possible colours.
2 bits per pixel (00 to 11): four possible colours.
3 bits per pixel (000 to 111): eight possible colours.
4 bits per pixel (0000 – 1111): 16 possible colours.
16 bits per pixel (0000 0000 0000 0000 – 1111 1111 1111 1111): over 65 000 possible colors.

## Slide 16: Coding Systems for images
0000 | Color1
0001 | Color2
0010 | Color3
0011 | Color4
0100 | Color5
0101 | Color6
0110 | Color7
0111 | Color8
1000 | Color9
1001 | Color10
1010 | Color11
1011 | Color12
1100 | Color13
1101 | Color14
1110 | Color15
1111 | Color16

## Slide 17: Coding Systems for Audio data
Sound needs to be converted into binary for computers to be able to process it. To do this, sound is captured - usually by a microphone - and then converted into a digital signal.
An analogue to digital converter will sample a sound wave at regular time intervals. For example, a sound wave like this can be sampled at each time sample point.
The samples can then be converted to binary. They will be recorded to the nearest whole number.
Time sample | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Denary | 8 | 3 | 7 | 6 | 9 | 7 | 2 | 6 | 6 | 6
Binary | 1000 | 0011 | 0111 | 0110 | 1001 | 0111 | 0010 | 0100 | 0110 | 0110

## Slide 18: Coding Systems for Audio data
If the time samples are then plotted back onto the same graph, it can be seen that the sound wave now looks different. This is because sampling does not take into account what the sound wave is doing in between each time sample.
This means that the sound loses quality as data has been lost between the time samples. The way to increase the quality and store the sound at a quality closer to the original, is to have more time samples that are closer together. This way, more detail about the sound can be collected, so when it’s converted to digital and back to analogue again it does not lose as much quality.

## Slide 19: Coding Systems for Audio data
The frequency at which samples are taken is called the sample rate, and is measured in Hertz (Hz). 1 Hz is one sample per second.
Most CD-quality audio is sampled at 44 100 or 48 000 KHz.

## Slide 20: Representing Programs: Machine Language

## Slide 21: Representing Programs: Machine Language
Machine language: Binary-based language for representing computer programs the computer can execute directly.
  Early programs were written in machine language.
  Today’s programs still need to be translated into machine language in order to be understood by the computer.
Most programs are written in other programming languages .
  Language translators are used to translate the programs into machine language.

## Slide 22
Chapter 2:
The System Unit: Processing and Memory
Data and Program Representation
Digital Data Representation
The Binary Numbering System
Coding Systems for Text-Based Data
Coding Systems for Images
Coding Systems for Audio
Representing Programs: Machine Language
Inside the System Unit
The Motherboard
The CPU
Memory
Fans, Heat Sinks, and Other Components
Expansion Slots and Expansion Cards
How the CPU Works
Typical CPU Components
Making Computers Faster and Better

## Slide 23: Inside the System Unit
System unit: The main case of a computer
  A computer case, also known as a computer chassis is the enclosure that contains most of the components of a personal computer (usually excluding the display, keyboard, and mouse).
  Cases are usually constructed from steel, aluminum and plastic. Other materials such as glass and wood .
  Houses the processing hardware for a computer.
  Also contains storage devices, the power supply, and cooling fans.
  Houses the CPU, memory, interfaces to connect to peripheral devices (printers, etc), and other components such as CD/DVD drives.
  With a desktop computer, usually looks like a rectangular box.

## Slide 24: Inside the System Unit

## Slide 25: The Motherboard

## Slide 26: The Motherboard
Computer chip: A very small pieces of silicon or other semi-conducting material onto which integrated circuits are embedded.
Circuit board: A thin board containing computer chips and other electronic components.
Motherboard or system board: The main circuit board inside the system unit.
  All devices must connect to the motherboard.
  External devices (monitors, keyboards, mice, printers) typically connect by plugging into a port exposed through the exterior of the system unit.
  Wireless devices connect through a transceiver or wireless networking technology (like Bluetooth).

## Slide 27: The CPU
The CPU is the core component that defines a computing device, and while it is of critical importance, the CPU can only function alongside other hardware. The silicon chip sits in a special socket located on the main circuit board inside the device.
CPUs are built by placing billions of microscopic transistors onto a single computer chip. Those transistors allow it to make the calculations it needs to run programs that are stored on your system’s memory.

## Slide 28: The CPU
They’re gates that switch on or off, thereby conveying the ones or zeros that translate into everything you do with the device, be it watching videos or writing an email.
Dual-core CPU: Contains the processing components (cores) of two separate processors on a single CPU.
Quad-core CPU: Contains 4 cores.
Typically different CPUs for desktop computers, portable computers, servers, mobile devices, etc.

## Slide 29: The CPU

## Slide 30: The CPU

## Slide 31: Clock Cycle and Frequency

## Slide 32: Processing Speed
CPU clock speed: One measurement of processing speed.
  Measured in megahertz (MHz) or gigahertz (GHz).
  Higher CPU clock speed = more instructions processed per second.
Alternate measure of processing speed is the number of instructions a CPU can process per second.
  Megaflops, gigaflops, teraflops.
Other factors (CPU architecture, memory, bus speed, amount of RAM, etc.) also affect the overall processing speed of a computer.
Benchmark tests: Can be used to evaluate overall processing speed.

## Slide 33: Word Size and Cache Memory
Word size: The amount of data that a CPU can manipulate at one time.
  Typically 32 or 64 bits.
Cache memory: Special group of very fast memory chips located on or close to the CPU.
  Level 1 is fastest, then Level 2, then Level 3.
  More cache memory typically means faster processing.
  Usually internal cache (built into the CPU).
  Often some cache dedicated to each core; may also have some shared cache accessible by any core.

## Slide 34: Bus Width, Bus Speed, and Bandwidth
Bus: An electronic path over which data can travel.
Bus width: The number of wires in the bus over which data can travel.
Bus width and speed determine the throughput (or bandwidth) of the bus.
  The amount of data that can be transferred by the bus in a given time period.

## Slide 35: Memory
Memory refers to chip based storage.
RAM (random access memory): Computer’s main memory.
  Consists of chips arrange on a circuit board called a memory module plugged into the motherboard.
  Stores essential parts of operating system, programs, and data the computer is currently using.
  Volatile: Contents of RAM is lost when the computer is shut off.

## Slide 36: Memory
ROM (read-only memory): Non-volatile chips located on the motherboard into which data or programs have been permanently stored.
  Retrieved by the computer when needed.
Flash memory: Type of nonvolatile memory that can be erased and reprogrammed.
  Some flash memory chips are used by the computer.
  Flash memory chips are also used in flash memory storage media (sticks, cards, and drives).

## Slide 37: Fans, Heat Sinks, and Other Cooling Components

## Slide 38: Fans, Heat Sinks, and Other Cooling Components
Heat: A continuing problem for CPU and computer manufacturers.
Fans: Used on most personal computers.
Heat sinks: Small components typically made out of aluminum with fins that help to dissipate heat.
Water cooling systems: Cool the computer with liquid-filed tubes.
Notebook cooling stands.
Other cooling methods (such as ion pump cooling systems) are under development.

## Slide 39: Fans, Heat Sinks, and Other Cooling Components

## Slide 40: Expansion Slots, Expansion Cards, and Express Cards
Expansion slot: A location on the motherboard into which expansion cards are inserted.
Expansion card: A circuit board used to add additional functionality or to attach a peripheral device.
Express Card modules: Designed for notebook computer expansion.

## Slide 41
Chapter 2:
The System Unit: Processing and Memory
Data and Program Representation
Digital Data Representation
The Binary Numbering System
Coding Systems for Text-Based Data
Coding Systems for Images
Coding Systems for Audio
Representing Programs: Machine Language
Inside the System Unit
The Motherboard
The CPU
Memory
Fans, Heat Sinks, and Other Components
Expansion Slots and Expansion Cards
How the CPU Works
Typical CPU Components
Making Computers Faster and Better

## Slide 42: How the CPU Works
CPU: Consists of a variety of circuitry and components packaged together.
  Transistor: Key element of the microprocessor
    Made of semi-conductor material that acts like a switch controlling the flow of electrons inside a chip.
Today’s CPUs contain hundreds of millions of transistors; the number doubles about every 18 months (Moore’s Law).

## Slide 43: Typical CPU Components
Arithmetic/Logic Unit (ALU): Performs integer arithmetic and logical operations.
Floating Point Unit (FPU): Performs decimal arithmetic.
Control unit: Coordinates and controls activities.
Prefetch unit: Tries to fetch data and instructions before they are needed from cache or RAM.
Decode unit: Translates instructions so they are understood by the control unit, ALU, and FPU.
Internal cache: Store data and instructions needed by the CPU.
Bus interface unit: Allows the core to communicate with other CPU components.

## Slide 44: Making Computers Faster and Better
  Perform system maintenance:
    Uninstall programs properly.
    Consider placing large files on external storage devices.
    Delete temporary files.
    Error check and defragment.
    Scan for viruses and spyware.
    Clean out dust once or twice a year.
  Add more memory.
  Buy a larger or second hard drive.
  Upgrade your Internet connection.
  Upgrade your video graphics card.

## Slide 45: Review: Representing data
  Bit: The smallest unit of data that a binary computer can recognize (a single 1 or 0). Byte = 8 bits.
Decimal numbering system.
  Uses 10 symbols (0-9).
Binary numbering system.
  Uses only two symbols (1 and 0) to represent all possible numbers.
In both systems, the position of the digits determines the power to which the base number (such as 10 or 2) is raised.

## Slide 46: Review: Representing images
Images also need to be converted into binary.
Need metadata to know the size of an image.
Adding binary digit will double the number of colours that are available:
1 bit per pixel (0 or 1): two possible colours.
2 bits per pixel (00 to 11): four possible colours.
3 bits per pixel (000 to 111): eight possible colours.
4 bits per pixel (0000 – 1111): 16 possible colours.

## Slide 47: Review: Representing audio
An analogue to digital converter will sample a sound wave at regular time intervals.
The samples can then be converted to binary. They will be recorded to the nearest whole number.
More time samples that are closer together more detail about the sound can be collected, so does not lose as much quality.
The frequency at which samples are taken is called the sample rate.
Time sample | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Denary | 8 | 3 | 7 | 6 | 9 | 7 | 2 | 6 | 6 | 6
Binary | 1000 | 0011 | 0111 | 0110 | 1001 | 0111 | 0010 | 0100 | 0110 | 0110

## Slide 48: Review: Motherboard
CPU, power supply, fan, hard drive, DVD drive, ports, memory slots, expansion slots, expansion cards.
CPU is the core component that defines a computing device.
Billions of microscopic transistors.
Processing speed measurments (CPU clock speed, IPC, number of cores, architecture, memory speed, bus speed, ram size.
Memory hierarchy ( HD, RAM, Cache, registers).
Bus width and speed determine the throughput of the bus.
Fans, Heat sinks, Water cooling systems.

## Slide 49: Reference