## Slide 1
Prepared by Dr. Eng. Gamal Selim
Computer Organization and Architecture
Lecture 08

## Slide 2
Revision

## Slide 3
Decoders

## Slide 4: Decoder
  Accepts a value and decodes it
    Output corresponds to value of n inputs
  Consists of:
    Inputs (n)
    Outputs (2n , numbered from 0  2n - 1)
    Selectors / Enable (active high or active low)

## Slide 5: 2-to-4 Decoder

## Slide 6: 2-to-4 Decoder

## Slide 7: Example on expansion decoder
Construct a 5-to-32 decoder using only 2-to-4 decoders and 3-to-8 decoders (with enable).
We are going to make 5-to-32 decoder like the one shown below:

## Slide 8: Example on expansion decoder
We need four 3-to-8 decoder for the last stage and one 2-to-4 decoder for selecting each of them at the first stage:

## Slide 9
Encoders

## Slide 10: Encoders

## Slide 11
4-to-2 line Encoder

## Slide 12: 4 to 2 line Encoder
In 4 to 2 line encoder, there are total of four inputs, i.e., Y0, Y1, Y2, and Y3, and two outputs, i.e., A0 and A1. In 4-input lines, one input-line is set to true at a time to get the respective binary code in the output side. Below are the block diagram and the truth table of the 4 to 2 line encoder.

## Slide 13: 4 to 2 line Encoder

## Slide 14: 4 to 2 line Encoder

## Slide 15: 4 to 2 line Encoder
The logical expression of the term A0 and A1 is as follows:
A1=Y3+Y2 A0=Y3+Y1

## Slide 16
Encoder vs Decoder

## Slide 17: Encoder vs Decoder
ENCODER | DECODER
Encoder circuit basically converts the applied information signal into a coded digital bit stream. | Decoder performs reverse operation and recovers the original information signal from the coded bits.
In case of encoder, the applied signal is the active signal input. | Decoder accepts coded binary data as its input.
The number of inputs accepted by an encoder is 2n. | The number of input accepted by decoder is only n inputs.
The output lines for an encoder is n. | The output lines of an decoder is 2n.

## Slide 18: Encoder vs Decoder
ENCODER | DECODER
The encoder generates coded data bits as its output. | The decoder generates an active output signal in response to the coded data bits.
The operation performed is simple. | The operation performed is complex.
The encoder circuit is installed at the transmitting end. | The decoder circuit is installed at the receiving side.
OR gate is the basic logic element used in it. | AND gate along with NOT gate is the basic logic element used in it.

## Slide 19
Digital Circuits Cont.

## Slide 20: Digital Circuits Cont.
Multiplexer
Demultiplexer

## Slide 21: Multiplexer / Demultiplexer
The basic function of the Multiplexer (MUX).
The typical application of a MUX.
A 4-to-1 MUX designed with Small Scale Integration (SSI).
A 4-to-1, 8-to-1, & 16-to-1 Medium Scale Integration (MSI) MUX.
The basic function of the Demultiplexer (DEMUX).
The typical application of a DEMUX.
A 1-to-4 DEMUX design with Small Scale Integration (SSI).

## Slide 22
Multiplexer (MUX)

## Slide 23: What is a Multiplexer (MUX)?
The term Multiplexer means many into one.
Multiplexing is the process of transmitting a large number of information over a single line.
A Digital Multiplexer (MUX) is a combinational Circuit that select one digital information from several sources and transmits the selected information on a single output line.
A Multiplexer is also called a Data Selector.
The Multiplexer has several data input line and a single output line.

## Slide 24: What is a Multiplexer (MUX)?
MUX directs one of the inputs to its output line by using a control bit word (selection line) to its select lines.
Multiplexer contains the followings:
  data inputs
  selection inputs
  a single output
Selection input determines the input that should be connected to the output.
The multiplexer acts like an electronic switch that selects one from different.

## Slide 25: What is a Multiplexer (MUX)?
A MUX is a digital switch that has multiple inputs (sources) and a single output (destination).
The select lines determine which input
is connected to the output.
MUX Types
   2-to-1 (1 select line)
   4-to-1 (2 select lines)
   8-to-1 (3 select lines)
   16-to-1 (4 select lines)

## Slide 26: Typical Application of a MUX

## Slide 27: 4-to-1 Multiplexer (MUX)

## Slide 28
DeMultiplexer (DEMUX)

## Slide 29: What is a Demultiplexer (DEMUX)?
The De-Multiplexer is a combinational logic circuit that performs the reverse operation of multiplexer (Several output lines, one input line).
De -Multiplexer means one to many. A De-Multiplexer is a circuit with one input and many output. By applying control signal, we can steer any input to the output. Few types of De -Multiplexer are 1-to 2, 1-to-4, 1-to-8 and 1-to 16 De -Multiplexer .
De-Multiplexer is the process of taking information from one input and transmitting the same over one of several outputs.

## Slide 30: What is a Demultiplexer (DEMUX)?
A DEMUX is a digital switch with a single input (source) and a multiple outputs (destinations).
The select lines determine which output
the input is connected to.
DEMUX Types
   1-to-2 (1 select line)
   1-to-4 (2 select lines)
   1-to-8 (3 select lines)
   1-to-16 (4 select lines)

## Slide 31: Typical Application of a DEMUX

## Slide 32: 1-to-4 De-Multiplexer (DEMUX)

## Slide 33: Example of expansion Multiplexer
  Design a 32-to-1 multiplexer using only 8-to-1 multiplexer
We use four 8-to-1 in the first stage and another
one to select between the output of the others:

## Slide 34
MUX vs DeMUX

## Slide 35: Difference between Multiplexer and Demultiplexer
  Both multiplexer and demultiplexer are types of combinational digital circuit that are used in several large-scale digital systems. However, there are many differences between a multiplexer and a demultiplexer, which are highlighted in the following table

## Slide 36: Difference between Multiplexer and Demultiplexer
Basis of Difference | Multiplexer | Demultiplexer
Definition | A multiplexer is a combinational digital circuit that takes multiple data inputs and provides only single output. | A demultiplexer is a combinational digital circuit that takes single input and provides multiple outputs.
Abbreviated name | The abbreviation used to represent the multiplexer is MUX. | The abbreviation used to represent the demultiplexer is DEMUX.
Input and output lines | Multiplexer has 2n input lines and 1 output line. Where, n is the number of select lines. | Demultiplexer has 1 input line and 2n output lines. Where, n is the number of select lines.
Also known as | Multiplexer is also known as a "data selector". | Demultiplexer is also known as "data distributor".

## Slide 37: Difference between Multiplexer and Demultiplexer
Basis of Difference | Multiplexer | Demultiplexer
Operating principle | The operating principle of the multiplexer is "many to one". | The operating principle of a demultiplexer is "ne to many".
Acts as | Multiplexer acts as a digital multi-position switch. | Demultiplexer acts as a digital circuit.
Conversion technique | A multiplexer performs parallel to serial conversion. | A demultiplexer performs serial to parallel conversion.
Function of control signal | In case of multiplexer, the function of control signal is to select a specific input that has to be transmitted at the output. | In demultiplexer, the function of control signal is to deliver the single input signal over the multiple output lines.

## Slide 38: Difference between Multiplexer and Demultiplexer
Basis of Difference | Multiplexer | Demultiplexer
Examples | Examples of some common multiplexers are − 8:1 Multiplexer 16:1 Multiplexer 32:1 Multiplexer | Some common demultiplexers are − 1:2 Demultiplexer 1:4 Demultiplexer 1:8 Demultiplexer 1:16 Demultiplexer
Practical importance | In practice, the multiplexer increases the efficiency of the communication system by enabling the data transmission using a single line. | In practice, the demultiplexer takes the output of a multiplexer and convert in its original form at the receiver end.

## Slide 39: Difference between Multiplexer and Demultiplexer
Basis of Difference | Multiplexer | Demultiplexer
Usage in time-division multiplexing | A multiplexer is used at the transmitter end in the time-division multiplexing (TDM). | The demultiplexer is used at the receiver end in the time-division multiplexing.
Applications | The multiplexers are commonly used in communication systems, telephone networks, computer memories, etc. | The demultiplexers are used in communication systems, reconstruction of parallel data, ALU, etc.

## Slide 40
  Thank You