## Slide 1
Prepared by Dr. Ahmed Omar
Lecture 2
IT391
System Administration 1
System Administration 1

## Slide 2
Network Foundations
Lecture 2
Dr. Ahmed Omar
Prepared by
IT391
System Administration 1

## Slide 3
Agenda
Introduction to Networks
Network Components Overview
Types of Networks
Network Topologies
Network Protocols
Client and Server
Network Operating System (NOS)
Virtual Machine (VM)

## Slide 4
Introduction to Networks
Definition of a Network
A network is a group of computers connected to each other to provide services to users.
Purpose
Enables communication, resource sharing, and access to modern technologies.

## Slide 5
Types of Network Services
Data Sharing
  Example: File server allows multiple users to access and share files.
Resource Sharing
  Example: Shared devices like printers and scanners.
Modern Technologies
  Examples: VOIP (Voice Over IP), Video Conferencing, Internet of Things (IoT), Cloud Computing.

## Slide 6
Types of Network Services
Data Sharing
  Example: File server allows multiple users to access and share files.
  Centralized storage for documents and media.
  Facilitates collaboration and backup.

## Slide 7
Types of Network Services
Resource Sharing
  Shared access reduces cost and increases efficiency.
  Users can send print or scan jobs from any connected device.
  Example: Shared devices like printers and scanners.

## Slide 8
Types of Network Services
Modern Technologies
VOIP
  Internet-based voice communication.
Video Conferencing
  Real-time video meetings over the network.
IoT (Internet of Things)
  Connecting smart devices for automation and monitoring.
Cloud Computing
  Access to computing resources and storage over the internet.

## Slide 9
Network Components Overview
Three Main Categories
End Devices
Network Devices
Media (Wired/Wireless)

## Slide 10
Network Components Overview
End Devices
Devices that users interact with directly.
Examples
  PCs (Personal Computers)
  Laptops
  CAM (likely refers to Cameras)
  IP Phones
  Printers

## Slide 11
Network Components Overview
Network Devices
Their primary roles : Establishing and Managing Connections

## Slide 12
Network Components Overview
Network Media
the physical pathways or channels that carry data signals between devices in a network.
serve as the channel over which data travels from the source to the destination, enabling communication between computers, servers, and other devices

## Slide 13
Network Components Overview
Network Media
Wired Media
Examples: Ethernet cables, fiber optics.
Advantages: High speed, reliability.
Wireless Media
Examples: Wi-Fi, Bluetooth.
Advantages: Mobility, ease of installation.

## Slide 14
Types of Networks
LAN (Local Area Network):
  Covers a small geographic area (e.g., home, school, office).
  Owned and maintained by a single organization.
  Used for sharing resources like files and printers within a building.

## Slide 15
Types of Networks
WAN (Wide Area Network):
  Spans a large area, connecting LANs across cities, countries, or globally.
  Used by organizations with multiple locations (e.g., banks, multinational companies)

## Slide 16
Network Topologies
Network topology refers to the arrangement of various elements (links, nodes, devices) in a computer network. It describes how different computers, devices, and network resources are physically or logically connected and how data flows between them

## Slide 17
Network Topologies
Ring Topology
In ring topology, devices are connected in a circular pattern, with each device connected to exactly two neighbors. Data travels unidirectionally around the ring until it reaches its destination

## Slide 18
Network Topologies
Star Topology
Star topology connects all devices to a central hub, switch, or concentrator, with each device having a dedicated connection to the central point. All communication between devices must pass through this central hub

## Slide 19
Network Topologies
Mesh Topology
Mesh topology connects every device to every other device in the network, creating multiple paths for data transmission. This configuration can be full mesh (every device connected to all others) or partial mesh (devices connected only to frequently communicating partners)

## Slide 20
Network Topologies
Bus Topology
Bus topology features all devices connected to a single main cable called the backbone, with terminators at both ends. In this configuration, data travels in one direction along the cable, and all connected devices receive the information, but only the intended recipient processes it

## Slide 21
Network Topologies
Hybrid network topology diagram illustrating combination of multiple topology types in a single network

## Slide 22
Network Topologies
Topology | Cost | Installation | Scalability | Reliability | Performance
Bus | Low | Easy | Limited | Low | Decreases with more devices
Star | Medium | Easy | Good | Good | Consistent
Ring | Medium | Moderate | Limited | Low | Predictable
Mesh | High | Complex | Excellent | Excellent | High
Hybrid | High | Complex | Excellent | Good | Variable

## Slide 23
Network Protocols
Network protocols are sets of rules that determine how devices communicate and exchange information across a network.
Key Protocols:
TCP
IP
HTTP
FTP

## Slide 24
Network Protocols
TCP (Transmission Control Protocol)
TCP is a connection-oriented protocol that ensures reliable, ordered, and error-checked delivery of data between applications over a network.

## Slide 25
What is Internet Protocol (IP)?
IP is a set of rules for addressing and routing data packets so they can travel across networks.
IP addresses are the backbone of device identification on the network.
Function:
Assigns unique addresses to devices.
Ensures data reaches the correct destination.
Example:
IPv4: 192.168.1.1; IPv6: 2001:db8:85a3::8a2e:370:7334

## Slide 26
HTTP (Hypertext Transfer Protocol)
HTTP is an application-layer protocol used for communication between web browsers (clients) and web servers, forming the foundation of data exchange on the World Wide Web.
Follows a client-server model: clients send requests, servers send responses.
Stateless protocol: each request is independent, with no memory of previous interactions.
Supports various data formats (HTML, images, video, etc.).

## Slide 27
FTP (File Transfer Protocol)
FTP is a standard protocol for transferring files between a client and a server over a TCP/IP network.
Uses a client-server model for uploading, downloading, and managing files.

## Slide 28
The Internet
The internet is a global network of interconnected computers, servers, phones, and smart devices communicating via protocols like TCP/IP
Infrastructure:
Built on LANs, WANs, fiber optics, copper wires, and wireless

## Slide 29
Intranet
An intranet is a private network used within an organization for sharing information, communication, and collaboration.
Features:
Accessible only to authorized users (usually employees).
Uses the same technologies as the internet (TCP/IP).
Includes tools like internal websites, search engines, and communication apps.

## Slide 30
Extranet
An extranet is a private network that allows controlled access to outsiders (e.g., partners, suppliers, customers) for collaboration and information sharing.
Requires strong authentication and monitoring due to external access
Use Cases:
Project collaboration
Supply chain management
Customer self-service platforms

## Slide 31
Client and Server
In networking, the client and server are two distinct roles that interact to provide and consume services or resources.
This model distributes tasks between clients (requesters) and servers (providers), forming the backbone of most modern network applications

## Slide 32
What is a Client?
A client is a hardware device or software application that initiates requests for services or resources from a server
Function:
Acts as the front end, interacting directly with the user.
Sends requests and processes responses from the server.
Characteristics:
Handles user interface and displays information.
Typically supports a single user login.
Simpler hardware and software configuration compared to servers

## Slide 33
What is a Server?
A server is hardware or software that provides resources, data, or services to clients over a network.
Function:
Acts as the back end, managing and storing data.
Waits for and processes client requests, then sends responses
Characteristics:
Can handle multiple client requests simultaneously.
More complex hardware and software setup, designed for reliability and scalability.
Supports multiple user logins

## Slide 34
create infograph for:
client example:Web browsers, email clients, laptops, smartphones, desktop computers
server example:Web servers, database servers, file servers, mail servers
Client and Server
Feature | Client | Server
Role | Requests services/resources | Provides services/resources
User Interaction | Direct (front end) | Indirect (back end)
Example Devices | Laptops, desktops, smartphones | Web server, database server, file server
Hardware/Software | Simple configuration | Advanced configuration
Number of Users | Typically single-user | Supports multiple users
Tasks | Initiates requests, processes responses | Handles requests, manages and stores data
Performance | Lower performance needs | High performance, reliability, and scalability
Dependency | Depends on server for services | Operates independently, serves many clients

## Slide 35
What is a Network Operating System (NOS)
A Network Operating System (NOS) is specialized software designed to manage, coordinate, and secure network resources, enabling multiple computers and devices to communicate, share files, and access shared resources like printers and applications within a network.
Purpose
Unlike a traditional OS (which manages a single device), a NOS manages the entire network, ensuring efficient, secure, and reliable operations across all connected devices.

## Slide 36
Main Functions of a Network Operating System
Resource Sharing
User and Group Management
Network Security
Remote Access
Monitoring and Troubleshooting
Data Backup and Recovery

## Slide 37
Types of Network Operating Systems
Peer-to-Peer (P2P) NOS
  All devices are equal; users share resources directly.
  Best for small networks; less expensive and easier to set up.
  Example: Windows for Workgroups
Client-Server NOS
  Central server provides resources and services to client devices.
  Centralized management, better security, and scalability.
  Example: Windows Server, Linux Server, UNIX

## Slide 38
Key Features of Modern NOS
Centralized Resource Management.
Multiuser and Multitasking Support
Scalability
Stability and Reliability
Hardware Compatibility

## Slide 39
NOS in Practice – Use Cases
Corporate Networks:
  Centralized management of departments, offices, and resources
Educational Institutions:
  Manage computer labs, student accounts, and shared learning resources.
Healthcare:
  Secure management of patient data and interdepartmental communication.
Government and SMEs:
  Efficient, secure, and scalable networking for public sector and small businesses

## Slide 40
What is a Virtual Machine (VM)
  A virtual machine (VM) is a software-based emulation of a physical computer. It runs programs and operating systems in an isolated environment, using virtualized hardware resources such as CPU, memory, storage, and network interfaces.
  Key Concept:
  Multiple VMs can run on a single physical "host" machine, each VM acting as a separate "guest" computer with its own OS and applications

## Slide 41
Introduction to VMware Workstation
  VMware Workstation is a leading desktop virtualization software that allows users to create, configure, and manage multiple virtual machines on a single Windows or Linux computer

## Slide 42
Download and install VMware Workstation

## Slide 43
VMware Fusion Pro
Download link
https://www.vmware.com/products/desktop-hypervisor/workstation-and-fusion
Download and install VMware Workstation

## Slide 44
Installation
Download and install VMware Workstation

## Slide 45
Installation
Download and install VMware Workstation

## Slide 46
Installation
Download and install VMware Workstation

## Slide 47
Open VMware Workstation

## Slide 48
Open VMware Workstation

## Slide 49
Thank You