## Slide 1
Prepared by Dr. Khaled Eskaf
Human-Robot Interaction and Autonomous Systems
Lecture 9
AI 616
Master of Science in Artificial intelligence

## Slide 2
www.midocean.ae

## Slide 3
Chapter
08
www.midocean.ae

## Slide 4
Chapter
08
www.midocean.ae
Notes: 6

## Slide 5
Chapter
08
www.midocean.ae
Color-Based Navigation for a Webots Robot Using Camera Input 3X3 Matrix
Analyze a 3x3 matrix around the central pixel and use the average color values for decision-making.
We'll calculate the average red, green, and blue values of the nine pixels at the center of the image and use these averages to determine the robot's movement.
-1 | 0 | +1
-1 | 0 | +1
-1 | 0 | +1
Notes: 6

## Slide 6
www.midocean.ae
Main Simulation Loop to Analyze a 3x3 Pixel Matrix
-1 | 0 | +1
-1 | 0 | +1
-1 | 0 | +1
Chapter
08
Notes: 6

## Slide 7
www.midocean.ae
Main Simulation Loop to Analyze a 3x3 Pixel Matrix
# Adjust thresholds and decisions based on the average color
RED_THRESHOLD = 100
GREEN_THRESHOLD = 45
BLUE_THRESHOLD = 45
RED_THRESHOLD2 = 45
GREEN_THRESHOLD2 = 45
BLUE_THRESHOLD2 = 100
if avg_red > RED_THRESHOLD and avg_green < GREEN_THRESHOLD and avg_blue < BLUE_THRESHOLD:
left_motor.setVelocity(5) # Turn right
right_motor.setVelocity(-5)
elif avg_blue > BLUE_THRESHOLD2 and avg_green < GREEN_THRESHOLD2 and avg_red < RED_THRESHOLD2:
left_motor.setVelocity(-5) # Move backward
right_motor.setVelocity(-5)
else:
left_motor.setVelocity(5) # Move forward
right_motor.setVelocity(5)
Chapter
08
Notes: 6

## Slide 8
Chapter
08
www.midocean.ae
Notes: 6

## Slide 9
Chapter
08
www.midocean.ae
Control the robot's speed based on color detection—moving faster if the color is green and very slowly if the color is red.
We are going to use Machine Learning Algorithm.
We are going to use Linear regression.
Let's assume:
A high "color score" represents green, encouraging faster movement.
A low "color score" represents red, dictating slower movement.
For simplicity, let's say our model has determined the relationship between color score and speed
as y=0.2x−1,
where y is the robot's speed,
and x is the color score (ranging from 0 for red to 5 for green).
Notes: 6

## Slide 10
Chapter
08
www.midocean.ae
Color Score: This is a conceptual representation of how "green" or "red" the camera's view is. (by averaging the RGB values).
Linear Regression Model: The model y = 0.2x - 1 is a simple formula we're using to decide the robot's speed based on the detected color. The specific coefficients (0.2 and -1) are placeholders for this example and would be determined through actual model training in a real-world application.
Speed Adjustment: The speed is adjusted based on the color score, with a higher score (more green) resulting in faster speed and a lower score (more red) resulting in slower speed or stopping.
Notes: 6

## Slide 11
www.midocean.ae
from controller import Robot, Camera
# Initialization
robot = Robot()
timestep = int(robot.getBasicTimeStep())
# Assuming motor and camera initialization here
camera = robot.getDevice('camera')
camera.enable(timestep)
left_motor = robot.getDevice('left wheel motor')
right_motor = robot.getDevice('right wheel motor')
left_motor.setPosition(float('inf')) # Enable speed control
right_motor.setPosition(float('inf'))
left_motor.setVelocity(0) # Initially stop
right_motor.setVelocity(0)
Chapter
08
Notes: 6

## Slide 12
www.midocean.ae
while robot.step(timestep) != -1:
# Simulate getting a color score from the camera
# Let's say color score calculation logic has been applied here
# For simplification, assume we get this score directly from the camera
# A real implementation would involve analyzing the camera image
color_score = 3 # Placeholder for the actual color score calculation (0 = red, 5 = green)
# Apply the linear regression model
# For our example, the model equation is y = 0.2x - 1
predicted_speed = 0.2 * color_score - 1 # Simplified model to control speed based on color score
# Ensure the speed is within the robot's operational range
predicted_speed = max(-10, min(10, predicted_speed))
# Set the robot's motors to the predicted speed
left_motor.setVelocity(predicted_speed)
right_motor.setVelocity(predicted_speed)
Chapter
08
Notes: 6

## Slide 13
Chapter
08
www.midocean.ae
A simple machine learning (ML) algorithm into the previous Webots robot navigation example introduces beginners to the intersection of robotics and ML. A straightforward approach is to use a decision tree classifier to decide the robot's movement based on the average color detected by the camera in a 3x3 pixel area. This example assumes you have basic data to train the classifier, representing average color values for different actions (move forward, turn right, move backward).
This example will be conceptual, as implementing a full ML pipeline involves steps (like data collection and model training) that go beyond the scope of running code directly in the Webots environment.
We are going to use a simple decision tree classifier using scikit-learn, a popular ML library for Python.
Machine Learning (ML) Algorithm
Notes: 6

## Slide 14
Chapter
08
www.midocean.ae
Step 1: Install scikit-learn
To install scikit-learn in Webots, or any Python environment within a simulation or application, you generally need to ensure that Python is correctly set up and that you have the necessary permissions to install additional libraries. Here's a step-by-step guide to installing scikit-learn for use with Webots:
Step 1: Identify Your Python Environment
First, determine which Python environment Webots is using. Webots can use a global Python installation or a virtual environment. You can specify or check this in the Webots preferences:
Open Webots.
Go to Tools > Preferences (on macOS, Webots > Preferences).
In the General tab, check the Python command setting to see which Python is being used.
Notes: 6

## Slide 15
Chapter
08
www.midocean.ae
Step 2: Install scikit-learn
Using a Global Python Installation
If Webots is configured to use your global Python installation, you can install scikit-learn using pip in your command line or terminal. Make sure you have pip installed and then run:
pip install scikit-learn
Using a Virtual Environment
If Webots is using a Python virtual environment:
Activate the Virtual Environment: First, you need to activate the virtual environment. Navigate to the virtual environment directory and activate it using the command line or terminal:
On Windows:
.\venv\Scripts\activate
Notes: 6

## Slide 16
Chapter
08
www.midocean.ae
Error : .\venv\Scripts\activate The system cannot find the path specified.
Solution:
cd path\to\my_project
1- Navigate to the Correct Directory
2- Verify the Path to the Virtual Environment
dir
If you don't see the venv folder, or if the Scripts directory is missing inside venv, the virtual environment was not created correctly.
Notes: 6

## Slide 17
Chapter
08
www.midocean.ae
3- Recreate the Virtual Environment (If Necessary)
If the virtual environment doesn't exist or was not created properly, you'll need to recreate it. Make sure you have Python installed, and then run:
python -m venv venv
This command creates a new virtual environment named venv in the current directory. After creation, try activating it again:
.\venv\Scripts\activate
Notes: 6

## Slide 18
Chapter
08
www.midocean.ae
4- Install scikit-learn
Once your virtual environment is activated, you can install scikit-learn as previously mentioned:
pip install scikit-learn
Notes: 6

## Slide 19
Chapter
08
www.midocean.ae
5- Verify Installation
To verify that scikit-learn has been successfully installed, you can run a small Python script to import scikit-learn and print its version:
First: Type python
Then use the following command
import sklearn
print(sklearn.__version__)
Exit the Python Interactive Shell
Notes: 6

## Slide 20
Chapter
08
www.midocean.ae
6- Use scikit-learn in Your Webots Project
Able to use scikit-learn in your Webots projects. You can import scikit-learn in your Python controller scripts and use its functionalities as needed.
Notes: 6

## Slide 21
Chapter
08
www.midocean.ae
2- Simulated Training Data
# Example training data: [avg_red, avg_green, avg_blue, action]
# Actions: 0 - Move Forward, 1 - Turn Right, 2 - Move Backward
training_data = [
[150, 30, 30, 1], # Red-like colors prompt turning right.
[30, 30, 150, 2], # Blue-like colors prompt moving backward.
[80, 80, 80, 0], # Neutral colors prompt moving forward.
# Add more samples as needed
]
For simplicity, let's simulate training data. In a real scenario, you'd collect data based on the robot's observations and corresponding actions.
Notes: 6

## Slide 22
Chapter
08
www.midocean.ae
Step 3: Train a Simple Decision Tree Classifier
from sklearn.tree import DecisionTreeClassifier
import numpy as np
# Prepare training data
X = np.array([x[:-1] for x in training_data]) # Color components
y = np.array([x[-1] for x in training_data]) # Actions
# Train the classifier
clf = DecisionTreeClassifier()
clf.fit(X, y)
Notes: 6

## Slide 23
Chapter
08
www.midocean.ae
Step 4: Integrate the Classifier into the Webots Code
# Main simulation loop with ML decision-making
while robot.step(TIME_STEP) != -1:
# Image processing to get the average color...
avg_red, avg_green, avg_blue = get_average_color(camera)
# Predict the action using the trained classifier
action = clf.predict([[avg_red, avg_green, avg_blue]])[0]
# Define robot movements based on the predicted action
if action == 0: # Move Forward
set_velocity(left_motor, right_motor, 5, 5)
elif action == 1: # Turn Right
set_velocity(left_motor, right_motor, 5, -5)
elif action == 2: # Move Backward
set_velocity(left_motor, right_motor, -5, -5)
Notes: 6

## Slide 24
Chapter
08
www.midocean.ae
Understanding Decision Trees
A decision tree is a flowchart-like tree structure where an internal node represents a feature(or attribute), the branch represents a decision rule, and each leaf node represents the outcome. In the context of our robot, the features are the average red, green, and blue (RGB) color values of a 3x3 pixel area in the camera's field of view, and the outcome is the action the robot should take (move forward, turn right, move backward).
Notes: 6

## Slide 25
Chapter
08
www.midocean.ae
Example 2 : Decision Tree Classifier
This example assumes that we have a pretrained decision tree model. The training of the model is conceptually described, but in practice, you would need to collect data, label it, and train the model using a tool like scikit-learn in a Python environment outside of Webots.
Notes: 6

## Slide 26
Chapter
08
www.midocean.ae
Step 1: Simulated Training Data and Model Training
First, you would collect data and train your model. This step is conceptual and would typically happen outside of your Webots project using scikit-learn or a similar library:
# Simulate training data collection
# Features: Average R, G, B values; Label: Action (0=Forward, 1=Right, 2=Backward)
training_data = [
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0], # Neutral colors mean move forward
]
# Normally, here you would split your data into features (X) and labels (y),
# train a decision tree model using scikit-learn, and then save the model.
# For this example, assume we have a trained model ready to use.
Notes: 6

## Slide 27
Chapter
08
www.midocean.ae
Step 2: Webots Code Integrating the Trained Model
Now, integrating the model into your Webots controller script. This part simulates loading a pretrained model and using it within the main robot control loop:
Notes: 6

## Slide 28
www.midocean.ae
from controller import Robot, Camera, Motor
import numpy as np
# Define the robot's actions based on prediction
def robot_action(action, left_motor, right_motor):
speed = 5
if action == 0: # Move forward
left_motor.setVelocity(speed)
right_motor.setVelocity(speed)
elif action == 1: # Turn right
left_motor.setVelocity(speed)
right_motor.setVelocity(-speed)
elif action == 2: # Move backward
left_motor.setVelocity(-speed)
right_motor.setVelocity(-speed)
# Main robot control code
TIME_STEP = 64
robot = Robot()
# Initialize camera
camera = robot.getDevice('camera')
camera.enable(TIME_STEP)
Chapter
08
Notes: 6

## Slide 29
www.midocean.ae
# Initialize motors
left_motor = robot.getDevice('left wheel motor')
right_motor = robot.getDevice('right wheel motor')
left_motor.setPosition(float('inf'))
right_motor.setPosition(float('inf'))
left_motor.setVelocity(0)
right_motor.setVelocity(0)
# Assume 'model' is our pretrained decision tree classifier
# For educational purposes, we will simulate its predictions based on color thresholds
while robot.step(TIME_STEP) != -1:
image = camera.getImage()
width = camera.getWidth()
height = camera.getHeight()
Chapter
08
Notes: 6

## Slide 30
www.midocean.ae
# Center coordinates of the image
centerX = width // 2
centerY = height // 2
# Calculate the average color of the central 3x3 pixels
avg_color = np.zeros(3)
for dx in range(-1, 2):
for dy in range(-1, 2):
# Correcting the method to get RGB components for each pixel
red = camera.imageGetRed(image, width, centerX + dx, centerY + dy)
green = camera.imageGetGreen(image, width, centerX + dx, centerY + dy)
blue = camera.imageGetBlue(image, width, centerX + dx, centerY + dy)
avg_color += np.array([red, green, blue])
avg_color /= 9 # Average RGB values
Chapter
08
Notes: 6

## Slide 31
www.midocean.ae
# Determine action based on average color
# Red detection
if avg_color[0] > 100 and avg_color[1] < 50 and avg_color[2] < 50:
action = 1 # Turn right due to red
# Green detection
elif avg_color[1] > 100 and avg_color[0] < 50 and avg_color[2] < 50:
action = 0 # Move forward due to green
else:
action = 2 # Move backward for any other color as default
# Execute the action
robot_action(action, left_motor, right_motor)
Chapter
08
Notes: 6

## Slide 32
Chapter
09
www.midocean.ae
Notes: 6

## Slide 33
Chapter
09
www.midocean.ae
To integrate the machine learning model training and prediction directly into a Webots controller script, you'll have to prepare a slightly different setup. This setup involves simulating the training data collection, training a decision tree model, and using the model for real-time decision-making based on the robot's camera input.
However, it's important to note that for a real-world scenario or more complex simulations, you'd likely perform the model training outside of the Webots environment due to the computational costs and then load the trained model into your Webots controller for predictions.
ML_Decissio-Tree_2
Notes: 6

## Slide 34
www.midocean.ae
Step 1: Setting Up Your Environment
from controller import Robot
from sklearn.tree import DecisionTreeClassifier
import numpy as np
robot = Robot()
timestep = int(robot.getBasicTimeStep())
NOTE: You're importing necessary libraries (Robot class from Webots, DecisionTreeClassifier from scikit-learn, and numpy) and initializing your robot. The timestep variable stores the simulation timestep, which is essential for synchronizing your control commands with the simulation.
Chapter
09
Notes: 6

## Slide 35
www.midocean.ae
Step 2: Initializing Devices
camera = robot.getDevice('camera')
camera.enable(timestep)
left_motor = robot.getDevice('left wheel motor')
right_motor = robot.getDevice('right wheel motor')
left_motor.setPosition(float('inf'))
right_motor.setPosition(float('inf'))
left_motor.setVelocity(0)
right_motor.setVelocity(0)
NOTE: You initialize the camera and motors attached to your robot. Setting the motor position to infinity (float('inf')) switches the motors to velocity control mode. Initially, the robot's motors are set to 0 speed, meaning the robot will not move.
Chapter
09
Notes: 6

## Slide 36
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
Step 3: Preparing Training Data for the Decision Tree
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
NOTE: This block creates an array of training data, where each row represents a different scenario. The first three numbers in each row are RGB values simulating the color the robot sees, and the fourth number is the action the robot should take (0 for forward, 1 for right, 2 for backward). This data is split into features (X_train) and labels (y_train).
Chapter
09
Notes: 6

## Slide 37
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
Step 4: Training the Decision Tree Classifier
clf = DecisionTreeClassifier()
clf.fit(X_train, y_train)
NOTE: A decision tree classifier is initialized and trained with the RGB values as features and the corresponding actions as labels. The .fit() method adjusts the model parameters to best fit the training data.
Chapter
09
Notes: 6

## Slide 38
3] # Actions
www.midocean.ae
Step 5: Defining the Action Function
def perform_action(action, left_motor, right_motor):
# This function translates the predicted action into motor commands.
NOTE: This function maps the predicted action to actual motor speeds, controlling the robot's movement. Depending on the action, both motors may move forward, rotate in opposite directions (to turn), or both move backward.
Chapter
09
Notes: 6

## Slide 39
3] # Actions
www.midocean.ae
Step 6: Main Control Loop
while robot.step(timestep) != -1:
current_rgb = np.array([[85, 90, 75]]) # Simulated current color
predicted_action = clf.predict(current_rgb)[0]
perform_action(predicted_action, left_motor, right_motor)
NOTE: Within an infinite loop that runs for the simulation's duration, you simulate getting RGB values from the camera and use your trained model to predict the appropriate action. The action is then performed by adjusting the motors' velocities.
Chapter
09
Notes: 6

## Slide 40
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
Simulate Color Detection: For demonstration purposes, current_rgb is a placeholder for RGB values you might get from processing the camera's image.
Predict Action: The model predicts the best action (move forward, turn right, move backward) based on the current RGB values.
Execute Action: The predicted action is translated into motor movements, controlling the robot's behavior in the simulation.
This example demonstrates a basic application of machine learning within a robotics simulation. By training a decision tree to associate colors with movements, you've created a model that can guide a robot's navigation based on visual cues. While simplified, this process lays the foundation for more complex applications involving real-time data processing and decision-making in robotic systems.
Conclusion
Chapter
09
Notes: 6

## Slide 41
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
ML_Decission-Tree_3
Chapter
09
Notes: 6

## Slide 42
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
ML_Decission-Tree_3
"""ML_DecissionTree_3 controller."""
# Dr. Khaled Eskaf
#Using ML Decision Tree 3
from controller import Robot
import numpy as np
from sklearn.tree import DecisionTreeClassifier
# Initialize the robot and simulation timestep
robot = Robot()
timestep = int(robot.getBasicTimeStep())
# Initialize camera and motors
camera = robot.getDevice('camera')
camera.enable(timestep)
left_motor = robot.getDevice('left wheel motor')
right_motor = robot.getDevice('right wheel motor')
left_motor.setPosition(float('inf')) # Enable speed control mode
right_motor.setPosition(float('inf'))
left_motor.setVelocity(0) # Initially stop the robot
right_motor.setVelocity(0)
Chapter
09
Notes: 6

## Slide 43
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
ML_Decission-Tree_3
# Simulated training data for decision making
training_data = np.array([
[120, 40, 40, 1], # Red-ish object
[40, 40, 120, 2], # Blue-ish object
[80, 110, 90, 0] # Neutral object
])
# Split training data into features and labels
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
# Train the decision tree classifier
clf = DecisionTreeClassifier()
clf.fit(X_train, y_train)
# Main control loop
while robot.step(timestep) != -1:
image = camera.getImage()
width = camera.getWidth()
height = camera.getHeight()
Chapter
09
Notes: 6

## Slide 44
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
ML_Decission-Tree_3
# Calculate center pixel coordinates
centerX = width // 2
centerY = height // 2
# Initialize sum of RGB values
sum_rgb = np.zeros(3)
# Iterate over a 3x3 matrix around the central pixel
for dx in range(-1, 2):
for dy in range(-1, 2):
index = ((centerY + dy) * width + (centerX + dx)) * 4
r = image[index]
g = image[index + 1]
b = image[index + 2]
sum_rgb += np.array([r, g, b])
print(f"RGB at ({centerX+dx}, {centerY+dy}): ({r}, {g}, {b})") # Print RGB values of each pixel
# Calculate average RGB values
avg_rgb = sum_rgb / 9
print(f"Average RGB: {avg_rgb}") # Print the average RGB values
Chapter
09
Notes: 6

## Slide 45
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
ML_Decission-Tree_3
# Predict the action based on the current RGB values
predicted_action = clf.predict([avg_rgb])[0]
# Set motor speeds based on the predicted action
speed = 5
if predicted_action == 0: # Move forward
left_motor.setVelocity(speed)
right_motor.setVelocity(speed)
elif predicted_action == 1: # Turn right
left_motor.setVelocity(speed)
right_motor.setVelocity(-speed)
elif predicted_action == 2: # Move backward
left_motor.setVelocity(-speed)
right_motor.setVelocity(-speed)
Chapter
09
Notes: 6

## Slide 46
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
Initializes a simulated robot in Webots, equipping it with a camera and motors for navigation.
Sets up training data linking specific RGB values to actions (forward, right, backward) using a decision tree classifier.
Trains the classifier on this data, enabling the robot to make decisions based on color detected by the camera.
During operation, captures real-time camera images, extracting average RGB values from a central 3x3 pixel matrix.
Uses the trained model to predict actions based on these RGB values, guiding the robot's movement.
Demonstrates basic machine learning application in robotics for environment-responsive navigation based on visual cues.
# ML_Decision Tree _4
Chapter
09
Notes: 6

## Slide 47
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
Import Libraries:
  Robot from Webots allows you to control the simulated robot.
  numpy is used for handling arrays efficiently.
  DecisionTreeClassifier from scikit-learn is the machine learning model the robot will use to make decisions.
Initialize the Robot and Simulation Timestep:
  Create a Robot instance to interact with the simulation.
  timestep determines how often the robot's sensors are updated and actions are taken.
Set Up Camera and Motors:
  Access the camera and motors by their names, then enable the camera and set the motors to velocity control mode by assigning their positions to infinity. Initially, the motors are stopped.
Prepare Training Data:
  The training data simulates situations where different RGB color values are associated with specific actions (e.g., moving forward, turning, or moving backward). This data is represented in an array where each row contains RGB values followed by an action label.
Chapter
09
Notes: 6

## Slide 48
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
5) Train the Decision Tree Classifier:
  The features (RGB values) and labels (actions) are extracted from the training data. The decision tree classifier is then trained on these features and labels, learning to associate specific color patterns with actions.
6) Main Control Loop:
  In an infinite loop, the robot continually captures images from its camera, calculates the average RGB values from a central 3x3 matrix, and uses the trained classifier to predict an action based on these values.
7) Calculate Average RGB Values:
  For each pixel in the 3x3 matrix centered around the camera's focal point, extract the RGB values, sum them, and then divide by 9 to get the average RGB values. This step involves iterating over the pixels, extracting their color, and accumulating the values.
Chapter
09
Notes: 6

## Slide 49
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
8) Predict and Perform Actions:
The average RGB values are fed into the trained classifier, which predicts the most appropriate action (move forward, turn right, or move backward). The predicted action is then translated into motor velocities to move the robot accordingly.
9) Print Statements:
Throughout the process, print statements output the RGB values of each pixel in the 3x3 matrix and the overall average RGB values. This helps in understanding how the robot perceives its environment and decides on its actions.
Chapter
09
Notes: 6

## Slide 50
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
# Import necessary libraries:
# - Robot: to control the simulated robot in Webots.
# - numpy: for efficient array operations, crucial for handling data.
# - DecisionTreeClassifier: a simple machine learning model from scikit-learn.
from controller import Robot
import numpy as np
from sklearn.tree import DecisionTreeClassifier
# Create an instance of the Robot class to interact with the simulation.
robot = Robot()
# Get the basic time step of the current world, which determines
# how often the simulation updates the robot's sensors and actuators.
timestep = int(robot.getBasicTimeStep())
# Access the camera and motor devices by their names in the robot's definition.
# Then, enable the camera to start capturing images at the simulation's timestep.
camera = robot.getDevice('camera')
camera.enable(timestep)
Chapter
09
Notes: 6

## Slide 51
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
# For the motors, set their positions to infinity, which switches them
# to velocity control mode, allowing us to specify speed rather than position.
left_motor = robot.getDevice('left wheel motor')
right_motor = robot.getDevice('right wheel motor')
left_motor.setPosition(float('inf'))
right_motor.setPosition(float('inf'))
# Initially, stop the robot by setting both motors' speeds to 0.
left_motor.setVelocity(0)
right_motor.setVelocity(0)
# Define the training data for the decision tree classifier.
# This data simulates scenarios where certain RGB color values of objects
# seen by the robot are associated with specific actions (turning or moving).
training_data = np.array([
[120, 40, 40, 1], # Red objects make the robot turn right.
[40, 40, 120, 2], # Blue objects make the robot move backward.
[80, 110, 90, 0] # Neutral (less distinctly colored) objects make the robot move forward.
])
Chapter
09
Notes: 6

## Slide 52
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
# Split the training data into features (X) and labels (y).
# Features are the RGB values, and labels are the actions.
X_train = training_data[:, :3] # Extract the first three columns as features.
y_train = training_data[:, 3] # Extract the last column as labels.
# Initialize the decision tree classifier and train (fit) it on the provided data.
clf = DecisionTreeClassifier()
clf.fit(X_train, y_train)
# The main control loop of the robot.
while robot.step(timestep) != -1:
# Retrieve the current image captured by the camera.
image = camera.getImage()
# Get the width and height of the camera image to calculate the center pixel.
width = camera.getWidth()
height = camera.getHeight()
# Calculate the coordinates of the center pixel.
centerX = width // 2
centerY = height // 2
Chapter
09
Notes: 6

## Slide 53
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
# Prepare to calculate the average RGB values of the 3x3 area around the center pixel.
sum_rgb = np.zeros(3) # Initialize a sum for RGB values.
# Loop over the pixels in a 3x3 area around the center.
for dx in range(-1, 2):
for dy in range(-1, 2):
# Calculate the index for each pixel in the flattened image array.
index = ((centerY + dy) * width + (centerX + dx)) * 4
# Extract the RGB values of each pixel and add them to the sum.
r = image[index]
g = image[index + 1]
b = image[index + 2]
sum_rgb += np.array([r, g, b])
# Print the RGB values for educational purposes.
print(f"RGB at ({centerX+dx}, {centerY+dy}): ({r}, {g}, {b})")
Chapter
09
Notes: 6

## Slide 54
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
# Calculate the average RGB values by dividing the sum by the number of pixels (9).
avg_rgb = sum_rgb / 9
# Print the average RGB values for insight into the decision-making process.
print(f"Average RGB: {avg_rgb}")
# Use the trained classifier to predict the action based on the average RGB values.
predicted_action = clf.predict([avg_rgb])[0]
# Based on the predicted action, set the speeds of the motors to move the robot.
speed = 5 # Define a base speed.
if predicted_action == 0: # If the action is to move forward.
left_motor.setVelocity(speed)
right_motor.setVelocity(speed)
elif predicted_action == 1: # If the action is to turn right.
left_motor.setVelocity(speed)
Chapter
09
Notes: 6

## Slide 55
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
# If the action is to turn right, the left motor moves forward and the right motor moves backward.
left_motor.setVelocity(speed)
right_motor.setVelocity(-speed)
elif predicted_action == 2: # If the action is to move backward.
# If the action is to move backward, both motors move in reverse.
left_motor.setVelocity(-speed)
right_motor.setVelocity(-speed)
Chapter
09
Notes: 6

## Slide 56
training_data = np.array([
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0] # Neutral colors mean move forward
])
X_train = training_data[:, :3] # RGB values
y_train = training_data[:, 3] # Actions
www.midocean.ae
Chapter
09
Notes: 6

## Slide 57
Chapter
09
www.midocean.ae
Integrations between robotics and AI are shaping the future of numerous industries, transforming how tasks are performed, from manufacturing and healthcare to agriculture and domestic chores. This synergy enhances the capabilities of robots, allowing them to operate more autonomously, make decisions in real-time, and adapt to new or changing environments without human intervention.
Notes: تعمل عمليات التكامل بين الروبوتات والذكاء الاصطناعي على تشكيل مستقبل العديد من الصناعات، وتغيير كيفية أداء المهام، بدءًا من التصنيع والرعاية الصحية وحتى الزراعة والأعمال المنزلية. ويعزز هذا التآزر قدرات الروبوتات، مما يسمح لها بالعمل بشكل أكثر استقلالية، واتخاذ القرارات في الوقت الفعلي، والتكيف مع البيئات الجديدة أو المتغيرة دون تدخل بشري.

## Slide 58
Chapter
09
www.midocean.ae
1. Manufacturing Automation
In the manufacturing sector, AI-enhanced robots are being used for a variety of tasks including assembly, painting, and quality control. AI algorithms can analyze data from the manufacturing process in real-time, enabling robots to identify and correct errors, optimize production processes, and predict maintenance needs.
Notes: أتمتة التصنيع:وفي قطاع التصنيع، يتم استخدام الروبوتات المعززة بالذكاء الاصطناعي في مجموعة متنوعة من المهام بما في ذلك التجميع والطلاء ومراقبة الجودة. يمكن لخوارزميات الذكاء الاصطناعي تحليل البيانات من عملية التصنيع في الوقت الفعلي، مما يمكّن الروبوتات من تحديد الأخطاء وتصحيحها، وتحسين عمليات الإنتاج، والتنبؤ باحتياجات الصيانة.

## Slide 59
Chapter
09
www.midocean.ae
2. Healthcare and Surgery
Robots equipped with AI are revolutionizing the healthcare industry by assisting in surgeries with precision beyond human capability, managing patient care, and even providing companionship. These robots can learn from data collected during medical procedures, improving their performance over time.
Notes: الرعاية الصحية والجراحة
تُحدث الروبوتات المجهزة بالذكاء الاصطناعي ثورة في صناعة الرعاية الصحية من خلال المساعدة في العمليات الجراحية بدقة تفوق القدرة البشرية، وإدارة رعاية المرضى، وحتى توفير الرفقة. يمكن لهذه الروبوتات أن تتعلم من البيانات التي تم جمعها أثناء الإجراءات الطبية، مما يحسن أدائها بمرور الوقت.

## Slide 60
Chapter
09
www.midocean.ae
3. Agriculture
AI-driven robotic systems are being deployed in agriculture for tasks such as planting seeds, harvesting crops, and monitoring field conditions. These robots can analyze data from various sensors and satellite images to optimize crop yield and reduce waste.
Notes: 3. الزراعة
يتم نشر الأنظمة الآلية التي تعتمد على الذكاء الاصطناعي في الزراعة للقيام بمهام مثل زراعة البذور، وحصاد المحاصيل، ومراقبة الظروف الميدانية. يمكن لهذه الروبوتات تحليل البيانات من أجهزة الاستشعار المختلفة وصور الأقمار الصناعية لتحسين إنتاجية المحاصيل وتقليل النفايات.

## Slide 61
Chapter
09
www.midocean.ae
4. Search and Rescue Operations
Robots, combined with AI, play a crucial role in search and rescue missions, especially in environments that are dangerous or inaccessible to humans. They can navigate through rubble, identify victims using heat sensors, and assess structures' stability.
Notes: 4. عمليات البحث والإنقاذ
تلعب الروبوتات، جنبًا إلى جنب مع الذكاء الاصطناعي، دورًا حاسمًا في مهام البحث والإنقاذ، خاصة في البيئات الخطرة أو التي يتعذر على البشر الوصول إليها. يمكنهم التنقل عبر الأنقاض، وتحديد الضحايا باستخدام أجهزة استشعار الحرارة، وتقييم استقرار الهياكل.

## Slide 62
Chapter
09
www.midocean.ae
5. Domestic Robots
In the domestic sphere, robotic vacuum cleaners and lawn mowers are becoming smarter through AI, learning the layout of homes and gardens to optimize their cleaning paths. Future developments may lead to more complex domestic robots capable of performing a wide range of household tasks.
Notes: 6

## Slide 63
Chapter
09
www.midocean.ae
6. Autonomous Vehicles
Autonomous vehicles, essentially robots on wheels, rely heavily on AI for navigating and making decisions on the road. This integration is crucial for interpreting sensor data, predicting the actions of other road users, and choosing the safest course of action.
Notes: 6. المركبات ذاتية القيادة
تعتمد المركبات ذاتية القيادة، وهي في الأساس روبوتات على عجلات، بشكل كبير على الذكاء الاصطناعي للتنقل واتخاذ القرارات على الطريق. يعد هذا التكامل أمرًا بالغ الأهمية لتفسير بيانات المستشعر، والتنبؤ بتصرفات مستخدمي الطريق الآخرين، واختيار مسار العمل الأكثر أمانًا.

## Slide 64
Chapter
09
www.midocean.ae
7. Logistics and Supply Chain
AI-powered robots are streamlining logistics and supply chain operations by automating warehousing tasks, such as sorting, packing, and shipping goods. These robots can adapt to changes in inventory levels or demand patterns, improving efficiency and reducing operational costs.
Notes: 7. الخدمات اللوجستية وسلسلة التوريد
تعمل الروبوتات التي تعمل بالذكاء الاصطناعي على تبسيط العمليات اللوجستية وسلسلة التوريد من خلال أتمتة مهام التخزين، مثل فرز البضائع وتعبئتها وشحنها. يمكن لهذه الروبوتات التكيف مع التغيرات في مستويات المخزون أو أنماط الطلب، مما يحسن الكفاءة ويقلل تكاليف التشغيل.

## Slide 65
Thank You