## Slide 1
AI-Based Nowcasting of National CO₂ Emissions
Using Satellite-Derived Indicators
A Hybrid Framework for GCC Countries
Master's Thesis in Artificial Intelligence
Satellite-Based Nowcasting for Climate Monitoring
Mohammad Wajeeh Bader
Supervisor: Dr. Amjad

## Slide 2
The Problem
1,158 Mt
GCC CO₂ Emissions (2023)
3.1%
of Global Emissions
58.8M
Population Affected
CRITICAL CHALLENGE
The GCC region lacks real-time, granular carbon monitoring systems despite being one of the world's highest per-capita emitters.
KEY GAPS
Annual reporting delays of 1-2 years
No integration of satellite-based environmental indicators
Limited regional ML-based forecasting studies
Vision 2030 requires actionable environmental intelligence

## Slide 3
Research Gap: This Study's Position

## Slide 4
Research Objectives
PRIMARY OBJECTIVE
Develop an AI-enhanced framework for nowcasting CO₂ emissions in Saudi Arabia and the GCC region using satellite data integration.
BASELINE
Establish temporal baseline using XGBoost with 24 years of emissions data (2000-2023)
Target: R² ≥ 0.70
INTEGRATE
Integrate satellite-derived features from Google Earth Engine (LST, NDVI, Nightlights)
Target: Quantify accuracy-timeliness trade-off
VALIDATE
Evaluate model performance at country level across all six GCC nations
Target: MAPE < 15%

## Slide 5
Literature Review
EXISTING RESEARCH (20+ STUDIES REVIEWED)
AI/ML-Based Forecasting
LSTM networks for time-series prediction
XGBoost for feature-based modeling
Ensemble methods achieving R² 0.85-0.95
Satellite-Based Monitoring
OCO-2/3 for direct CO₂ measurement
MODIS LST as emission proxy
Nightlights for urbanization tracking
Regional Studies
China, EU, USA dominant focus
Limited GCC-specific research
IDENTIFIED RESEARCH GAP
No existing study combines temporal ML forecasting with satellite-derived features specifically for the GCC region.
Most studies focus on single data sources
GCC's unique climate patterns ignored
Multi-country regional models rare
Oil economy factors underexplored
THIS RESEARCH ADDRESSES
First integrated framework combining XGBoost temporal modeling with GEE satellite features for GCC-wide emissions monitoring.

## Slide 6
Literature Review

## Slide 7
Study Area: GCC Region
TOTAL EMISSIONS
1,158 Mt CO₂
POPULATION
58.8M
Saudi Arabia
672 Mt
58% of GCC | 18.2 t/capita
UAE
190 Mt
16% of GCC | 19.3 t/capita
Qatar
99 Mt
8.5% of GCC | 32.8 t/capita
Kuwait
95 Mt
8.2% of GCC | 21.6 t/capita
Oman
64 Mt
5.5% of GCC | 12.4 t/capita
Bahrain
38 Mt
3.3% of GCC | 23.1 t/capita
GEOGRAPHIC COVERAGE

## Slide 8
GCC Emissions Distribution

## Slide 9
Data Sources
SOCIOECONOMIC DATA
Our World in Data
CO₂ Emissions
Per Capita Emissions
Energy Consumption
Primary Energy Mix
World Bank API
GDP (current USD)
Population
Urban Population %
Industry Value Added
Final panel used in this thesis: 144 country–year observations (6 GCC countries × 24 years, 2000–2023), combining OWID / World Bank socioeconomic indicators with satellite features from MODIS (LST, NDVI), VIIRS night lights, MERRA-2 AOD, and Sentinel-5P NO₂.
100%
Data Completeness
144
Country-Years
SATELLITE DATA (Google Earth Engine)
MODIS Land Surface Temperature
MOD11A2 | 8-day composites | Day/Night LST | Emissivity
MODIS Vegetation Index
MOD13A2 | 16-day composites | NDVI | EVI
VIIRS Nighttime Lights
VIIRS DNB Monthly | Annual composites | Radiance | Lit Area
Sentinel-5P TROPOMI
NO₂ Column Density | (2018+)

## Slide 10
Satellite Data Sources & Pipeline

## Slide 11
Feature Correlation Analysis

## Slide 12
Research Framework
DATA COLLECTION
Our World in Data
World Bank API
Google Earth Engine
PREPROCESSING
Missing data handling
Temporal alignment
Feature scaling
FEATURE ENG.
Feature engineering
seasonal aggregation
derived features
MODELING
XGBoost Regressor
3-Model comparison
Temporal split
EVALUATION
R², RMSE, MAPE
Feature importance
Country-level analysis
Model A
Socioeconomic Only
GDP, Population, Energy, CO₂ Intensity
(5 features)
Model B
Satellite + Population
LST, NDVI, Nightlights, AOD + Population Density
(6 features)
Model C
Satellite Only
LST (Summer/Winter), NDVI, Nightlights, AOD )NO₂
(5 features)

## Slide 13
Research Methodology: 4 Phases

## Slide 14
Google Earth Engine Workflow

## Slide 15
XGBoost: Gradient Boosting

## Slide 16
Temporal Validation Strategy

## Slide 17
Results: Model Performance
MODEL A
Socioeconomic Only
0.96
Test R²
46.3
RMSE (Mt)
8.7%
MAPE
MODEL B
Satellite + Population
0.69
Test R²
124.2
RMSE (Mt)
18.3%
MAPE
MODEL C
Satellite Only
0.67
Test R²
129.1
RMSE (Mt)
19.8%
MAPE
TRADE-OFF
Trade-off
Accuracy cost for near-real-time data
Model B trades accuracy for near-real-time data availability (days vs years)
OVERFITTING CHECK
Train R²
0.96
Test R²
0.69
Gap
27%
Moderate train–test gap indicates some overfitting; the model still generalizes reasonably but requires cautious interpretation.
TARGET ACHIEVEMENT
R² ≥ 0.70 near target (0.69)
MAPE < 15% 18.3% (not met)
Satellite improvement Trade-off

## Slide 18
Key Finding: Accuracy vs Timeliness

## Slide 19
Feature Importance Analysis
MODEL B FEATURES
LST Summer (34%)
LST Winter (22%)
Night Lights (22%)
NDVI (5%)
AOD (4%)
Pop. Density 13%
Pop. Density (13%)
Other
FEATURE CONTRIBUTION
56%
Temperature (LST)
44%
Other Features
KEY INSIGHT
Temperature features (LST Summer + Winter) account for 56% of predictive power, reflecting cooling demand as primary emission driver in GCC.
SATELLITE VALUE
LST Summer is the most important feature, capturing seasonal energy demand patterns.
IMPLICATION
Satellite features enable near-real-time emissions estimation with R²=0.69, trading some accuracy for immediate data availability.

## Slide 20
Country-Level Performance
Saudi Arabia
0.72
R²
68.4 Mt
RMSE
UAE
0.68
R²
28.3 Mt
RMSE
Qatar
0.65
R²
18.2 Mt
RMSE
Kuwait
0.67
R²
14.1 Mt
RMSE
Oman
0.64
R²
12.8 Mt
RMSE
Bahrain
0.61
R²
8.4 Mt
RMSE
PATTERN OBSERVED
Larger economies (SA, UAE) show better predictions due to more stable emission patterns and data availability.
SMALLER COUNTRIES
Bahrain and Oman show higher variability - may benefit from country-specific models.

## Slide 21
Limitations & Future Work
LIMITATIONS
Data Temporal Coverage
Satellite data limited to 2000-2023; Sentinel-5P only from 2018
Annual Resolution
Country-level annual data; cannot capture sub-annual or regional variations
Sample Size
144 observations across 6 countries may limit complex model training
Model Scope
XGBoost only; deep learning methods not explored
FUTURE DIRECTIONS
Higher Resolution Modeling
City-level or grid-based predictions using downscaling techniques
Deep Learning Integration
LSTM, Transformer models for temporal sequence learning
Real-time Dashboard
Web-based monitoring system with automated GEE data pipeline
Sectoral Disaggregation
Industry, transport, residential emission breakdowns

## Slide 22
Future Research Directions

## Slide 23
Conclusions
This research demonstrates that using satellite-derived features with population density enables near-real-time CO₂ emission estimation for the GCC region, achieving R² ≈ 0.69 and supporting Vision 2030 environmental monitoring goals.
NOVEL FRAMEWORK
First integrated AI framework combining XGBoost temporal modeling with Google Earth Engine satellite data for GCC emissions monitoring.
SATELLITE VALUE
Quantified satellite contribution: Temperature (summer and winter LST) and Nighttime Lights together account for ~78% of the model’s feature importance in Model B.
REGIONAL INSIGHTS
Country-level analysis reveals performance patterns: larger economies (Saudi Arabia R²=0.72) benefit most from integrated approach.
PRACTICAL IMPACT
Framework can reduce emission reporting delays from 1-2 years to near real-time estimates.
POLICY RELEVANCE
Supports Saudi Vision 2030 and GCC climate commitments with actionable environmental intelligence.

## Slide 24
Thank You
Questions & Discussion
Mohammad Wajeeh Bader
Master's Student in Artificial Intelligence
Midocean University
251000462@st.midocean.edu.km
Supervisor: Dr. Amjad Qtaish
AI-Based Nowcasting of National CO₂ Emissions
A Hybrid Framework for GCC Countries