## Slide 1
Prepared by Dr. Ehab Mahmoud
Project Quality Management

## Slide 2
Project Quality Management
Lecture 5
PMG354
Statistical Quality Control – part 2
Dr. Ehab Mahmoud
Prepared by

## Slide 3
At the end of this lecture, we expect to acquire a knowledge about fundamentals for statistical quality control to use in project stages and assure the conformity od outcomes
Objectives
Lecture
05

## Slide 4
Contents
What if the Process is Out of Control Basic Tools of Quality?
Revised Control Limits for X and R
Example
Control Charts for variables (XmR)
Attribute Control Charts
Types of Attribute Control Chart
Control Chart for Nonconformities (Defects) (c)
Example
Control Chart for Average Number of Nonconformities per Unit (U)
Example
Lecture
05

## Slide 5: What if the Process is Out of Control
If points plot out of control, then the control limits must be revised.
Before revising, identify out of control points and look for assignable causes.
  If assignable causes can be found, then discard the point(s) and recalculate the control limits.
  If no assignable causes can be found then retain the point(s) considering the trial control limits as appropriate for current control.

## Slide 6: Revised Control Limits for X and R
Revised center line for x and R control charts

## Slide 7: Revised Control Limits for X and R
Where d2 is a factor from the table.

## Slide 8: Revised Control Limits for X and R
Where A, D1 and D2 are factors from the table corresponding to subgroup size n.

## Slide 9: Example
The following data represent the depth of keyway taken in millimeters. We wish to establish statistical control of the process using x and R charts. Twenty five samples, each of size 4, have been taken when we think the process is in control.
  The depth of keyway measurements data from these samples are shown in the next table.

## Slide 10: Example
Sample Number | Date | Time | Measurements |  |  |  | Average | Range | Comment
 |  |  | x1 | x2 | x3 | x4 |  | Ri | 
1 | 23/12 | 8:50 | 6.35 | 6.40 | 6.32 | 6.37 | 6.36 | 0.08 | 
2 |  | 11:30 | 6.46 | 6.37 | 6.36 | 6.41 | 6.40 | 0.01 | 
3 |  | 1:45 | 6.34 | 6.40 | 6.34 | 6.36 | 6.36 | 0.06 | 
4 |  | 3:45 | 6.69 | 6.64 | 6.68 | 6.59 | 6.65 | 0.10 | New, temporary operator
5 |  | 4:20 | 6.38 | 6.34 | 6.44 | 6.40 | 6.39 | 0.10 | 
6 | 27/12 | 8:35 | 6.42 | 6.41 | 6.43 | 6.34 | 6.40 | 0.09 | 
7 |  | 9:00 | 6.44 | 6.41 | 6.41 | 6.46 | 6.43 | 0.05 | 
8 |  | 9:40 | 6.33 | 6.41 | 6.38 | 6.36 | 6.37 | 0.08 | 
9 |  | 1:30 | 6.48 | 6.44 | 6.47 | 6.45 | 6.46 | 0.04 | 
… |  |  |  |  |  |  |  |  | 
24 |  | 2:00 | 6.43 | 6.43 | 6.35 | 6.38 | 6.38 | 0.08 | 
25 |  | 4:25 | 6.39 | 6.39 | 6.43 | 6.44 | 6.41 | 0.06 | 
Sum |  |  |  |  |  |  | 160.25 | 2.19 | 

## Slide 11: Example
Since the R chart indicates that the process variability is out of control, we may revise the chart.
Also, the chart is out of control, and need revision.
R chart has to be revised first, and then chart

## Slide 12: Example
Test Results for X-bar Chart of X1, ..., X4
TEST 1. One point more than 3.00 standard deviations from center line.
Test Failed at points: 4, 16, 20
  Sample 4 : Assignable cause; New temporary operator
  Sample 16: Random Cause
  Sample 20: Assignable cause; Bad material
Test Results for R Chart of X1, ..., X4
TEST 1. One point more than 3.00 standard deviations from center line.
Test Failed at points: 18
  Sample 18: Assignable cause; Damage oil line

## Slide 13: Example
The revised center line is
The value of d2, for sample of size n = 4 and using the table equal
  d2 =2.059

## Slide 14: Example
Therefore, the Revised control limits for the R chart are

## Slide 15: Example
Now, the R chart is in control at the stated level. i.e the variability of the process is within control.
We can revise the chart, to control the process center.

## Slide 16: Example
The revised center line is
The value of d2, for sample of size n = 4 and using the table equal
  d2 =2.059

## Slide 17: Example
Therefore, the Revised control limits for the x chart are

## Slide 18: Example
The chart is now in control at the stated level; center line and control limits.
Note that subgroup 9 is out of control. The cause responsible for this signal should be treated as random cause.

## Slide 19: Control Charts for variables (XmR)
The Shewhart Control Chart for Individual Measurements
What if you could not get a sample size greater than 1 (n =1)? Examples include
  Automated inspection and measurement technology is used, and every unit manufactured is analyzed.
  The production rate is very slow, and it is inconvenient to allow samples sizes of n > 1 to accumulate before analysis
  Repeated measurements on the process differ only because of laboratory or analysis error, as in many chemical processes.

## Slide 20: Control Charts for variables (XmR)
  Multiple measurement are taken on the same unit of product, such as measuring oxide thickness at several locations on a wafer in semiconductor manufacturing.
  In process plants, such as papermaking, measurements on some parameter such as coating thickness across the roll will differ very little and produce a standard deviation that is much too small if the objective is to control coating thickness along the roll.
  Periodic (Weekly, Monthly) administrative data
The X and MR charts are useful for samples of sizes n = 1.

## Slide 21: Control Charts for variables (XmR)
The moving range (MR) is defined as the absolute difference between two successive observations:
MRi = |xi - xi-1|
which will indicate possible shifts or changes in the process from one observation to the next.

## Slide 22: Control Charts for variables (XmR)
The X chart is the plot of the individual observations. The control limits are
where

## Slide 23: Control Charts for variables (XmR)
The control limits on the moving range chart are:

## Slide 24: Example
The viscosity of an aircraft primer paint is an important quality characteristic.
The product is produced in batches, and because each batch takes several hours to produce, the production rate is too slow to allow samples sizes greater than 1.
The viscosity of the previous 15 batches are shown in the table in the next slide.
Set up a control chart for this situation.

## Slide 25: Example
Batch number | Viscosity, x | Moving Range MR
1 | 33.75 | 
2 | 33.05 | 0.70
3 | 34.00 | 0.95
4 | 33.81 | 0.19
5 | 33.46 | 0.35
6 | 34.02 | 0.56
7 | 33.68 | 0.34
8 | 33.27 | 0.41
9 | 33.49 | 0.22
10 | 33.20 | 0.29
11 | 33.62 | 0.42
12 | 33.00 | 0.62
13 | 33.54 | 0.54
14 | 33.12 | 0.42
15 | 33.84 | 0.72

## Slide 26: Example
Using the data from the previous table, we find that the center line for the MR chart is
For samples of n = 1, and using the table we have
  D3 = 0
  D4 = 3.267

## Slide 27: Example
The trial control limits for the MR chart are

## Slide 28: Example
Here, no points exceed the upper control limits, we can consider that the process is in control

## Slide 29: Example
For the control chart of individual measurement, the parameters are
If a moving range of n=1 observations is used, then
  d2 = 1.128

## Slide 30: Example
There is no indication of an out of control condition.

## Slide 31: Example
X Charts can be interpreted similar to MR charts. MR charts cannot be interpreted the same as X or R charts.
Since the MR chart plots data that are “correlated” with one another, then looking for patterns on the chart does not make sense.
More emphasis should be placed on interpretation of the X chart.

## Slide 32: Example
Batch number | Viscosity, x | Moving Range MR
16 | 33.50 | 0.34
17 | 33.25 | 0.25
18 | 33.40 | 0.15
19 | 33.27 | 0.13
20 | 34.65 | 1.38
21 | 34.80 | 0.15
22 | 34.55 | 0.25
23 | 35.00 | 0.45
24 | 34.75 | 0.25
25 | 34.50 | 0.25
26 | 34.70 | 0.20
27 | 34.29 | 0.41
28 | 34.61 | 0.32
29 | 34.49 | 0.12
30 | 35.03 | 0.54

## Slide 33: Example

## Slide 34: Example
Interpretation of the chart, an upward shift in mean viscosity has occurred around batch 20 or 21, Since there is an obvious “shift in process level” pattern on the chart for individual.
Note that the moving range chart also reacts to this level shift with a single large spike at sample 20.
This spike on the moving range chart sometimes helpful in identifying exactly where a process shift in the mean has occurred.

## Slide 35: Example

## Slide 36: Attribute Control Charts
Data that can be classified into one of several categories or classifications is known as attribute data.
Classifications such as conforming and nonconforming are commonly used in quality control.
Another example of attributes data is the count of defects.

## Slide 37: Types of Attribute Control Chart
Charts for nonconformities (based on the Poisson distribution).
  C chart (Number of defects or nonconformities) - in case of the sample contains one unit for inspection
  U chart (Nonconformities per unit) – in case the sample contains more than one inspection unit.

## Slide 38: Control Chart for Nonconformities (Defects) (c)
Standard Given:
No Standard Given:

## Slide 39: Example
The data in the following table presents the number of nonconformities observed in 26 successive samples of 100 printed circuit boards.
For reason of convenience, each sample represent one inspection unit. The inspection unit is defined as 100 boards.
Set up a c chart to test whether the process exhibit control.

## Slide 40: Example
Sample Number | Number of Nonconformities | Sample Number | Number of Nonconformities | Sample Number | Number of Nonconformities
1 | 21 | 12 | 24 | 23 | 16
2 | 24 | 13 | 16 | 24 | 19
3 | 16 | 14 | 19 | 25 | 17
4 | 12 | 15 | 10 | 26 | 15
5 | 15 | 16 | 17 | Sum | 516
6 | 5 | 17 | 13 |  | 
7 | 28 | 18 | 22 |  | 
8 | 20 | 19 | 18 |  | 
9 | 31 | 20 | 39 |  | 
10 | 25 | 21 | 30 |  | 
11 | 20 | 22 | 24 |  | 

## Slide 41: Example
Since the 26 samples contain 516 nonconformities, we estimate c by:
Therefore, the trial control limits are given by:

## Slide 42: Example
Two points plot outside the control limits, samples 6 and 20.
The process is out of control.
The point must be investigated to see whether an assignable cause can be determined

## Slide 43: Example
After dropping samples 6 and 20, the estimate of c is now:
The revised control limits are given by:

## Slide 44: Control Chart for Average Number of Nonconformities per Unit (U)
If we find x total nonconformities in a sample of n inspection units, then the average number of nonconformities per inspection unit is u = x/n.
The control limits for the average number of nonconformities is

## Slide 45: Example
A personal computer manufacture wishes to establish a control chart for nonconformities per unit on the final assembly line.
The sample size is selected as five computers.
Data on the number of nonconformities in 20 samples of 5 computers each are shown in the next table.

## Slide 46: Example
Sample Number, i | Sample Size n | Total Number of Nonconformities, xi | Average Number of Nonconformities per unit, ui =xi /n
1 | 5 | 10 | 2.0
2 | 5 | 12 | 2.4
3 | 5 | 8 | 1.6
4 | 5 | 14 | 2.8
5 | 5 | 10 | 2.0
6 | 5 | 16 | 3.2
7 | 5 | 11 | 2.2
8 | 5 | 7 | 1.4
9 | 5 | 10 | 2.0
10 | 5 | 15 | 3.0
11 | 5 | 9 | 1.8
……………… | ……………… | ……………… | ………………
19 | 5 | 7 | 1.4
20 | 5 | 5 | 1.0
Sum |  | 193 | 38.6

## Slide 47: Example
From the data, we would estimate the average number of nonconformities per unit to be:
Therefore, the trial control limits are given by:

## Slide 48: Example
The preliminary data do not exhibit lack of statistical control.
The trial control limits should be adopted for current control purposes.
The average number of nonconformities is unacceptably high.
Management intervention are required.

## Slide 49
Thank You