## Slide 1
Module 4
Middleboxes
Prepared by Dr. Manal Mizher
Lecture 8
Network programming
Course ID: CYB615

## Slide 2
Outlines
Module
4
      TCP Flags, Inbound, Outbound
      Write/Read to .pcap file in Scapy
      Middleboxes
      (Definition, Network Functions (NFs), Benefits, How is use it? , Criticism and challenges, Categories)
Examples of Middleboxes
      Firewalls
      Intrusion detection systems (IDSs)
      Intrusion prevention systems (IPSs)
      Network address translators (NATs) Port-Translating NAT (PAT)
      WAN optimizers
      Proxy server
      Load balancers

## Slide 3
TCP Flags
Module
4
https://www.geeksforgeeks.org/tcp-flags/
In TCP connection:
  Flags are used to indicate a particular state of connection or to provide some additional useful information like troubleshooting purposes or to handle a control of a particular connection.
  Most commonly used flags are “SYN”, “ACK” and “FIN”. Each flag corresponds to 1 bit information. Where set flag = 1, unset =0

## Slide 4
TCP Flags
Module
4

## Slide 5
TCP Flags in Wireshark
Module
4

## Slide 6
Inbound and Outbound
Module
4
  Inbound means someone else from outside of your computer initiate the connection to your computer, so the traffic starts flowing inward to your machine.
  Outbound means you initiate the connection and the traffic starts flowing outward of your computer to the destination you intended. Example you connect to a server.
  You can stop inbound and outbound packets and modify them, before they will be processed by Windows network stack.

## Slide 7
      Write/Read to .pcap file in Scapy
Module
4
from scapy.all import * data = 'Everyone s Smart University' a = IP(dst='129.132.2.21') / UDP() / Raw(load=data) send(a) wrpcap('ESU_udp.pcap', a, append=True) a.show() print(a) data2 = 'Network programming class' packet = Ether()/IP(src='129.132.2.1', dst='129.132.2.21')/TCP(sport=50, dport=100, flags='A')/Raw(load=data2) sendp(packet) wrpcap('ESU_tcp.pcap', packet, append=True) packet.show() print(packet)
Write:

## Slide 8
      Write/Read to .pcap file in Scapy
Module
4
Read:
from scapy.all import * packets = rdpcap('ESU_udp.pcap') print('packets =', packets) for pkt in packets: if TCP in pkt: pdataTCP = bytes(pkt[TCP].payload) print('TCP') print('pdataTCP =', pdataTCP) if Raw in pkt: pdataRaw = bytes(pkt[Raw].payload) print('Raw') print('pdataRaw =', pdataRaw) if UDP in pkt: pdataUDP = bytes(pkt[UDP].payload) print('UDP') print('pdataUDP =', pdataUDP) else: pdataNone = "" print('None') print('pdataNone =', pdataNone)

## Slide 9
Definition (Middleboxes)
Module
4
Computer networking device (Or software): that transforms, inspects, filters, and manipulates traffic for purposes other than packet forwarding.
Any intermediary network device performing functions other than standard functions of an IP forwarding between two end hosts.
These extraneous functions have interfered with application performance and have been criticized for violating "important architectural principles" such as the end-to-end principle.
Examples of middleboxes include firewalls, network address translators (NATs), load balancers, and deep packet inspection (DPI) boxes.

## Slide 10
      Network Functions (NFs) (
Module
4
Special-purpose operations on packets:
        - Service Providers: DPI, load-balancer, …
        - Enterprises: Firewalls, NAT, …
Physical appliances (middle-boxes) are expensive.
Virtual appliances (VNFs) difficult to scale.

## Slide 11
Who uses middleboxes?
Module
4
Middleboxes are widely deployed across both private and public networks.
Cellular networks use middleboxes to ensure scarce network resources are used efficiently as well as to protect client devices.
Dedicated middlebox hardware is widely deployed in enterprise networks to improve network security and performance, however, even home network routers often have integrated firewall, NAT, or other middlebox functionality (has some middlebox capabilities!).
Service Providers (ISPs)

## Slide 12
Benefits of Middleboxes
Module
4
Reasons driving the deployment of middleboxes come in two main categories:
      (1) Security to enhance the visibility of network traffic and enable the enforcement of security policies.
      (2) Performance enhancements through traffic shaping, caching and transparent proxying.

## Slide 13
Criticism and challenges of Middleboxes
Module
4
Compared to forwarding devices such as switches and routers, middleboxes are complex.
Indeed, they operate on flows of packets at multiple layers of the network stack, from the network layer to the application layer, and do so at line rate.
Middleboxes interfere with end-to-end packet transmission, application functionality, and restricting or preventing end host applications from functioning properly.

## Slide 14
Criticism and challenges of Middleboxe
Module
4

## Slide 15
Middlebox Categories
Module
4
Middlebox interference can be categorized into three types:
Middleboxes intentionally drop or filter packets according to policies:
    For example, network administrators filter P2P file sharing traffic to avoid the legal implications of copyrighted content .
  Middleboxes modify the content of packets:
      Some web proxies modify HTTP headers to control meta information between client and server (e.g., cache preferences).
Middleboxes also inject forged packets, e.g., for blocking purposes:
    A notorious example is the Great Firewall of China (GFC) that blocks specific sites by injecting spoofed DNS responses, with obvious consequences in terms of Internet censorship

## Slide 16
Examples of Middleboxes
Module
4
Firewalls
Intrusion detection systems (IDSs)
Intrusion prevention systems (IPSs)
Network address translators (NATs) Port-Translating NAT (PAT)
WAN optimizers
Proxy server
Load balancers

## Slide 17
Examples of Middleboxes (Firewalls)
Module
4
Firewalls:
  Filter traffic based on a set of predefined security rules defined by a network administrator.
  IP firewalls reject packets "based purely on fields in the IP and transport headers (e.g., disallow incoming traffic to certain port numbers, disallow any traffic to certain subnets etc.)“.
  Other types of firewalls may use more complex rule sets, including those that inspect traffic at the session or application layer.
https://docs.rackspace.com/support/how-to/best-practices-for-firewall-rules-configuration/

## Slide 18
Firewall Configuration
Module
4
So, Firewall filters packet-by-packet, based on:
  - Source and destination IP addresses and port #’s
  - TCP SYN and ACK bits; ICMP message type
  - Deep packet inspection on packet contents (DPI)
Firewall applies a set of rules to each packet
  - To decide whether to permit or deny the packet
Each rule is tested on the packet
  - Comparing headers, deciding whether to allow/deny
Order matters
  - Once packet matches a rule, the decision is done

## Slide 19
Packet Filtering Examples
Module
4
Block all packets with IP protocol field = 17 and with either src port or dst port = 23
  - All incoming and outgoing UDP flows blocked
  - All Telnet connections are blocked
Block inbound TCP packets with SYN but no ACK
  - Prevents external clients from making TCP connections with internal clients
  - But allows internal clients to connect to outside
Block all packets with TCP port of Fortnite
- Ex: 80, 443 and 5222 all TCP

## Slide 20
from scapy.all import * global my_keyword1, my_keyword2 my_keyword1 = TCP my_keyword2 = UDP def pkt_callback(pkt): global my_keyword1, my_keyword2 if my_keyword1 in pkt: pkt.show() print("recognized TCP packet") print('Destination port =', pkt[TCP].dport) print('Source port =', pkt[TCP].sport) elif my_keyword2: pkt.show() print("recognized UDP packet") print('Destination port =', pkt[UDP].dport) print('Source port =', pkt[UDP].sport) else: pkt.show() print("This packet is neither TCP nor UDP") # Spkt = sniff(iface='Qualcomm Atheros AR9485WB-EG Wireless Network Adapter', count=4, filter="udp sport 80 or dport 80 ", prn=lambda x:x.summary()) Spkt = sniff(iface='Qualcomm Atheros AR9485WB-EG Wireless Network Adapter', filter=" tcp or udp", count=2, prn=pkt_callback) Spkt.summary()
Filtering packets using Scapy
Module
4

## Slide 21
Filtering packets using Scapy
Module
4
The sniff() function listens for an infinite period of time until the user interrupts.
To restrict the number of packets to be captured sniff() allows a count parameter.
You can also filter packets while sniffing using the filter parameter. It uses a Berkeley Packet Filter (BPF) syntax.
You can filter any packet on the basis of source/destination IP address, port number, protocol and lot more by using the BPF syntax.
We can also sniff packets offline from pcap files by running the following command: sniff(offline="<file name>") , ex: ="<file name> = 1.pcap
When scapy sniffs packets, it generally sniffs from all of your network interfaces. However, we can explicitly mention the interfaces that we would like to sniff on using the iface parameter.
https://biot.com/capstats/bpf.html

## Slide 22
Filtering packets using Scapy
Module
4
sniff() function has another interesting parameter called prn that allows you to pass a function that executes with each packet sniffed. This allows us to do some custom actions with each packet sniffed. sniff(prn=lambda x:x.summary(), count=5)
In order for your program/script to format and return the packet info as you wish, the sniff function passes the packet object as the one and only argument into the function you specify in the sniff's prn argument. This gives us the option to do some fun stuff (not just formatting) with each packet sniffed
https://biot.com/capstats/bpf.html

## Slide 23
Custom Formatted ARP Monitor
Module
4
Here are some conditional statements to very clearly tell me what ARP traffic in my computer is seeing.
Address Resolution Protocol (ARP) is a protocol or procedure that connects an ever-changing Internet Protocol (IP) address to a fixed physical machine.
from collections import Counter from scapy.all import ARP, sniff def arp_display(pkt): if pkt[ARP].op == 1: #who-has (request) return f"Request: {pkt[ARP].psrc} is asking about {pkt[ARP].pdst}" if pkt[ARP].op == 2: #is-at (response) return f"*Response: {pkt[ARP].hwsrc} has address {pkt[ARP].psrc}" sniff(prn=arp_display, filter="arp", store=0, count=10)
Small letters, ex: ip, arp, tcp, udp, icmp

## Slide 24
Scapy sniff filter tcp with SYN ACK
Module
4
from scapy.all import * def filter_TCP_flags(pkt): if pkt.haslayer(TCP): # print('Packet = ', pkt) # packetstr = "".join(map(chr, bytes(pkt))) # print('Packet AS string= ', packetstr) print('TCP flag is ', pkt[TCP].flags) if 'P' in pkt[TCP].flags: print('Could you drop this packet?') pkts = sniff(filter='tcp and (tcp.flags.syn or tcp.flags.ack)', prn=filter_TCP_flags, count=30)
If you wonder why the packets cannot be dropped: The software does not intercept the traffic, it instead shares a view on the network data through promiscuous mode.

## Slide 25
Filtering packets (IPs) using Scapy
Module
4
You can use haslayer() method:
def pkt_callback(pkt): if pkt.haslayer(TCP): pkt.show()
Q: Filter packets of a particular website in Python (using Scapy)? Suppose that you have a list of possible IPs (used for load balancing) of the website. And, you want to filter packets for all those IPs. How can you do that?
https://biot.com/capstats/bpf.html

## Slide 26
Filtering packets using Scapy
Module
4
from scapy.all import * global addresses, addressesBlocked addresses = ["239.255.255.250", "216.58.212.110", "142.251.37.163", "142.251.37.35", "142.250.200.238"] addressesBlocked = [] def pkt_callback(pkts): global addresses, addressesBlocked print(pkts[IP].dst) if pkts[IP].dst in addresses: if pkts[IP].dst in addressesBlocked: a = 4 else: addressesBlocked.append(pkts[IP].dst) Spkt = sniff(iface='Qualcomm Atheros AR9485WB-EG Wireless Network Adapter', count=3, prn=pkt_callback, store=0) if len(addressesBlocked): print('Blocked IPs : ', addressesBlocked) else: print('*** NO Blocked IPs! ***') # store=0 ---> discard sniffed packets

## Slide 27
Examples of Middleboxes (IDs)
Module
4
Intrusion detection systems (IDSs):
  Monitor traffic and collect data for offline analysis for security anomalies.
  Unlike firewalls, IDSs do not filter packets in real time, as they are capable of more complex inspection and must decide whether to accept or reject each packet as it arrives.
https://www.dnsstuff.com/network-intrusion-detection-software

## Slide 28
IDS by Scapy
Module
4
def detect_TCPflood(self,packet): if packet.haslayer(TCP): pckt_src=packet[IP].src pckt_dst=packet[IP].dst stream = pckt_src + ':' + pckt_dst if stream in type(self).__ip_cnt_TCP: type(self).__ip_cnt_TCP[stream] += 1 else: type(self).__ip_cnt_TCP[stream] = 1 for stream in type(self).__ip_cnt_TCP: pckts_sent = type(self).__ip_cnt_TCP[stream] if pckts_sent > type(self).__THRESH: src = stream.split(':')[0] dst = stream.split(':')[1] print("Possible Flooding Attack from %s --> %s"%(src, dst))

## Slide 29
IDS by Scapy
Module
4

## Slide 30
Examples of Middleboxes (IPSs)
Module
4
Intrusion prevention systems (IPSs):
  is a network security tool (which can be a hardware device or software) that continuously monitors a network for malicious activity and takes action to prevent it, including reporting, blocking, or dropping it, when it does occur.
  Intrusion prevention systems expand on the capabilities of intrusion detection systems (IDS), which serve the fundamental purpose of monitoring network and system traffic.
  What makes intrusion prevention systems more advanced than intrusion detection systems is that IPS are located in-line (directly in the path in which the source and destination communicate) and have the capability to prevent or block the malicious activity that is occurring.
  https://digitalguardian.com/dskb/intrusion-prevention-system

## Slide 31
Intrusion Detection VS Prevention Systems
Module
4
https://purplesec.us/intrusion-detection-vs-intrusion-prevention-systems/
Intrusion prevention systems are usually located behind a firewall to function as another filter for malicious activity.

## Slide 32
Examples of Middleboxes (NAT)
Module
4
Network address translators (NATs):
  replace the source and/or destination IP addresses of packets that traverse them.
  Typically, NATs are deployed to allow multiple end hosts to share a single IP address: hosts "behind" the NAT are assigned a private IP address and their packets destined to the public Internet traverse a NAT, which replaces their internal private address with a shared public address. These are widely used by cellular network providers to manage scarce resources.

## Slide 33
Examples of Middleboxes (NAT)
NAT
inside
outside
10.0.0.1
10.0.0.2
Problem: Local address not globally addressable
NAT rewrites the IP addresses
  Make “inside” look like single IP addr
  Change header checksums accordingly
  Outbound: Rewrite the src IP addr
  Inbound: Rewrite the dest IP addr
138.76.29.7

## Slide 34
Examples of Middleboxes (PAT)
Module
4
Port Address Translation (PAT): is an extension of Network Address Translation (NAT) that permits multiple devices on a LAN to be mapped to a single public IP address to conserve IP addresses.
  Map of (src addr, port #) to (NAT addr, new port #)

## Slide 35
Examples of Middleboxes (WAN optimizer)
Module
4
WAN optimizers:
  Improve bandwidth consumption and perceived latency between endpoints.
  Typically deployed in large enterprises, WAN optimizers are deployed near both sending and receiving endpoints of communication; the devices then coordinate to cache and compress traffic that traverses the Internet.

## Slide 36
Examples of Middleboxes (Proxy)
Module
4
Proxy server:
  is a system or router that provides a gateway between users and the internet.
  Therefore, it helps prevent cyber attackers from entering a private network.
  It is a server, referred to as an “intermediary” because it goes between end-users and the web pages they visit online.
https://www.varonis.com/blog/what-is-a-proxy-server

## Slide 37
Examples of Middleboxes (Proxy)
Module
4
A proxy server is basically a computer on the internet with its own IP address that your computer knows. When you send a web request, your request goes to the proxy server first. The proxy server then makes your web request on your behalf, collects the response from the web server, and forwards you the web page data so you can see the page in your browser.
When the proxy server forwards your web requests, it can make changes to the data you send and still get you the information that you expect to see. A proxy server can change your IP address, so the web server doesn’t know exactly where you are in the world. It can encrypt your data, so your data is unreadable in transit. And lastly, a proxy server can block access to certain web pages, based on IP address.

## Slide 38
Examples of Middleboxes (Proxy)
Module
4

## Slide 39
Examples of Middleboxes (Load balancer)
Module
4
Load balancers: provide one point of entry to a service, but forward traffic flows to one or more hosts that actually provide the service.

## Slide 40
Load balancers
Module
4
What is load balancers in network? (Traffic cop)
    A load balancer is a device (Or software) that acts as a reverse proxy and distributes network or application traffic across a number of servers. Load balancers are used to increase capacity (concurrent users) and reliability of applications.
Benefits of Load Balancing:
    Reduced downtime
    Scalable
    Redundancy
    Flexibility
    Efficiency

## Slide 41
Load balancers
Module
4
Load balancer performs the following functions:
  Distributes client requests or network load efficiently across multiple servers.
  Ensures high availability and reliability by sending requests only to servers that are online.
  Provides the flexibility to add or subtract servers as demand dictates.

## Slide 42
Hardware vs. Software Load Balancing
Module
4
Load balancers typically come in two flavors:
  hardware‑based and software‑based.
  Vendors of hardware‑based solutions load proprietary software onto the machine they provide, which often uses specialized processors.
  To cope with increasing traffic at your website, you have to buy more or bigger machines from the vendor.
  Software solutions generally run on commodity hardware, making them less expensive and more flexible.
  You can install the software on the hardware of your choice or in cloud environments like AWS EC2.
** Commodity hardware refers to cheap, standardized servers that are easy to buy off the shelf from any vendor.