## Slide 1
Prepared by Dr. Eng. Gamal Selim
Computer Organization and Architecture
Lecture 04 – Binary Arithmetic Operations

## Slide 2
Arithmetic for Computers

## Slide 3: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
ALU: Arithmetic Logic Unit
  HW performs addition, subtraction, and usually logical operations such as AND and OR

## Slide 4
Addition in Binary

## Slide 5: Addition in Binary
In decimal if you add two digits and the sum is more than the base ( 10 ) you add all the 10s in the result to the next higher digit and leave the remainder in the current digit.
The rule is the same for integer and decimal fractions.
In binary this rule applies as :
1+0 = 1
1+1 =
10 ( as no 2 is allowed in binary)

## Slide 6: Problem 1
( )2
(b) 1111 + 0011
Solution:
( 15)10: (1111)2
( 3)10: (0011)2
+
0
1
0
0
1
(18)10:
Add the following in binary and check results by doing addition in decimal:
(c) 1011.1101 + 11.1
Solution:
( 11.8125)10: (1011.1101)2
( 3.5)10: (0011.1000)2
+
1
0
1
0
1
1
1
1
( 15.3125)10:
.
(e) 1111000 + 00010010
Solution:
( 120)10: (1111000 )2
( 18)10: (0010010 )2
+
0
1
0
1
0
0
0
( 138)10:
1
( )2
( )2

## Slide 7: Example
Add 10011 and 11101 in binary:
10011 + 11101 ------ 110000

## Slide 8
Signed Numbers

## Slide 9: Signed number representation in binary
We have two ways of representing signed numbers:
Sign-magnitude system.
2’s complement system

## Slide 10: Sign-magnitude system
In decimal we have positive and negative numbers like +20 or – 31
In binary bits are stored in Flip-flops ( units that can only store 1 or 0)
The negative number in signed magnitude binary representation is as follows:
-4 = 1100 (sign bit always at the left most bit =1)
If represented in 8 bits -4 = 1000 0100
Positive numbers have the sign bit = 0
+4 = 0100 (sign bit always at the left most bit =0)
If represented in 8 bits +4 = 0000 0100

## Slide 11: 2’s complement system
The positive form of a number is the same as the sign magnitude having the MSB as the sign bit with 0 to indicate positive value.
The negative form of a number is done using the 2’s complement of the positive number.
So how can the 2’s complement of a number be deduced ??
We start by getting the 1’s complement form of a number then the 2’s complement.

## Slide 12: 1’s complement
The 1’s complement of a number N is the number added to N to make it all 1s (2n - 1) .
The 1's complement of N is (2n - 1) - N.
Note that 2n - 1 is a binary number represented by n 1s.
For example, with n = 4, we have 24 = (10000)2 and 24 - 1 = (1111)2.
Thus the 1's complement of a binary number is obtained by subtracting each digit from 1.

## Slide 13: 1’s complement
However, the subtraction of a binary digit from 1 causes the bit to change from 0 to 1 or from 1 to 0. Therefore, the 1's complement of a binary number is formed by changing 1s into 0s and 0s into 1s.
For example, the 1's complement of 1011001 is 0100110 and the 1's complement of 0001111 is 1110000.
What is the 1’s complement of 0 ?

## Slide 14: 2’s complement
The 2’s complement of a number N with n bits is the number added to N to make it 2n.
The 2's complement of N is 2n - N.
Note that 2n is represented by a binary number that consists of a 1 followed by n 0s.
For example, with n = 4, we have 24 = (10000)2.
Hence we have 2 ways to get the 2’s complement:
By getting the 1’s complement then adding 1 to it [(2n-1- N) +1]= 2n-N.
By subtracting the number from the 1 followed by n 0s for example:
the 2’s complement of 1100 is
10000
1100
-
0100

## Slide 15: 2’s complement
Hence, the 2's complement can be formed by leaving all least significant 0's and the first 1 unchanged, and then replacing 1's by 0's and 0's by 1's in all other higher significant bits.
The 2's complement of 1101100 is 0010100 and is obtained by leaving the two low-order 0' s and the first 1 unchanged, and then replacing 1's by 0's and 0's by 1's in the other four most significant bits.
If the original number N contains a radix point, it should be removed temporarily to form the 2's or 1's complement then restored to the complemented number in the same relative position.

## Slide 16: 2’s complement
The complement of the complement restores the number to its original value.
The 2's complement of N is 2n - N. The complement of the complement is 2n - (2n - N) = N giving back the original number.
Representing binary numbers in 2’s complement form enables us to represent negative numbers.

## Slide 17: Problem 2
Repeat each of the following signed decimal numbers in 2's-complement system. Use a total of 8 bits including sign bit
(a)+32
Solution:
The representation of 32 in binary is 100000
In 8 bits = 00100000

## Slide 18: Problem 2
(b) -1
Solution:
First we obtain the positive number in binary then get the 2’s complement of this binary number in 8 bits
1 = 00000001
2’s complement of 00000001
-1 = 11111111

## Slide 19: Problem 2 cont.
Repeat each of the following signed decimal numbers in 2's-complement system. Use a total of 8 bits including sign bit
(c) -128
Solution:
First we obtain the positive number in binary then get the 2’s complement of this binary number
128 = 2 7
128 → 10000000
2’s complement of 10000000
-128= 10000000

## Slide 20: Problem 3
Each of the following numbers represents a signed decimal number in the 2's-complement system. determine the decimal value in each case. (Hint: Use negative to convert negative numbers to positive)
(a) 01101
Solution:
The sign bit = 0
Then the number is positive and the value =
8+4+1 = 13

## Slide 21: Problem 3
Each of the following numbers represents a signed decimal number in the 2's-complement system. determine the decimal value in each case. (Hint: Use negative to convert negative numbers to positive)
(b) 01111111
Solution:
The sign bit = 0
Then the number is positive and the value =
27-1 = 128 -1 = 127

## Slide 22: Problem 3 cont.
Each of the following numbers represents a signed decimal number in the 2's-complement system. determine the decimal value in each case. (Hint: Use negative to convert negative numbers to positive)
(d) 1000000
Solution:
The sign bit = 1
Then the number is negative in 2’s complement form and the value is the 2’s complement of the number
The 2’s complement of 1000000 = 1000000
Decimal value of 1000000 = 26 = - 64
Hence the decimal value of 11111111 = -1

## Slide 23: Problem 4
(a) What range of signed decimal values can be represented using 12 bits in 2’s complement form including sign bit?
Solution:
When excluding the sign bit we have 11 bits hence the largest decimal positive number = 2n-1 = 211-1 = 2048 -1 = 2047
  In negative the largest value in 12 bits is
  100000000000
  Because the 2’s complement of this value is equal to the same number which is equal to 211 hence the largest negative value is -2048
  The range for signed decimal values can be represented using N bits including sign bit is from 2(N-1)-1 to -2(N-1)
  (b) How many bits would be required to represent decimal numbers from -32,768 to 32,767?
  Solution:
  we get 2n representing -32,768 by getting log 32,768 / log 2 = 15
  Hence in (15+1) = 16 bits we can represent – 215 to + 215-1

## Slide 24: Problem 5
Represent each of the following decimal values as 5-bit signed magnitude binary values. Then negate each one.
(b) -12
Solution:
-12 =
11100
The negative of -12 = 01100

## Slide 25
Subtraction in Binary

## Slide 26: Subtraction in binary
The direct method of subtraction taught in elementary schools uses the borrow concept.
In this method we borrow a 1 from a higher significant position when the minuend digit is smaller than the corresponding subtrahend digit.
In binary this is difficult as bits are stored in Flip-flops and cannot do the borrow operation.
Hence the subtraction is converted to addition using complements.

## Slide 27: Subtraction using 1’s complement
If we have two numbers M, N ( M and N have n digits)
We have the 1’s complement of N = (2n-1) –N
Hence to get the M-N we have
( M + 1’s complement of N )
= M + ((2n-1) –N )
= M – N + 2n-1
That leads to the conclusion that when you need to subtract two numbers you can add the 1’s form of the subtrahend to the minuend then discard the carry digit ( 2n = 1 followed by n digits) and add 1 to get the result you need.

## Slide 28: Subtraction using 1’s complement
Example:
For b = 10 ( M = 35 , N = 14, 9s complement of 14 = 85)
35 +85 =
20
To get the final result discard the 1( MSD) and add 1
M-N = 21
Example: For b= 2 ( M = 100011 , N = 001110)
100011 + 110001 =
010100
To get the final result discard the 1( MSD) and add 1
M-N = (010101)2= 21

## Slide 29: Subtraction using 2’s complement
The subtraction of two n-digit unsigned numbers M - N (N 0) in base b can be done as follows:
Add the minuend M to the 2's complement of the subtrahend N. This performs M + (2n - N) = M - N + 2n.
There are three cases :
  If M > N, the sum will produce an end carry 2n which is discarded, and what is left is the result M - N.
  If M < N, the sum does not produce an end carry and is equal to 2n- (N- M), which is the 2's complement of (N- M). To obtain the answer in a familiar form, take the b's complement of the sum and place a negative sign in front.

## Slide 30: Subtraction using 2’s complement
  3. If N and M are both in b’s complement form (i.e. both are considered negative then )
    We add the two numbers to get the result which will be considered negative
    (2n-M)+ (2n-N) = 2n-(M+N) +2n
    The result indicated that there will be a carry bit which will be discarded then the rest of the result is considered the 2’s complement of the needed result.

## Slide 31: Problem 6
Perform the following operation in 2's-complement system. Use 8-bit (including the sign bit) for each number. Check your results by converting the binary result back to decimal.
(a) Add + 19 to -24
(24)10 = (00011000)2
( 19)10: (00010011)2
(-24)10: (11101000)2
+
1
1
0
1
1
1
1
1
(-5)10:
( 5)10: (00000101)2
(b) Add -48 to -80
(48)10 = (00110000)2
(80)10 = (01010000)2
( -48)10: (11010000)2
( -80)10: (10110000)2
+
0
0
0
0
0
0
0
1
(-128)10:
1
1
( 128)10: (10000000)2

## Slide 32: Problem 6 cont.
Perform the following operation in 2's-complement system. Use 8-bit (including the sign bit) for each number. Check your results by converting the binary result back to decimal.
(c) Subtract + 16 from +17
17 – 16 = 17 + ( -16)
(16)10=(00010000)2
(17)10: (00010001)2
(-16)10: (11110000)2
+
1
0
0
0
0
0
0
0
(1)10:
1

## Slide 33: Problem 6 cont.
Perform the following operation in 2's-complement system. Use 8-bit (including the sign bit) for each number. Check your results by converting the binary result back to decimal.
(d) Subtract +21 from -13
-13-(21) = -13 +(-21)
(13)10=(00001101)2
(21)10=(00010101)2
(-13)10: (11110011)2
(-21)10: (11101011)2
+
0
1
1
1
1
0
1
1
(-34)10:
1
(34)10: (00100010)2

## Slide 34: Problem 6 cont.
Perform the following operation in 2's-complement system. Use 8-bit (including the sign bit) for each number. Check your results by converting the binary result back to decimal.
(g) Subtract -17 from -17
-17-(-17) = -17 +17 = 17 -17
( 17)10: (00010001)2
(-17)10: (11101111)2
+
0
0
0
0
0
0
0
0
(0)10:
1

## Slide 35
Multiplication in Binary

## Slide 36: Problem 7
Multiply the following pairs of binary numbers and check by doing multiplication in decimal.
(b) 1011 × 1011
Solution:
( 11 )10: (1011)2
( 11 )10: (1011)2
×
0
1
1
1
(121)10:
1
0
1011
1011
0000
1011
1
(d) 11111 × 101
Solution:
( 31 )10: (11111)2
( 5 )10: (101)2
×
0
1
1
0
(155)10:
1
1
11111
00000
0
11111
1

## Slide 37
Problem 8

## Slide 38
Division in Binary

## Slide 39: Problem 9
Perform the following divisions. Check the results by doing division in decimal.
(1001)2
1
0
0
0
0
1
1
1
1
(111111)2
(a) 111111/1001
Solution
1001
0
1
1001
0
0
1
0
1
1001
0000
(7)10

## Slide 40: Problem 9 cont.
Perform the following divisions. Check the results by doing division in decimal.
(7)10:(111)2
0
1
0
0
0
0
0
0
0
(1110111)2 : ( 119 )10
(b) 1110111/111
Solution
111
0
1
111
000
(17)10
1
1
1

## Slide 41
  Thank You