## Slide 1
Prepared by Dr. Diaa Salama
Cybersecurity
Concepts
Lecture 2
FNT625
Network Basics

## Slide 2
Cybersecurity
Concepts
Lecture 2
FNT625
Introduction to Network and Network Security
Dr. Diaa Salama
Prepared by
www.midocean.ae

## Slide 3
Book Title:
Cryptography and Network Security
Authors:
William Stallings
Publisher:
Pearson Education, Inc.
Edition:
Seven edition

## Slide 4
Introduction to Network and Network Security
Lets Start the second Lecture
Lecture
02
www.midocean.ae

## Slide 5
What is Cyber Security (Network Security) !
Lecture
02
www.midocean.ae
A network is simply two or more computers linked together to share data, information or resources.
Security : prevention of system Crash

## Slide 6
Introduction to Computer Networks
www.midocean.ae

## Slide 7: Introduction to Computer Networks
How to communicate each point to another point or points.
www.midocean.ae

## Slide 8: Introduction to Computer Networks
Drainage networks
Networks
Telephone networks
Electricity networks
Difficult for data transmission
www.midocean.ae

## Slide 9
Types of Computer Networks
www.midocean.ae

## Slide 10: Types of Computer Networks
LAN
Local Area Network
Network Types
WAN
Wide Area Network
MAN
Internal network
not small network
External network
not Large network
Hardware:
Cables
Switch
Pc with NIC [network
interface card]
Hardware:
Cables
Switch
Pc with NIC [network
interface card]
Router
www.midocean.ae

## Slide 11: Introduction to Computer Networks
Connecting two Computers on the same location (e.g. in Lab).
Connecting two Computers on different and distant locations.
www.midocean.ae

## Slide 12
How to Setup a LAN
www.midocean.ae

## Slide 13: How to Setup a LAN
Hardware
LAN
Component
Software
Hardware:
Cables
Switch
Pc with
NIC [network
interface card]
www.midocean.ae

## Slide 14
1- Cables
www.midocean.ae

## Slide 15: Cables
Type | Scientific Name | Speed/distance Data transfer | Comments
Coaxial Cable | Thin 10 base 2 (20 milli) (Megabit/s) Thick 10 base 5 (50 milli) (Megabit/s) Thick 100 base 5 (Megabit/s) Thick 1000 base 5 (1000 Megabit/s) | 100 m (long distance need repeater). 500 m | Cable is not elastic so it is not practical for long distance. It uses BNC connector for terminals so it needs a converter to connect to a switch or router device . It is expensive
UTP unshielded twisted pair | 10 base T (Twisted Pair). In market it is famous with Cat 5 (max speed 10 Megabit/s) Cat 5 e (enhanced max) max speed 100 Megabit/s Cat 6 (max speed 1000 Megabit/s ) | 100 m Connector RJ45 | It is not expensive It is connected directly to switch or router.
Max
Speed
Thickness
If cable speed is 10 means 10 Mega bits/second
Network speed is measured by bit.
While storing data is measured by byte.
www.midocean.ae
Cables

## Slide 16: Cables
Type | Scientific Name | Speed/distance (Data transfer) | Comments
STP shielded twisted pair | 10 base T (Twisted Pair). In market it is famous with Cat 5 (max speed 10 Megabit/s) Cat 5 e (enhanced max) max speed 100 Megabit/s Cat 6 (max speed 1000 Megabit/s) | 100 m Connector RJ45 | It is expensive It is connected directly to switch or router.
Fiber Optics | 10 base F | 300 km/s | 
www.midocean.ae

## Slide 17: Coaxial Cable
www.midocean.ae

## Slide 18: Unshielded Twisted Pair (UTP) VS (STP)
www.midocean.ae

## Slide 19: Fiber Optics
www.midocean.ae
Straight Tip Connector
Lucent Connector
Standard Connector

## Slide 20: Fiber optics Cables
Two types of optical cables: single-mode and multimode
Single-mode | Multimode
Carries single beam of light | Can carry multiple beams of light simultaneously
Distance up to 10km | Used for short distance (Modal dispersion weakens signal strength after certain distance )
Multimode Fiber
Single-mode Fiber

## Slide 21: Fiber Optics
www.midocean.ae
Straight Tip Connector
Lucent Connector
Standard Connector

## Slide 22
Connecting Two Devices
www.midocean.ae

## Slide 23
Cisco Certified Network Associate (CCNA)
Week
02
www.midocean.ae

## Slide 24: Connecting Two Devices
Standard (straight)
UTP Cable
Color arrangement
Crossover
Used when connecting
two different devices
Used when connecting
two similar devices
www.midocean.ae

## Slide 25: Connecting Two Devices
Used when connecting
two similar devices
Used when connecting
two different devices
trunk
switch
router
Hub
PC
Web
server

## Slide 26: Connecting Two Devices
Used when connecting
two similar devices
Used when connecting
two different devices
trunk

## Slide 27: Connecting Two Devices
Used when connecting
two similar devices
Used when connecting
two different devices
trunk
Both of these devices are expecting to connect to a switch. When connecting them together, we need to use a cross-over cables so that the transmit pair from 1 device, goes to the receive pair of the other device.

## Slide 28: Connecting Two Devices
Standard (straight)
Crossover
www.midocean.ae

## Slide 29
Cisco Certified Network Associate (CCNA)
Week
02
www.midocean.ae

## Slide 30
2- Switch
www.midocean.ae

## Slide 31: Switch
www.midocean.ae

## Slide 32: Switch
Ethernet 10 mbps
Megabit/second
Switch Ports
Ethernet 1000 mbps
Megabit/second
Ethernet 100 mbps
Megabit/second
Each port in the switch has a speed
Ports may be Ethernet 10 mbps Megabit/second.
Ports may be Fast Ethernet 100 mbps Megabit/second.
Ports may be Giga Ethernet 1000 mbps Megabit/second.
www.midocean.ae

## Slide 33: Switch
Actually you can not differentiate between a hub and a switch once viewed.
If PC1 to PC6 are connected to a hub. Assume that PC1 wants to send a message to PC4.
The hub will send the message to all PC’s and only PC4 will accept the message while the others will send a message to the hub “the message is not belong to me.”
www.midocean.ae

## Slide 34: Switch
Then the hub will send alert message to PC1 that the message is cancelled from PCx. all the returned message will cause a heavy on the network which we call it a loop.
www.midocean.ae

## Slide 35: Switch
The switch is smarter than the hub.
If PC1 to PC6 are connected to a switch. Assume that PC1 wants to send a message to PC4.
The switch will act as a hub “it will send the message to all PC’s and only PC4 will accept the message while the others will send a message to the hub “the message is not belong to me.”
The switch has flash memory and a table that save all IP address’s of all the connected PC’s.
Source |  | Destination | 
PC1 | device Address | PC4 | device Address
www.midocean.ae

## Slide 36: Switch
Then the switch will register PC4 address in the destination when it does not receive any massage from it.
After that the switch will send all the data from PC1 directly to PC4 address without sending it to the others.
The switch will reduce the loop on the network but not prevent it.
Source |  | Destination | 
PC1 | device Address | PC4 | device Address
www.midocean.ae

## Slide 37
3- Network Interface Card (NIC)
www.midocean.ae

## Slide 38: Network Interface Card
A NIC, or LAN adapter, provides the physical connection to the network at the PC or other end device.
The media that are connecting the PC to the networking device, plug directly into the NIC.
Physical Port - A connector or outlet on a networking device where the media is connected to an end device or another networking device.
www.midocean.ae

## Slide 39: Network Interface Card
Interface - Specialized ports on a networking device that connect to individual networks.
Because routers are used to interconnect networks, the ports on a router are referred to as network interfaces.
Note: Often, the terms port and interface are used interchangeably.
www.midocean.ae

## Slide 40
Design a Communications System
Open System Interconnection (OSI)
www.midocean.ae

## Slide 41: Design a Communications System
Design a Communications System
Objectives:
  Explain the role of protocols and standards organizations in facilitating interoperability in network communications.
  IP Addressing & Subnet Mask
  Protocol
  Port
Notes: 41
3 – Protocols and Models
3.0 – Introduction
3.0.3 – Class Activity – Design a Communications System

## Slide 42
Purpose: Identifying and locating devices on a network.
Format: IPv4 addresses are typically written as four sets of numbers separated by dots (e.g., 192.168.1.1).
IP Address and Subnet Mask Overview
Week
02
www.midocean.ae
An IP (Internet Protocol) address is a numerical label assigned to each device connected to a computer network.
Purpose: Identifying and locating devices on a network.
Format: IPv4 addresses are typically written as four sets of numbers separated by dots (e.g., 192.168.1.1).
Subnet Mask Overview
Definition: A subnet mask is a 32-bit number that divides an IP address into network and host portions.
Purpose: Determines the network and host parts of an IP address.
Format: Similar to an IP address, written in the same dotted decimal format (e.g., 255.255.255.0).

## Slide 43
Device Address
Week
02
www.midocean.ae
⦿ Media Access Control (MAC) Address
A unique identifier assigned to a network interface controller for use as a network address in communications within a network segment. No two devices can have the same MAC address in the same local network; otherwise, an address conflict occurs. Example: 00-13-02-1F-58-F5
The first 3 bytes (24 bits) of the address
denote the vendor
⦿ Internet Protocol (IP) Address A unique string of characters that identifies each computer using the Internet Protocol to communicate over a network.
An IP address is a string of numbers
separated by periods (.) or colons (:)
Versions of IP Address:
⦿ IPV4 , ex: 192.168.1.1
⦿ IPV6, ex: 1050:0:0:0:5:600:300c:326b

## Slide 44
Protocols and Ports
Week
02
www.midocean.ae

## Slide 45
Open System Interconnection Layers
Week
02
www.midocean.ae

## Slide 46
OSI Layers
Week
02
www.midocean.ae

## Slide 47
OSI Layers
Week
02
www.midocean.ae

## Slide 48
OSI Layers
Week
02
www.midocean.ae

## Slide 49
OSI Layers
Week
01
www.midocean.ae

## Slide 50
OSI Layers
Week
01
www.midocean.ae

## Slide 51
Network Layers Models
Week
01
www.midocean.ae

## Slide 52
Thank You