## Slide 1
Network Fundamentals
CCNA (200-301) Cisco Certified Network Associate
Prepared by Eng. Taghreed Elsayed
Lecture 1

## Slide 2
Network Fundamentals
Chapter
01
server
printer
Network: A set of devices connected together via shared channel plus s/w to provide service of communication

## Slide 3
Network Fundamentals
Chapter
01
what are the benefits of network ?
Communication
Sharing resources
Cost
Modern technologies
Network components
H/W
NIC
Shared channels
devices
S/W
protocols
o.s

## Slide 4: Network types
Network Fundamentals
Chapter
01
Coverage Area
Topology
Sharing Resources

## Slide 5: Coverage Area
Network Fundamentals
Chapter
01

## Slide 6
Network Fundamentals
Chapter
01

## Slide 7
Network Fundamentals
Chapter
01

## Slide 8
Network Fundamentals
Chapter
01
The main difference between peer to peer and client server network is that in peer to peer network, each node can request for services and provide services while in client server network, the client nodes requests for services and server node responds with services.
The devices in a network communicate with each other. Peer to peer and client server are two network types. In a client server network, multiple clients connect to a server. The clients require services, and the server provides required services. On the other hand, in a peer to peer network, there are no specific clients or servers. Instead, all the nodes can act as clients or servers. In other words, each node can request for services and provides services.

## Slide 9
Network Fundamentals
Chapter
01
A bus topology consists of a main central cable or ‘backbone’ as it is called, with a terminator at each end. All devices like workstations, printers, routers, servers, etc., are connected to the main cable through nodes in a linear configuration. The terminator is used at the end of the cable to absorb the signal thus preventing signal bounce.

## Slide 10
Network Fundamentals
Chapter
01
A ring topology is a network configuration where device connections create a circular data path. Each networked device is connected to two others, like points on a circle. Together, devices in a ring topology are referred to as a ring network.
Ring topologies may be used in either LANs (local area networks) or WANs (wide area networks). Depending on the network card used in each computer of the ring topology, a coaxial cable or an RJ-45 network cable is used to connect computers together.

## Slide 11
Network Fundamentals
Chapter
01
Star topology
Star topologies are used in many networks, large and small.
In a star topology all nodes indirectly connect to each other through one or more switches. The switch acts as a central point through which all communications are passed.
Large networks using a star topology are usually controlled by one or more servers. Hence, the client-server model usually uses a star topology. However, peer-to-peer networks can also have a star topology. Even though no single computer controls the network, all communications still pass through the central switch
Mesh topology there is no central connection point. Instead, each node is connected to at least one other node and usually to more than one. Each node is capable of sending messages to and receiving messages from other nodes. The nodes act as relays, passing on a message towards its final destination.
There are two types of mesh topology:
full mesh topology
partial mesh topology
Mesh networks are becoming increasingly popular due to their efficiency.

## Slide 12
Network Fundamentals
Chapter
01
Hubs , Repeater: dump devices are sending signal to all hosts in network (broadcasting logical topology)
switches, bridges: straight forwarding devices are sending signal from source to destination in network (unicast logical topology)
source: sender
Destination: receiver

## Slide 13
Network Fundamentals
Chapter
01
Physical media
Cables types
1.Coaxial cables
2.Twisted pair: STP /UTP
3.Fiber optics
Types of Coaxial :core of coaxial
1.Thin : maximum distance of signal 185 m
2.Thick:: maximum distance of signal 500 m
both of them are used in bus topology with 10MBPS

## Slide 14
Network Fundamentals
Chapter
01
STP
UTP
The basic difference between UTP and STP is UTP (Unshielded twisted pair) is a cable with wires that are twisted together to reduce noise and crosstalk. On the contrary, STP (Shielded twisted pair) is a twisted pair cable confined in foil or mesh shield that guards the cable against electromagnetic interference.
Types of UTP cables
CAT3: Rarely used today, CAT3 is usually deployed in phone lines. ...
CAT4: Typically used in token ring networks, CAT4 supports 16 Mbps for up to 100 meters.
CAT5: Used in Ethernet-based LANs, CAT5 contains two twisted pairs. ...
CAT5e: Used in Ethernet-based LANs, CAT5e contains four twisted pairs.

## Slide 15
Network Fundamentals
Chapter
01
Fiber optics
Fiber optics is the technology used to transmit information as pulses of light through strands of fiber made of glass or plastic over long distances.
There are several different types of fiber-optic networks but they all begin with optic cables running from the network hub to the curb near your home or straight to your home to provide a fiber-optic internet connection. The fastest type of fiber network is called Fiber to the Home (FTTH) or Fiber to the Premises (FTTP) because it’s a 100% fiber-optic connection with optical fiber cables installed to terminals directly connected to houses, apartment buildings and businesses.

## Slide 16: (OSI Model)
Network Fundamentals
Chapter
01

## Slide 17: (OSI Model)
Network Fundamentals
Chapter
01

## Slide 18
Network Fundamentals (OSI Model)
Chapter
01
7. Application Layer
The application layer is used by end-user software such as web browsers and email clients. It provides protocols that allow software to send and receive information and present meaningful data to users. A few examples of application layer protocols are the Hypertext Transfer Protocol (HTTP), File Transfer Protocol (FTP), Post Office Protocol (POP), Simple Mail Transfer Protocol (SMTP), and Domain Name System (DNS).
6. Presentation Layer
The presentation layer prepares data for the application layer. It defines how two devices should encode, encrypt, and compress data so it is received correctly on the other end. The presentation layer takes any data transmitted by the application layer and prepares it for transmission over the session layer.

## Slide 19
Network Fundamentals (OSI Model)
Chapter
01
7. Application Layer
The application layer is used by end-user software such as web browsers and email clients. It provides protocols that allow software to send and receive information and present meaningful data to users. A few examples of application layer protocols are the Hypertext Transfer Protocol (HTTP), File Transfer Protocol (FTP), Post Office Protocol (POP), Simple Mail Transfer Protocol (SMTP), and Domain Name System (DNS).
6. Presentation Layer
The presentation layer prepares data for the application layer. It defines how two devices should encode, encrypt, and compress data so it is received correctly on the other end. The presentation layer takes any data transmitted by the application layer and prepares it for transmission over the session layer.

## Slide 20
Network Fundamentals / OSI Model(Encapsulation data)
Chapter
01

## Slide 21
Network Fundamentals (OSI Model)
Chapter
01

## Slide 22
Network Fundamentals (OSI Model)
Chapter
01
De capsulation data

## Slide 23
NetworNetwork Fundamentals (OSI Model)
Chapter
01
7. Application Layer
The application layer is used by end-user software such as web browsers and email clients. It provides protocols that allow software to send and receive information and present meaningful data to users. A few examples of application layer protocols are the Hypertext Transfer Protocol (HTTP), File Transfer Protocol (FTP), Post Office Protocol (POP), Simple Mail Transfer Protocol (SMTP), and Domain Name System (DNS).
6. Presentation Layer
The presentation layer prepares data for the application layer. It defines how two devices should encode, encrypt, and compress data so it is received correctly on the other end. The presentation layer takes any data transmitted by the application layer and prepares it for transmission over the session layer.

## Slide 24
NetworNetwork Fundamentals (OSI Model)
Chapter
01
Domain Name System
The Domain Name System (DNS) works on Client Server model. It uses UDP protocol for transport layer communication. DNS uses hierarchical domain based naming scheme. The DNS server is configured with Fully Qualified Domain Names (FQDN) and email addresses mapped with their respective Internet Protocol addresses.
A DNS server is requested with FQDN and it responds back with the IP address mapped with it. DNS uses UDP port 53.
Simple Mail Transfer Protocol
The Simple Mail Transfer Protocol (SMTP) is used to transfer electronic mail from one user to another. This task is done by means of email client software (User Agents) the user is using. User Agents help the user to type and format the email and store it until internet is available. When an email is submitted to send, the sending process is handled by Message Transfer Agent which is normally comes inbuilt in email client software.

## Slide 25
NetworNetwork Fundamentals (OSI Model)
Chapter
01
Hyper Text Transfer Protocol (HTTP)
The Hyper Text Transfer Protocol (HTTP) is the foundation of World Wide Web. Hypertext is well organized documentation system which uses hyperlinks to link the pages in the text documents. HTTP works on client server model. When a user wants to access any HTTP page on the internet, the client machine at user end initiates a TCP connection to server on port 80. When the server accepts the client request, the client is authorized to access web pages.
To access the web pages, a client normally uses web browsers, who are responsible for initiating, maintaining, and closing TCP connections. HTTP is a stateless protocol, which means the Server maintains no information about earlier requests by clients.
HTTP versions
HTTP 1.0 uses non persistent HTTP
HTTP 1.1 uses persistent HTTP. In this version, multiple objects can be sent over a single TCP connection.

## Slide 26
Network Fundamentals (OSI Model)
Chapter
01

## Slide 27
Network Fundamentals (OSI Model)
Chapter
01
5. Session Layer
The session layer creates communication channels, called sessions, between devices. It is responsible for opening sessions, ensuring they remain open and functional while data is being transferred, and closing them when communication ends. The session layer can also set checkpoints during a data transfer—if the session is interrupted, devices can resume data transfer from the last checkpoint.
4. Transport Layer
The transport layer takes data transferred in the session layer and breaks it into “segments” on the transmitting end. It is responsible for reassembling the segments on the receiving end, turning it back into data that can be used by the session layer. The transport layer carries out flow control, sending data at a rate that matches the connection speed of the receiving device, and error control, checking if data was received incorrectly and if not, requesting it again.

## Slide 28
Network Fundamentals (OSI Model)
Chapter
01

## Slide 29
Network Fundamentals (OSI Model)
Chapter
01
TCP header

## Slide 30
Network Fundamentals (OSI Model)
Chapter
01
UDP header

## Slide 31
Network Fundamentals (OSI Model)
Chapter
01
UDP header
UDP has a number of benefits for different types of applications, including:
No retransmission delays – UDP is suitable for time-sensitive applications that can’t afford retransmission delays for dropped packets. Examples include Voice over IP (VoIP), online games, and media streaming.
Speed – UDP’s speed makes it useful for query-response protocols such as DNS, in which data packets are small and transactional.
Suitable for broadcasts – UDP’s lack of end-to-end communication makes it suitable for broadcasts, in which transmitted data packets are addressed as receivable by all devices on the internet. UDP broadcasts can be received by large numbers of clients without server-side overhead.

## Slide 32: 3. Network Layer The network layer has two main functions. One is breaking up segments into network packets, and reassembling the packets on the receiving end. The other is routing packets by discovering the best path across a physical network. The network layer uses network addresses (typically Internet Protocol addresses) to route packets to a destination node. Protocols (IP,ARP and ICMP). 2. Data Link Layer The data link layer establishes and terminates a connection between two physically-connected nodes on a network. It breaks up packets into frames and sends them from source to destination. This layer is composed of two parts—Logical Link Control (LLC), which identifies network protocols, performs error checking and synchronizes frames, and Media Access Control (MAC) which uses MAC addresses to connect devices and define permissions to transmit and receive data.
Chapter
01
Network Fundamentals (OSI Model)

## Slide 33: Data link layer and error detection The data link layer ensures an initial connection has been set up, divides output data into data frames and handles the acknowledgements from a receiver that the data arrived successfully. It also ensures incoming data has been received successfully by analyzing bit patterns at special places in the frames. If an error occurs, the data link layer notifies higher-level protocols that something has happened to the physical link. Frame sequencing capabilities within the data link layer permit the receiving device to reorder frames that might have been transmitted out of sequence. The data link layer verifies the packet is unimpaired. The data link layer also manages flows by enabling devices on a link to detect congestion. Nearby devices then transmit congestion information, so traffic can be rerouted accordingly
Chapter
01
Network Fundamentals (OSI Model)

## Slide 34
Chapter
01
Network Fundamentals (OSI Model)
What is a MAC Address
Whether you work in a wired network office or a wireless one, one thing is common for both
environments: It takes both network software and hardware (cables, routers, etc.) to transfer data
from your computer to another—or from a computer thousands of miles away to yours.
And in the end, to get the data you want right to YOU, it comes down to addresses.
So not surprisingly, along with an IP address (which is networks software), there’s also a
hardware address. Typically it is tied to a key connection device in your computer called the
network interface card, or NIC. The NIC is essentially a computer circuit card that makes it possible for your computer to connect to a network.
A NIC turns data into an electrical signal that can be transmitted over the network.

## Slide 35
Chapter
01
Network Fundamentals (OSI Model)
1. Physical Layer The physical layer is responsible for the physical cable or wireless connection between network nodes. It defines the connector, the electrical cable or wireless technology connecting the devices, and is responsible for transmission of the raw data, which is simply a series of 0s and 1s, while taking care of bit rate control.

## Slide 36
Thanks