## Slide 1
Prepared by Dr. Khaled Eskaf
Human-Robot Interaction and Autonomous Systems
Lecture 6
AI 616
Master of Science in Artificial intelligence

## Slide 2
www.midocean.ae

## Slide 3
Chapter
03
www.midocean.ae

## Slide 4
Chapter
05
www.midocean.ae

## Slide 5
Chapter
05
www.midocean.ae
Tutorial 1: Moving the Robot Forward
Objective: Learn how to initialize your robot and make it move forward.
Step 1: Setting Up Your Webots Project
Open Webots and create a new project.
Add an e-puck robot to your scene from the Webots library.
Step 2: Creating Your Controller
Navigate to File > New > New Robot Controller....
Name your controller move_forward.
Select Python as the programming language and confirm.
Step 3: Writing the Controller Code
Open the move_forward.py file generated by Webots and follow along:

## Slide 6
Chapter
05
www.midocean.ae
This code initializes the robot but doesn't yet move it. Let's proceed to add movement.

## Slide 7
Chapter
05
www.midocean.ae
Example 1:
# Import the Robot class to interact with the robot
from controller import Robot
# Create a robot instance to control it
robot = Robot()
# Define the simulation step time
TIME_STEP = 64
# Main control loop
while robot.step(TIME_STEP) != -1:
# This loop runs until the simulation is stopped
pass # We will add movement code in the next tutorial
Example 2:
# Import the Motor class to control the wheels
from controller import Robot, Motor
# Initialization steps as before
# Retrieve motor devices
leftMotor = robot.getDevice('left wheel motor')
rightMotor = robot.getDevice('right wheel motor')
# Set the motors to velocity control mode
leftMotor.setPosition(float('inf'))
rightMotor.setPosition(float('inf'))
# Define a forward speed
FORWARD_SPEED = 6.28
# Apply the speed to both motors to move forward
leftMotor.setVelocity(FORWARD_SPEED)
rightMotor.setVelocity(FORWARD_SPEED)
# Main control loop
while robot.step(TIME_STEP) != -1:
# This loop runs until the simulation is stopped
pass # We will add movement code in the next tutorial

## Slide 8
Chapter
05
www.midocean.ae
Tutorial 2: Avoiding Obstacles Using a Front Infrared Sensor
Objective: Modify the robot's behavior to stop when an obstacle is detected.
Step 1: Enhancements to the Controller
Build upon the move_forward controller by adding sensor functionality to detect obstacles.

## Slide 9
Chapter
05
www.midocean.ae
Controller programming requires some information related to the e-puck model. In order to create the collision avoidance algorithm, we need to read the values of its 8 infra-red distance sensors located around its turret, and we need to actuate its two wheels. The way that the distance sensors are distributed around the turret and the e-puck direction are depicted in this figure.

## Slide 10
Chapter
05
www.midocean.ae
# Import necessary classes
from controller import Robot, Motor, DistanceSensor
# Initialization steps as before
# Initialize the front distance sensor
frontSensor = robot.getDevice('ps0')
frontSensor.enable(TIME_STEP)
# Control loop
while robot.step(TIME_STEP) != -1:
# Read the sensor value
distance = frontSensor.getValue()
# Check for obstacles
if distance < 800: # Adjust based on your environment
# An obstacle is detected, stop the robot
leftMotor.setVelocity(0)
rightMotor.setVelocity(0)
else:
# No obstacle, move forward
leftMotor.setVelocity(FORWARD_SPEED)
rightMotor.setVelocity(FORWARD_SPEED)

## Slide 11
Chapter
05
www.midocean.ae

## Slide 12
www.midocean.ae
from controller import Robot, Motor, DistanceSensor
TIME_STEP = 64
MAX_SPEED = 6.28 # Adjusting MAX_SPEED for realism, assuming it's in radians/sec which is typical in simulations
# create the Robot instance.
robot = Robot()
# get a handler to the motors and set target position to infinity (speed control)
leftMotor = robot.getDevice('left wheel motor')
rightMotor = robot.getDevice('right wheel motor')
leftMotor.setPosition(float('inf'))
rightMotor.setPosition(float('inf'))
# Initialize and enable the distance sensor
distanceSensor = robot.getDevice('ps0') # Assuming 'sp0' is the correct sensor name
distanceSensor.enable(TIME_STEP)
# set up the motor speeds at 10% of the MAX_SPEED.
leftMotor.setVelocity(0.1 * MAX_SPEED)
rightMotor.setVelocity(0.1 * MAX_SPEED)
while robot.step(TIME_STEP) != -1:
# Read the sensor value
distance = distanceSensor.getValue()
print(distance)
# Check for obstacles - assuming a threshold value for when to stop
# You may need to adjust the threshold based on your simulation environment
if distance < 62: # Example threshold value, adjust based on your sensor's range and sensitivity
# An obstacle is detected, stop the robot
leftMotor.setVelocity( MAX_SPEED)
rightMotor.setVelocity(0)
else:
# No obstacle, continue moving forward
leftMotor.setVelocity(0.1 * MAX_SPEED)
rightMotor.setVelocity(0.1 * MAX_SPEED)

## Slide 13
Chapter
05
www.midocean.ae
The concepts of HRI efficiency and effectiveness metrics for mission effectiveness and human factors.
Metrics for Mission Effectiveness
مقاييس فعالية المهمة
Notes: مقاييس فعالية المهمة
مفاهيم مقاييس كفاءة وفعالية HRI لفعالية المهمة والعوامل البشرية.

## Slide 14
Chapter
05
www.midocean.ae
How Fast Robots and Humans Complete Tasks Together:
Explanation: Checking if a robot and human can finish a job quickly, like cleaning up a room.
Example: If a robot helps a human clean a room and they finish in 30 minutes instead of an hour, that’s good and means they work well together.
Notes: التحقق من قدرة الروبوت والإنسان على إنهاء المهمة بسرعة، مثل تنظيف الغرفة.مثال: إذا ساعد الروبوت إنسانًا في تنظيف الغرفة وانتهى في 30 دقيقة بدلاً من ساعة، فهذا أمر جيد ويعني أنهما يعملان معًا بشكل جيد.

## Slide 15
Chapter
05
www.midocean.ae
Doing the Right Job:
Explanation: Making sure the robot does its part of the job correctly, like a robot that sorts books by color without mistakes.
Example: A robot helps sort red and blue books into separate boxes. If it puts all the books in the right boxes without mixing them up, it’s doing a great job.

## Slide 16
Chapter
05
www.midocean.ae
Robots Working on Their Own:
Explanation: Seeing if the robot can do tasks by itself without needing a human to tell it what to do every time.
Example: A robot vacuum cleans the floors by itself every day without someone having to start it each time.
Notes: الروبوتات تعمل بمفردها:الشرح: معرفة ما إذا كان الروبوت يستطيع القيام بالمهام بنفسه دون الحاجة إلى إنسان ليخبره بما يجب عليه فعله في كل مرة.مثال: تقوم المكنسة الكهربائية الروبوتية بتنظيف الأرضيات بنفسها كل يوم دون أن يضطر أحد إلى تشغيلها في كل مرة.

## Slide 17
Chapter
05
www.midocean.ae
Changing Plans When Needed:
Explanation: The robot can change what it’s doing based on new situations, like avoiding spilled juice on the floor it didn’t know was there.
Example: If a robot is delivering mail indoors and finds a hallway blocked, it figures out a different way to go on its own.
Notes: تغيير الخطط عند الحاجة:الشرح: يستطيع الروبوت تغيير ما يفعله بناءً على المواقف الجديدة، مثل تجنب العصير المسكوب على الأرض والذي لم يكن يعلم بوجوده.مثال: إذا كان الروبوت يقوم بتسليم البريد في الداخل ووجد ممرًا مسدودًا، فإنه يكتشف طريقة مختلفة للمضي قدمًا بمفرده.

## Slide 18
Chapter
05
www.midocean.ae
Keeping the Robot Busy:
Explanation: Making sure the robot has tasks to do so it’s not just sitting around unused.
Example: A robot in a store helps customers find items, clean up, and restock shelves all day instead of standing idle.
Notes: إبقاء الروبوت مشغولاً:الشرح: التأكد من أن الروبوت لديه مهام للقيام بها، بحيث لا يبقى فقط غير مستخدم.مثال: يساعد الروبوت الموجود في أحد المتاجر العملاء في العثور على العناصر وتنظيف الأرفف وإعادة تخزينها طوال اليوم بدلاً من الوقوف خاملاً.

## Slide 19
Chapter
05
www.midocean.ae
Metrics for Human Factors
How Happy People Are with the Robot:
Explanation: After working with the robot, people feel good about it and think it’s helpful.
Example: After using a robot assistant in class, students feel it’s fun and helps them learn better.
Notes: مقاييس العوامل البشرية
مدى سعادة الناس مع الروبوت:شرح سهل: بعد العمل مع الروبوت، يشعر الناس بالرضا تجاهه ويعتقدون أنه مفيد.مثال: بعد استخدام مساعد الروبوت في الفصل، يشعر الطلاب بأنه ممتع ويساعدهم على التعلم بشكل أفضل.

## Slide 20
Chapter
05
www.midocean.ae
Thinking Hard?:
Explanation: Checking if using the robot makes people feel stressed or tired from thinking too much.
Example: If a teacher uses a robot to grade tests and finds it easy to use without getting a headache, that’s great.
Notes: تفكير صعب؟:شرح سهل: التحقق مما إذا كان استخدام الروبوت يجعل الناس يشعرون بالتوتر أو التعب من التفكير أكثر من اللازم.مثال: إذا كان المعلم يستخدم الروبوت لتقدير الاختبارات ويجد أنه سهل الاستخدام دون الإصابة بالصداع، فهذا أمر رائع.

## Slide 21
Chapter
05
www.midocean.ae
Trusting the Robot:
Explanation: People believe the robot will do its job well and not make mistakes.
Example: A family trusts their robot pet sitter to feed and play with their cat correctly when they are not home.
Notes: الثقة بالروبوت:شرح سهل: يعتقد الناس أن الروبوت سيقوم بعمله بشكل جيد ولن يرتكب أي أخطاء.مثال: تثق إحدى العائلات في الروبوت الخاص بجليسة الحيوانات الأليفة لإطعام قطتها واللعب معها بشكل صحيح عندما لا تكون في المنزل.

## Slide 22
Chapter
05
www.midocean.ae
Learning to Use the Robot:
Explanation: Finding out if it’s easy and quick for someone to learn how to work with the robot.
Example: If someone can start using a robot to make coffee after a quick lesson, that means it’s easy to learn.
Notes: تعلم استخدام الروبوت:شرح سهل: معرفة ما إذا كان من السهل والسريع أن يتعلم شخص ما كيفية العمل مع الروبوت.مثال: إذا تمكن شخص ما من البدء في استخدام الروبوت لإعداد القهوة بعد درس سريع، فهذا يعني أنه من السهل التعلم.

## Slide 23
Chapter
05
www.midocean.ae
Making Human Jobs Easier:
Explanation: The robot takes over tasks that are hard or boring, so people can do other important things.
Example: A robot takes over cleaning the floors at a restaurant, so the staff can spend more time making meals and helping customers.
Notes: جعل الوظائف البشرية أسهل:شرح سهل: يتولى الروبوت المهام الصعبة أو المملة، حتى يتمكن الأشخاص من القيام بأشياء مهمة أخرى.مثال: يتولى الروبوت تنظيف الأرضيات في أحد المطاعم، حتى يتمكن الموظفون من قضاء المزيد من الوقت في إعداد وجبات الطعام ومساعدة العملاء.

## Slide 24
Chapter
06
www.midocean.ae

## Slide 25
Chapter
06
www.midocean.ae
e-puck robot

## Slide 26
Chapter
06
www.midocean.ae
Tutorial 3: Using Multiple Infrared Sensors for Enhanced Obstacle Avoidance
Objective: Expand obstacle detection to utilize multiple infrared sensors for more nuanced navigation.
Step 1: Controller Expansion for Multiple Sensors
Enhance the controller to read from multiple sensors and react accordingly.

## Slide 27
Chapter
06
www.midocean.ae
Controller programming requires some information related to the e-puck model. In order to create the collision avoidance algorithm, we need to read the values of its 8 infra-red distance sensors located around its turret, and we need to actuate its two wheels. The way that the distance sensors are distributed around the turret and the e-puck direction are depicted in this figure.

## Slide 28
Chapter
06
www.midocean.ae
Obstacle detection and navigation

## Slide 29
# Import necessary classes for the robot control
from controller import Robot, Motor, DistanceSensor
# Initialize the Robot instance
robot = Robot()
# Define the time step of the robot's control loop
TIME_STEP = 64
# Initialize motor devices
leftMotor = robot.getDevice('left wheel motor')
rightMotor = robot.getDevice('right wheel motor’)
# Set to infinite position mode
leftMotor.setPosition(float('inf'))
rightMotor.setPosition(float('inf’))
# Initial velocity
leftMotor.setVelocity(0.0)
rightMotor.setVelocity(0.0)
# Speed constants
FORWARD_SPEED = 5.0
# Initialize multiple distance sensors by their names
sensors = ['ps0', 'ps1', 'ps2', 'ps7']
sensorObjects = []
for sensorName in sensors:
sensor = robot.getDevice(sensorName) # Get the sensor device
sensor.enable(TIME_STEP) # Enable the sensor with the defined time step
sensorObjects.append(sensor) # Append the sensor object to the list
# Control loop: execute at each simulation step
while robot.step(TIME_STEP) != -1:
# Read sensor values into a list
sensorValues = [sensor.getValue() for sensor in sensorObjects]
# Basic obstacle detection and navigation strategy
if sensorValues[0] < 70 or sensorValues[1] < 70:
# Obstacle detected in front or front-right: turn left
leftMotor.setVelocity(-FORWARD_SPEED)
rightMotor.setVelocity(FORWARD_SPEED)
elif sensorValues[3] < 800:
# Obstacle detected in front-left: turn right
leftMotor.setVelocity(FORWARD_SPEED)
rightMotor.setVelocity(-FORWARD_SPEED)
else:
# No obstacle detected: move forward
leftMotor.setVelocity(FORWARD_SPEED)
rightMotor.setVelocity(FORWARD_SPEED)

## Slide 30
Chapter
06
www.midocean.ae
Initializing multiple distance sensors on a robot

## Slide 31
Chapter
06
www.midocean.ae
Explain the process of reading sensor values into a list
sensorValues = [sensor.getValue() for sensor in sensorObjects]

## Slide 32
Chapter
06
www.midocean.ae
The obstacle detection and navigation strategy uses sensor readings to control the robot's movement. When sensors 0 or 1 detect an obstacle (values below 800), indicating something in front or to the front-right, the robot turns left by setting a negative velocity for the left motor and a positive velocity for the right motor. If sensor 3 detects an obstacle, implying an obstruction is to the front-left, it turns right by reversing these velocities. If no obstacles are detected, both motors propel the robot forward at the same speed. This basic logic helps the robot navigate by avoiding collisions.

## Slide 33
Chapter
06

## Slide 34
Chapter
06
www.midocean.ae
Robot that flashes its LED red and white three times before turning right when it detects an obstacle.

## Slide 35
Chapter
# Function to flash LED three times
def flashLED(led):
for _ in range(3):
led.set(1) # Turn LED red
robot.step(TIME_STEP)
led.set(0) # Turn LED off (or white if your robot supports it)
robot.step(TIME_STEP)
# Main control loop
while robot.step(TIME_STEP) != -1:
# Read sensor values
value0 = sensor0.getValue()
value7 = sensor7.getValue()
# Check if there is an obstacle in front
if value0 < 70 and value7 < 70:
flashLED(led) # Flash LED if obstacle is detected
# Turn right
leftMotor.setVelocity(5) # Adjust velocity to turn the robot
rightMotor.setVelocity(-5)
else:
# Move forward if no obstacle
leftMotor.setVelocity(5)
rightMotor.setVelocity(5)
from controller import Robot, LED, DistanceSensor
# Initialize the robot
robot = Robot()
# Define the time step
TIME_STEP = 64
# Initialize the LEDs on the robot
led = robot.getDevice('led0') # Assuming the robot has an LED named 'led0'
# Initialize the distance sensors
sensor0 = robot.getDevice('ps0')
sensor7 = robot.getDevice('ps7')
sensor0.enable(TIME_STEP)
sensor7.enable(TIME_STEP)
# Initialize motors, assuming the robot has motors named 'left wheel motor' and 'right wheel motor'
leftMotor = robot.getDevice('left wheel motor')
rightMotor = robot.getDevice('right wheel motor')
leftMotor.setPosition(float('inf'))
rightMotor.setPosition(float('inf'))
leftMotor.setVelocity(0)
rightMotor.setVelocity(0)

## Slide 36
Chapter
06
www.midocean.ae
E-puck robot can use its camera to capture an image and analyze the color of the central pixel in the Webots simulation environment.

## Slide 37
# Retrieve the width and height of the camera image.
# These values are set in the Webots world file and can be used to process the image.
cameraWidth = camera.getWidth()
cameraHeight = camera.getHeight()
print(f"Captured an image of size: {cameraWidth}x{cameraHeight}")
# Calculate the position of the central pixel in the image.
# We divide the width and height by 2 to find the center.
centerX = cameraWidth // 2
centerY = cameraHeight // 2
# Get the RGB color values of the central pixel.
# imageGetRed, imageGetGreen, and imageGetBlue methods are used to extract
# the color components of a pixel at a specified position.
red = camera.imageGetRed(image, cameraWidth, centerX, centerY)
green = camera.imageGetGreen(image, cameraWidth, centerX, centerY)
blue = camera.imageGetBlue(image, cameraWidth, centerX, centerY)
# Print the RGB color values of the central pixel.
# This can be useful for tasks like color detection or analysis.
print(f"Color of the central pixel: R={red}, G={green}, B={blue}")
# Import necessary modules from the Webots library.
# Robot is the main class for robot control.
# Camera is for accessing the robot's camera.
from controller import Robot, Camera
# Define the simulation time step in milliseconds.
# This is how often the simulation updates the robot's sensors and actuators.
TIME_STEP = 64
# Create an instance of the Robot class.
# This will be our main handle to interact with the robot.
robot = Robot()
# Get a handle to the camera device on the robot.
# 'camera' is the name of the camera device specified in the robot's model.
# If the camera has a different name in your project, change 'camera' accordingly.
camera = robot.getDevice('camera')
# Enable the camera to start capturing images.
# The camera will update its image every TIME_STEP milliseconds.
camera.enable(TIME_STEP)
# Main loop: Execute actions repeatedly until the simulation is stopped.
while robot.step(TIME_STEP) != -1:
# Capture an image from the camera.
# The getImage() method returns the latest image captured by the camera.
image = camera.getImage()

## Slide 38
Chapter
06
www.midocean.ae

## Slide 39
Chapter
06
www.midocean.ae
"Innovative Designs and Real-World Applications of Robotics and AI"
Notes: "التصاميم المبتكرة والتطبيقات الواقعية للروبوتات والذكاء الاصطناعي"

## Slide 40
Chapter
06
www.midocean.ae
Robotic Surgery: Surgical robots, like the da Vinci Surgical System, allow surgeons to perform complex procedures with more precision, flexibility, and control than traditional techniques. These robots offer minimally invasive options, reducing recovery time and improving patient outcomes.
Healthcare:
Notes: الجراحة الروبوتية: تسمح الروبوتات الجراحية، مثل نظام دافنشي الجراحي، للجراحين بإجراء عمليات معقدة بدقة ومرونة وتحكم أكبر من التقنيات التقليدية. توفر هذه الروبوتات خيارات طفيفة التوغل، مما يقلل من وقت التعافي ويحسن نتائج المرضى.

## Slide 41
Chapter
06
www.midocean.ae
2.Care Robots: Robots designed for care settings assist with tasks ranging from patient monitoring to delivering therapy, helping to alleviate the workload on human caregivers and enhancing patient care.
Healthcare:
Notes: روبوتات الرعاية: تساعد الروبوتات المصممة لإعدادات الرعاية في مهام تتراوح بين مراقبة المريض وتقديم العلاج، مما يساعد على تخفيف عبء العمل على مقدمي الرعاية البشرية وتعزيز رعاية المرضى.

## Slide 42
Chapter
06
www.midocean.ae
Agriculture
Agricultural Drones and Robots: These technologies revolutionize farming practices by providing detailed aerial views that help in crop monitoring, health assessment, and targeted pesticide spraying. Ground-based robots automate tasks like weeding, planting, and harvesting.
Notes: زراعة:
الطائرات بدون طيار والروبوتات الزراعية: تُحدث هذه التقنيات ثورة في الممارسات الزراعية من خلال توفير مناظر جوية مفصلة تساعد في مراقبة المحاصيل وتقييم الصحة ورش المبيدات الحشرية المستهدفة. تعمل الروبوتات الأرضية على أتمتة المهام مثل إزالة الأعشاب والزراعة والحصاد.

## Slide 43
Chapter
06
www.midocean.ae
Agriculture
Precision Agriculture: AI-driven analysis of data collected from sensors and drones enables farmers to make informed decisions about water management, crop rotation, and optimal planting strategies, leading to increased crop yield and sustainability.
Notes: الزراعة الدقيقة: يتيح التحليل المعتمد على الذكاء الاصطناعي للبيانات المجمعة من أجهزة الاستشعار والطائرات بدون طيار للمزارعين اتخاذ قرارات مستنيرة بشأن إدارة المياه وتناوب المحاصيل واستراتيجيات الزراعة المثالية، مما يؤدي إلى زيادة إنتاجية المحاصيل واستدامتها.

## Slide 44
Chapter
06
www.midocean.ae
Environmental Conservation
Wildlife Conservation: AI algorithms analyze images and data from camera traps to monitor wildlife, track poaching activities, and study biodiversity, contributing to conservation efforts.
Notes: الحفاظ على البيئة:
الحفاظ على الحياة البرية: تقوم خوارزميات الذكاء الاصطناعي بتحليل الصور والبيانات من مصائد الكاميرا لمراقبة الحياة البرية، وتتبع أنشطة الصيد غير المشروع، ودراسة التنوع البيولوجي، مما يساهم في جهود الحفاظ على الحياة البرية.

## Slide 45
Chapter
06
www.midocean.ae
Ocean Cleanup: Innovative robotic systems are deployed to collect plastic and other waste from oceans and rivers, addressing the critical issue of water pollution.
Notes: تنظيف المحيطات: يتم نشر أنظمة روبوتية مبتكرة لجمع النفايات البلاستيكية وغيرها من النفايات من المحيطات والأنهار، لمعالجة القضية الحاسمة المتمثلة في تلوث المياه.

## Slide 46
Chapter
06
www.midocean.ae
Education
Educational Robots: Robots serve as teaching assistants or learning platforms, offering interactive and personalized learning experiences. They help in teaching coding, STEM subjects, and languages, making education more engaging.
Notes: الروبوتات التعليمية: تعمل الروبوتات كمساعدين تدريس أو منصات تعليمية، حيث تقدم تجارب تعليمية تفاعلية وشخصية. فهي تساعد في تدريس البرمجة وموضوعات العلوم والتكنولوجيا والهندسة والرياضيات واللغات، مما يجعل التعليم أكثر جاذبية.

## Slide 47
Chapter
06
www.midocean.ae
Smart Cities
Traffic Management: AI-driven traffic control systems analyze real-time data to optimize traffic flow, reduce congestion, and improve road safety.

## Slide 48
Chapter
06
www.midocean.ae
Waste Management: Smart waste collection systems use sensors to monitor trash levels and optimize collection routes, improving efficiency and cleanliness.
Notes: إدارة النفايات: تستخدم أنظمة جمع النفايات الذكية أجهزة استشعار لمراقبة مستويات النفايات وتحسين طرق التجميع، مما يؤدي إلى تحسين الكفاءة والنظافة.

## Slide 49
Thank You

## Slide 50
Chapter
06
www.midocean.ae