## Slide 1
Computer Networks
Eng. Eman Hamdy
IT111 - Introduction to Information Technology

## Slide 2
Describe local and wide area networks (LANs and Wans).
Distinguish an internet from the Internet.
Describe the TCP/IP protocol suite as the network model in the internet.
Define the layers in the TCP/IP protocol suite and their relationship.
Objectives

## Slide 3
Introduction
A network is a combination of hardware and software that sends data from one location to another.
The hardware consists of the physical equipment that carries signals from one point in the network to another.
The software consists of instructions that make the services that we expect from a network possible.
6.1 Introduction

## Slide 4
A network is the interconnection of devices capable of communication.
A device can be a host (such as a computer, desktop, laptop, workstation, mobile phone, or security system) and can be a connecting device such as a router connecting the network to other networks, a switch which connects devices together, a modem (modulator-demodulator) that changes the form of data, etc.
These devices in a network are connected using wired or wireless transmission media.
When connecting two computers, we have created a network, although very small.
6.1.1 Networks

## Slide 5
A point-to-point connection provides a dedicated link between two devices, and the entire capacity of the link is reserved for transmission between these two devices.
A multipoint connection (also called multidrop connection) is one in which more than two specific devices share a single link (Figure 6.1.b). In a multipoint environment, the capacity of the channel is shared, either spatially or temporally.
Type of Connection
Type of Connection
Notes: يوفر الاتصال من نقطة إلى نقطة ارتباطًا مخصصًا بين جهازين ، ويتم حجز السعة الكاملة للرابط للإرسال بين هذين الجهازين.
الاتصال متعدد النقاط اتصال متعدد النقاط (يسمى أيضًااتصال متعدد المحطات) هو أحد الأجهزة التي يشترك فيها أكثر من جهازين محددين في ارتباط واحد (الشكل 6.1.ب). في بيئة متعددة النقاط ، يتم تقاسم سعة القناة ، إما مكانياً أو زمنياً.

## Slide 6
Physical topology
The term physical topology refers to the way in which a network is laid out physically. Two or more devices connect to a link; one or more links form a topology. The topology of a network is the geometric representation of the relationship of all the links and devices (usually called nodes) to one another. There are four basic topologies possible: mesh, star, bus and ring
Physical topology

## Slide 7
In a mesh topology, every device has a dedicated point-to-point link to every other device.
Mesh Topology
Mesh Topology
Notes: Each topology has its own advantages and disadvantages. A mesh guarantees that each connection can carry its own data load, eliminating traffic problems. It is also robust in the sense that if one link becomes unusable, it does not incapacitate the entire network.
The main disadvantages of a mesh topology are related to the amount of cabling and the number of input/output ports required.

## Slide 8
A bus topology uses a multipoint link. One long cable, called the bus, acts as a backbone to link all the devices in a network. Nodes are connected to the bus cable by drop lines and taps (connectors).
Bus Topology
Bus Topology
Notes: A bus topology can be easily installed. Backbone cable can be laid along the most efficient path, then connected to the nodes by drop lines of various lengths. However, a fault or break in the bus cable stops all transmission, even between devices on the same side of the problem section.

## Slide 9
In a ring topology, each device has a dedicated point-to-point connection with only the two devices on either side of it. A signal is passed along the ring in one direction, from device to device, until it reaches its destination. Each device in the ring incorporates a repeater. When a device receives a signal intended for another device, its repeater regenerates the bits and passes them along.
Ring Topology
Ring Topology
Notes: A ring is relatively easy to install and reconfigure. In addition, fault isolation is simplified. However, a break in the ring (such as a disabled station) can disable the entire network. This weakness can be solved by using a dual ring or a switch capable of closing off the break. Ring topology was prevalent when IBM introduced its local-area network Token Ring. Today, the need for higher-speed networks has made this topology less popular.

## Slide 10
In a star topology, each device has a dedicated point-to-point link only to a central controller, usually called a hub.
Star Topology
Start Topology
Notes: Today the most common topology in high-speed local-area networks is a star. A star topology is less expensive than a mesh topology, but has most of the advantages of the latter. One big disadvantage of a star topology is the dependency of the whole topology on one single point, the hub. If the hub goes down, the whole system is dead. However, the low cost of a star topology and ease of installation and scalability has made the star topology the only common topology.

## Slide 11
Categories of networks
Today networks can be divided into three broad categories:
Local-area networks (LANs): A LAN normally covers a small area, while a MAN covers a small city or town.
Wide-area networks (WANs): a WAN can be worldwide
Metropolitan area networks (MANs): a MAN covers a small city or town.
Categories of networks

## Slide 12
A local area network (LAN) is privately owned and connects hosts in a single office, building, or campus.
LANs can be as simple as two PCs and a printer in someone’s home office, or it can extend throughout a company and include audio and video devices.
Each host in a LAN has an identifier, an address, that uniquely defines them. A packet sent by a host to another carries both the source host’s and the destination host’s addresses.
Local area network

## Slide 13
A wide area network (WAN) is an interconnection of devices capable of communication.
Wide area network
Notes: Differences between LAN and WAN:
A LAN is limited in size, spanning an office, a building, or a campus; a WAN has a wider geographical span, spanning a town, a state, a country, or even the world.
A LAN interconnects hosts; a WAN interconnects connecting devices such as switches, routers, or modems.
A LAN is normally privately owned by the organization that uses it; a WAN is normally created and run by communication companies and leased by an organization that uses it.
A wide area network (WAN) provides long-distance transmission of data, images, audio as well as video information over large geographic areas that may comprise a country, a continent or even the whole world. A WAN can be as complex as the backbones that connect the internet or as simple as a dial-up line that connects a home computer to the internet. A point-to-point WAN is normally a single line connection between two devices such a dial-up line or a cable line. A backbone WAN is a complex network operated by a service provider and normally connects internet service providers (ISPs) (see Figure 6.4).

## Slide 14
Metropolitan Area Networks
A metropolitan area network (MAN) is a network with a size between a LAN and a WAN. It normally covers the area inside a town or a city. It is designed for customers who need high-speed connectivity, normally to the internet and has endpoints spread over a city or part of city. A good example of a MAN is that part of a telephone company’s network that can provide a high-speed DSL line to the customer. Another example is the cable television network that was originally designed for cable television but today can also be used for high-speed data connection to the internet.
Metropolitan Area Networks

## Slide 15
Today, it is very rare to see a network in isolation as networks are connected to one another. When two or more networks are connected, they become an internetwork, or an internet (lowercase ‘i’).
An example of an internet. In other words, a network is a group of connected communicating devices such as computers and printers while an internet is two or more networks that can communicate with each other.
An internet

## Slide 16
Seven LANs and two WANs.
Notes: Each LAN is a local network connecting computers, printers and other devices inside a building or a campus. The WANs are either point-to-point (a leased line, for example) or a backbone operated by a network service provider. The routers are connecting devices that route the packets (messages) travelling through the internet.

## Slide 17
An internet is two or more networks that can communicate with each other. The most notable is the Internet which is made of thousands of networks.
6.1.2 The Internet
6.1.2 The Internet

## Slide 18
It is difficult to give an accurate representation of the internet, because it is continually changing—new networks are being added and networks of defunct organizations removed. Today most end users who want an internet connection use the services of internet service providers (ISPs).
An ISP is an organization with one or more servers (high-capacity computers) that are connected to the internet through high-speed links. Individual internet users or small companies can be connected to the servers of a local ISP by establishing a service contract and paying a fee.

## Slide 19
There are:
international service providers,
national service providers,
regional service providers and
local service providers.
The internet today is run by private companies, not the government.

## Slide 21
For communication to happen both hardware and software are required.
This is similar to a complex computation in which both a computer and a program are needed.
These combinations are coordinated with each other using protocol layering.
6.1.3 Hardware and software
6.1.3 Hardware and software

## Slide 22
6.2 TCP/IP PROTOCOL SUITE
Compare this to a service provided by a computer network. For example, the task of sending an email from one place in the world to another can be broken down into several tasks, each performed by a layer. Each layer uses the services of a lower layer. At the lowest layer, a signal or a set of signals, is sent from the source computer to the destination computer.
6.2 TCP/IP PROTOCOL SUITE

## Slide 23
6.2 TCP/IP PROTOCOL SUITE
To divide the services required to perform a task, the internet has created a set of rules called protocols. These allow different local and wide area networks, using different technologies, to be connected together and carry a message from one point to another.
The set, or suite, of protocols that controls the internet today is referred to as the TCP/IP protocol suite. The abbreviations (TCP and IP) will become clear as we explain different protocols.
6.2 TCP/IP PROTOCOL SUITE

## Slide 24
6.2 TCP/IP PROTOCOL SUITE
The original TCP/IP protocol suite was defined as having four layers: host-to-network
(or link), internet (network), transport and application. However, the TCP/IP protocol suite today is normally considered as a five-layer model.
6.2 TCP/IP PROTOCOL SUITE

## Slide 25
6.2 TCP/IP PROTOCOL SUITE
Figure 6.8 shows the layers involved when a message is sent from device A to device
B. As the message travels from A to B, it may pass through many routers. Routers use only the first three layers. Within a single machine, each layer calls on the services of the layer immediately below it. Layer 3, for example, uses the services provided by layer 2 and provides services for layer 4.
6.2 TCP/IP PROTOCOL SUITE

## Slide 27
6.3 LAYERS
This section briefly describes the function of each layer in the TCP/IP protocol suite. We show how a message travels through the different layers until it reaches the physical layer and is sent by the transmission media.
6.3 LAYERS

## Slide 28
Modularity in this case means Independent layers. A layer (module) can be defined as a black box with inputs and outputs, without concern about how inputs are changed to outputs.
Note: If two machines provide the same outputs when given the same inputs, they can replace each other.
Advantages:
Separation of the services from the implementation. A layer needs to be able to receive a set of services from the lower layer and to give the services to the upper layer.
Communication does not always use only two end systems; there are intermediate systems that need only some layers, but not all layers. If we did not use protocol layering, we would have to make each intermediate system as complex as the end systems, which makes the whole system more expensive.
6.3 LAYERS
6.3 LAYERS

## Slide 29
6.3.1 Application layer
The application layer is responsible for providing services to the user.
The application layer enables a user, whether human or software, to access the network. It provides support for services such as electronic mail, remote file access and transfer, browsing the world wide web, and so on. The application layer is the only layer seen by most users of the internet.
6.3.1 Application layer

## Slide 30
Layer 4: Transport layer
Responsible for process-to-process delivery of the entire message.
A process is an application program running on a host.
It treats each packet as a separate message.
Layer 4: Transport layer

## Slide 31
Layer 3: Network layer
Responsible for the source-to-destination delivery of a packet, across multiple networks.
If two systems are connected to the same link (network), there is no need for a network layer.
Layer 3: Network layer

## Slide 32
The network layer is responsible for the delivery of individual packets from the source host to the destination host.
It also responsible for:
Logical addressing (IP) for destination outside the network
Routing : making decision based on the destination
Layer 3: Network layer
Layer 3: Network layer

## Slide 33
Source-to-destination delivery
Layer 3: Network layer
Layer 3: Network layer
Source-to-destination delivery

## Slide 34
Layer 2: Data link layer
Transforms the physical layer to a reliable link.
It make the physical layer appear error-free to the upper layer.
Layer 2: Data Link layer

## Slide 35
Hop-to-hop delivery
Layer 2: Data link layer
Layer 2: Data Link layer
Hop-to-hop delivery

## Slide 36
Layer 1: Physical layer
Coordinate the functions required to carry a bit stream over a physical medium.
It also defines the procedures and functions that physical devices and interfaces have to perform for transmission to occur.
Layer 1: Physical layer

## Slide 37
Layer 1: Physical layer
Layer 1: Physical layer
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.
It also responsible for:
Physical characteristics of interfaces and medium
Representation of bits (how 0,1 changes to signals)
Data rate (num of bits sent each second)
Synchronization of bits (using the same bit rate, same clock)
Line configuration (type of connection: P2P, multipoint)
Physical Topology (Bus/Star/Mesh/Ring)
Transmission mode (simplex/Duplex)

## Slide 38
Thank You