## Slide 1
Prepared by Dr. Khaled Eskaf
Human-Robot Interaction and Autonomous Systems
Lecture 8
AI 616
Master of Science in Artificial intelligence

## Slide 2
Chapter
06
www.midocean.ae

## Slide 3
Chapter
07
www.midocean.ae

## Slide 4
Chapter
07
www.midocean.ae
ADD Obstacle (ROCK) in Webots
+ > Add a node > PROTO nodes>Objects > search rocks >

## Slide 5
Chapter
07
www.midocean.ae
Click on the Arrows to move the object
Ctrl + V to copy paste the object
Change the color of Rock

## Slide 6
Chapter
07
www.midocean.ae
Epuck Camera with Color Object
1- Change the Location of the Gray Object to be in front of the Epuck Robot.
2- Read the RGB Values of the center of Camera

## Slide 7
# Assuming you've set the resolution in the Webots world file
cameraWidth = camera.getWidth()
cameraHeight = camera.getHeight()
print(f"Captured an image of size: {cameraWidth}x{cameraHeight}")
# Get the color of the central pixel
centerX = cameraWidth // 2
centerY = cameraHeight // 2
red = camera.imageGetRed(image, cameraWidth, centerX, centerY)
green = camera.imageGetGreen(image, cameraWidth, centerX, centerY)
blue = camera.imageGetBlue(image, cameraWidth, centerX, centerY)
print(f"Color of the central pixel: R={red}, G={green}, B={blue}")
from controller import Robot, Camera
# Time step definition
TIME_STEP = 64
# Create the Robot instance
robot = Robot()
# Initialize the camera and enable it
camera = robot.getDevice('camera')
camera.enable(TIME_STEP)
# Main control loop
while robot.step(TIME_STEP) != -1:
# Capture an image from the camera
image = camera.getImage()

## Slide 8
Chapter
07
www.midocean.ae
The output value of RGB: R=176 , G=173, B=174
Use any website to convert RGB values to Color:
https://www.w3schools.com/colors/colors_rgb.asp

## Slide 9
Chapter
07
www.midocean.ae

## Slide 10
Chapter
07
www.midocean.ae
Now Remove the gray object and let Epuck robot camera capture the red object

## Slide 11
Chapter
07
www.midocean.ae

## Slide 12
Chapter
07
www.midocean.ae
Epuck robot avoid RED obstacle using Camera

## Slide 13
# Import the necessary modules from the Webots API
from controller import Robot, Camera, Motor
# Set the time step of the simulation
TIME_STEP = 64
# Create a robot instance to interact with the robot
robot = Robot()
# Get the camera device, enable it, and set the timestep
camera = robot.getDevice('camera')
camera.enable(TIME_STEP)
# Get the motor devices
left_motor = robot.getDevice('left wheel motor')
right_motor = robot.getDevice('right wheel motor')
# Set the target position of the motors to infinity for velocity control
left_motor.setPosition(float('inf'))
right_motor.setPosition(float('inf'))
# Set the initial velocity of the motors to 0 (robot is stationary)
left_motor.setVelocity(0)
right_motor.setVelocity(0)

## Slide 14
# Main loop: this is where the robot's behavior is defined
while robot.step(TIME_STEP) != -1:
# Retrieve the image captured by the camera
image = camera.getImage()
# Get the width and height of the image from the camera's properties
width = camera.getWidth()
height = camera.getHeight()
# Calculate the central pixel's coordinates
centerX = width // 2
centerY = height // 2
# Get the red, green, and blue color components of the central pixel
red = camera.imageGetRed(image, width, centerX, centerY)
green = camera.imageGetGreen(image, width, centerX, centerY)
blue = camera.imageGetBlue(image, width, centerX, centerY)
print(f"Color of the central pixel: R={red}, G={green}, B={blue}")
# Define what we mean by 'red' (This can be adjusted as needed)
RED_THRESHOLD = 100
GREEN_THRESHOLD = 45
BLUE_THRESHOLD = 45
# Detect whether the central pixel is red enough
if red > RED_THRESHOLD and green < GREEN_THRESHOLD and blue < BLUE_THRESHOLD:
# If red enough, it means there's a red obstacle ahead, so turn right
left_motor.setVelocity(2) # positive speed turns the wheel forward
right_motor.setVelocity(-2) # negative speed turns the wheel backward
else:
# If not red enough, it means the path is clear, so move forward
left_motor.setVelocity(5)
right_motor.setVelocity(5)

## Slide 15
Chapter
07
www.midocean.ae
The ROBOT will move forward If the RED obstacle (ROCK) the Robot Turn Right, If the Obstacle BLUE the robot will move Backward.
Notes: 3

## Slide 16
Chapter
07
www.midocean.ae
Human-Robot Interaction (HRI) system classification
Human-Robot Interaction (HRI) system classification can be approached from several dimensions, reflecting the multifaceted nature of how humans and robots interact. The classification helps in understanding, designing, and evaluating HRI systems across various domains. Here’s an overview of common classification dimensions in HRI:
Objective: Classifying HRI systems provides a framework for understanding the diverse ways in which robots and humans can interact.
Notes: يمكن التعامل مع تصنيف نظام التفاعل بين الإنسان والروبوت (HRI) من عدة أبعاد، مما يعكس الطبيعة المتعددة الأوجه لكيفية تفاعل البشر والروبوتات. يساعد التصنيف في فهم وتصميم وتقييم أنظمة HRI عبر مختلف المجالات. فيما يلي نظرة عامة على أبعاد التصنيف الشائعة في
الهدف: يوفر تصنيف أنظمة HRI إطارًا لفهم الطرق المتنوعة التي يمكن أن يتفاعل بها الروبوتات والبشر.HRI:

## Slide 17
Chapter
07
www.midocean.ae
1. Type of Interaction
Teleoperation: The human operator controls the robot from a distance, often using a remote control interface. Applications include drone flying, remote surgery, and exploration in hazardous environments.
Notes: نوع التفاعل:
التشغيل عن بعد: يتحكم المشغل البشري في الروبوت من مسافة بعيدة، وغالبًا ما يستخدم واجهة التحكم عن بعد. وتشمل التطبيقات الطيران بدون طيار، والجراحة عن بعد، والاستكشاف في البيئات الخطرة.

## Slide 18
Chapter
07
www.midocean.ae
Autonomous Robots: Robots operate independently based on pre-programmed behaviors or AI-driven decisions, with minimal human intervention. Examples include autonomous household cleaning robots and self-driving vehicles.
Notes: الروبوتات المستقلة: تعمل الروبوتات بشكل مستقل بناءً على سلوكيات مبرمجة مسبقًا أو قرارات تعتمد على الذكاء الاصطناعي، مع الحد الأدنى من التدخل البشري. وتشمل الأمثلة روبوتات التنظيف المنزلية المستقلة والمركبات ذاتية القيادة.

## Slide 19
Chapter
07
www.midocean.ae
Collaborative Robots (Cobots): Robots working alongside humans in shared spaces, directly assisting human workers. Common in manufacturing and assembly lines.
Notes: الروبوتات التعاونية (Cobots): الروبوتات التي تعمل جنبًا إلى جنب مع البشر في المساحات المشتركة، وتساعد العمال البشريين بشكل مباشر. شائع في خطوط التصنيع والتجميع.

## Slide 20
Chapter
07
www.midocean.ae
2. Social Dynamics
Social Robots: Robots designed to engage with humans on a social or emotional level, such as companion robots for the elderly or educational robots for children.
Notes: 2. الديناميكيات الاجتماعية:
الروبوتات الاجتماعية: الروبوتات المصممة للتعامل مع البشر على المستوى الاجتماعي أو العاطفي، مثل الروبوتات المرافقة لكبار السن أو الروبوتات التعليمية للأطفال.

## Slide 21
Chapter
07
www.midocean.ae
Utility Robots: Focus on functional tasks without the need for social or emotional interaction, like warehouse robots or agricultural drones.
Notes: الروبوتات المساعدة: التركيز على المهام الوظيفية دون الحاجة إلى التفاعل الاجتماعي أو العاطفي، مثل روبوتات المستودعات أو الطائرات الزراعية بدون طيار.

## Slide 22
Chapter
07
www.midocean.ae
Fully Autonomous: Robots capable of performing tasks without human intervention, based on sensor data and pre-defined algorithms or learning.
3. Level of Autonomy
Notes: 3. مستوى الحكم الذاتي::
ذاتية التحكم بالكامل: روبوتات قادرة على أداء المهام دون تدخل بشري، بناءً على بيانات الاستشعار والخوارزميات المحددة مسبقًا أو التعلم.

## Slide 23
Chapter
07
www.midocean.ae
Semi-Autonomous: Robots that require occasional human guidance or decision-making to perform tasks.
Manual/Teleoperated: Robots fully controlled by humans, without autonomous capabilities.
Notes: شبه مستقلة: الروبوتات التي تتطلب توجيهًا بشريًا أو اتخاذ قرار في بعض الأحيان لأداء المهام.
يدوية/يتم تشغيلها عن بعد: روبوتات يتم التحكم فيها بالكامل من قبل البشر، دون قدرات ذاتية.

## Slide 24
Chapter
07
www.midocean.ae
4. Physical vs. Non-Physical Interaction
Physical Interaction (pHRI): Involves direct physical contact between the human and the robot. This includes collaborative manipulation of objects, physical assistance, and touch-based communication.
Notes: 4. التفاعل الجسدي مقابل التفاعل غير الجسدي
التفاعل الجسدي (pHRI): يتضمن الاتصال الجسدي المباشر بين الإنسان والروبوت. يتضمن ذلك التلاعب التعاوني بالأشياء والمساعدة الجسدية والتواصل القائم على اللمس.

## Slide 25
Chapter
07
www.midocean.ae
Non-Physical Interaction: Involves interaction through visual, auditory, or other non-tactile means, such as command and control through voice or graphical interfaces.
Notes: التفاعل غير الجسدي: يتضمن التفاعل من خلال وسائل بصرية أو سمعية أو غيرها من الوسائل غير اللمسية، مثل الأوامر والتحكم من خلال الواجهات الصوتية أو الرسومية.

## Slide 26
Chapter
07
www.midocean.ae
5. Purpose or Application Area
Industrial HRI: Interaction focused on manufacturing, assembly, and other industrial applications. Efficiency and safety are key concerns.
Medical HRI: Involves surgical robots, rehabilitation robots, and other healthcare applications. Precision and reliability are crucial.
Notes: 5. الغرض أو مجال التطبيق:
HRI الصناعي: يركز التفاعل على التصنيع والتجميع والتطبيقات الصناعية الأخرى. الكفاءة والسلامة هي الاهتمامات الرئيسية.
HRI الطبي: يتضمن الروبوتات الجراحية وروبوتات إعادة التأهيل وتطبيقات الرعاية الصحية الأخرى. الدقة والموثوقية أمر بالغ الأهمية.

## Slide 27
Chapter
07
www.midocean.ae
Service HRI: Encompasses service and assistance robots in retail, hospitality, and personal care. Usability and user experience are focal points.
Educational HRI: Robots used as teaching aids or learning platforms. Engagement and adaptability to different learning styles are important.
Notes: خدمة HRI: تشمل روبوتات الخدمة والمساعدة في مجال البيع بالتجزئة والضيافة والعناية الشخصية. تعتبر سهولة الاستخدام وتجربة المستخدم من النقاط المحورية.
HRI التعليمي: الروبوتات المستخدمة كوسائل تعليمية أو منصات تعليمية. تعد المشاركة والقدرة على التكيف مع أساليب التعلم المختلفة أمرًا مهمًا.

## Slide 28
Chapter
07
www.midocean.ae
Short-term Interaction: Brief encounters between humans and robots, typical in public spaces or for specific tasks.
Long-term Interaction: Prolonged engagement over time, common in companionship robots or when robots are integrated into daily routines.
6. Duration and Nature of Interaction
Notes: 6. مدة وطبيعة التفاعل:
التفاعل قصير المدى: لقاءات قصيرة بين البشر والروبوتات، نموذجية في الأماكن العامة أو لمهام محددة.
التفاعل طويل الأمد: التفاعل لفترة طويلة مع مرور الوقت، وهو أمر شائع في الروبوتات المرافقة أو عندما يتم دمج الروبوتات في الروتين اليومي.

## Slide 29
Chapter
08
www.midocean.ae
Notes: 6

## Slide 30
Chapter
08
www.midocean.ae
Color-Based Navigation for a Webots Robot Using Camera Input 3X3 Matrix
Analyze a 3x3 matrix around the central pixel and use the average color values for decision-making.
We'll calculate the average red, green, and blue values of the nine pixels at the center of the image and use these averages to determine the robot's movement.
-1 | 0 | +1
-1 | 0 | +1
-1 | 0 | +1
Notes: 6

## Slide 31
Chapter
08
www.midocean.ae
Main Simulation Loop to Analyze a 3x3 Pixel Matrix
-1 | 0 | +1
-1 | 0 | +1
-1 | 0 | +1
Notes: 6

## Slide 32
Chapter
08
www.midocean.ae
Main Simulation Loop to Analyze a 3x3 Pixel Matrix
# Adjust thresholds and decisions based on the average color
RED_THRESHOLD = 100
GREEN_THRESHOLD = 45
BLUE_THRESHOLD = 45
RED_THRESHOLD2 = 45
GREEN_THRESHOLD2 = 45
BLUE_THRESHOLD2 = 100
if avg_red > RED_THRESHOLD and avg_green < GREEN_THRESHOLD and avg_blue < BLUE_THRESHOLD:
left_motor.setVelocity(5) # Turn right
right_motor.setVelocity(-5)
elif avg_blue > BLUE_THRESHOLD2 and avg_green < GREEN_THRESHOLD2 and avg_red < RED_THRESHOLD2:
left_motor.setVelocity(-5) # Move backward
right_motor.setVelocity(-5)
else:
left_motor.setVelocity(5) # Move forward
right_motor.setVelocity(5)
Notes: 6

## Slide 33
Chapter
08
www.midocean.ae
Notes: 6

## Slide 34
Chapter
08
www.midocean.ae
Control the robot's speed based on color detection—moving faster if the color is green and very slowly if the color is red.
We are going to use Machine Learning Algorithm.
We are going to use Linear regression.
Let's assume:
A high "color score" represents green, encouraging faster movement.
A low "color score" represents red, dictating slower movement.
For simplicity, let's say our model has determined the relationship between color score and speed
as y=0.2x−1,
where y is the robot's speed,
and x is the color score (ranging from 0 for red to 5 for green).
Notes: 6

## Slide 35
Chapter
08
www.midocean.ae
Color Score: This is a conceptual representation of how "green" or "red" the camera's view is. (by averaging the RGB values).
Linear Regression Model: The model y = 0.2x - 1 is a simple formula we're using to decide the robot's speed based on the detected color. The specific coefficients (0.2 and -1) are placeholders for this example and would be determined through actual model training in a real-world application.
Speed Adjustment: The speed is adjusted based on the color score, with a higher score (more green) resulting in faster speed and a lower score (more red) resulting in slower speed or stopping.
Notes: 6

## Slide 36
Chapter
08
www.midocean.ae
from controller import Robot, Camera
# Initialization
robot = Robot()
timestep = int(robot.getBasicTimeStep())
# Assuming motor and camera initialization here
camera = robot.getDevice('camera')
camera.enable(timestep)
left_motor = robot.getDevice('left wheel motor')
right_motor = robot.getDevice('right wheel motor')
left_motor.setPosition(float('inf')) # Enable speed control
right_motor.setPosition(float('inf'))
left_motor.setVelocity(0) # Initially stop
right_motor.setVelocity(0)
Notes: 6

## Slide 37
Chapter
08
www.midocean.ae
while robot.step(timestep) != -1:
# Simulate getting a color score from the camera
# Let's say color score calculation logic has been applied here
# For simplification, assume we get this score directly from the camera
# A real implementation would involve analyzing the camera image
color_score = 3 # Placeholder for the actual color score calculation (0 = red, 5 = green)
# Apply the linear regression model
# For our example, the model equation is y = 0.2x - 1
predicted_speed = 0.2 * color_score - 1 # Simplified model to control speed based on color score
# Ensure the speed is within the robot's operational range
predicted_speed = max(-10, min(10, predicted_speed))
# Set the robot's motors to the predicted speed
left_motor.setVelocity(predicted_speed)
right_motor.setVelocity(predicted_speed)
Notes: 6

## Slide 38
Chapter
08
www.midocean.ae
A simple machine learning (ML) algorithm into the previous Webots robot navigation example introduces beginners to the intersection of robotics and ML. A straightforward approach is to use a decision tree classifier to decide the robot's movement based on the average color detected by the camera in a 3x3 pixel area. This example assumes you have basic data to train the classifier, representing average color values for different actions (move forward, turn right, move backward).
This example will be conceptual, as implementing a full ML pipeline involves steps (like data collection and model training) that go beyond the scope of running code directly in the Webots environment.
We are going to use a simple decision tree classifier using scikit-learn, a popular ML library for Python.
Machine Learning (ML) Algorithm
Notes: 6

## Slide 39
Chapter
08
www.midocean.ae
Step 1: Install scikit-learn
To install scikit-learn in Webots, or any Python environment within a simulation or application, you generally need to ensure that Python is correctly set up and that you have the necessary permissions to install additional libraries. Here's a step-by-step guide to installing scikit-learn for use with Webots:
Step 1: Identify Your Python Environment
First, determine which Python environment Webots is using. Webots can use a global Python installation or a virtual environment. You can specify or check this in the Webots preferences:
Open Webots.
Go to Tools > Preferences (on macOS, Webots > Preferences).
In the General tab, check the Python command setting to see which Python is being used.
Notes: 6

## Slide 40
Chapter
08
www.midocean.ae
Step 2: Install scikit-learn
Using a Global Python Installation
If Webots is configured to use your global Python installation, you can install scikit-learn using pip in your command line or terminal. Make sure you have pip installed and then run:
pip install scikit-learn
Using a Virtual Environment
If Webots is using a Python virtual environment:
Activate the Virtual Environment: First, you need to activate the virtual environment. Navigate to the virtual environment directory and activate it using the command line or terminal:
On Windows:
.\venv\Scripts\activate
Notes: 6

## Slide 41
Chapter
08
www.midocean.ae
Error : .\venv\Scripts\activate The system cannot find the path specified.
Solution:
cd path\to\my_project
1- Navigate to the Correct Directory
2- Verify the Path to the Virtual Environment
dir
If you don't see the venv folder, or if the Scripts directory is missing inside venv, the virtual environment was not created correctly.
Notes: 6

## Slide 42
Chapter
08
www.midocean.ae
3- Recreate the Virtual Environment (If Necessary)
If the virtual environment doesn't exist or was not created properly, you'll need to recreate it. Make sure you have Python installed, and then run:
python -m venv venv
This command creates a new virtual environment named venv in the current directory. After creation, try activating it again:
.\venv\Scripts\activate
Notes: 6

## Slide 43
Chapter
08
www.midocean.ae
4- Install scikit-learn
Once your virtual environment is activated, you can install scikit-learn as previously mentioned:
pip install scikit-learn
Notes: 6

## Slide 44
Chapter
08
www.midocean.ae
5- Verify Installation
To verify that scikit-learn has been successfully installed, you can run a small Python script to import scikit-learn and print its version:
First: Type python
Then use the following command
import sklearn
print(sklearn.__version__)
Exit the Python Interactive Shell
Notes: 6

## Slide 45
Chapter
08
www.midocean.ae
6- Use scikit-learn in Your Webots Project
Able to use scikit-learn in your Webots projects. You can import scikit-learn in your Python controller scripts and use its functionalities as needed.
Notes: 6

## Slide 46
Chapter
08
www.midocean.ae
2- Simulated Training Data
# Example training data: [avg_red, avg_green, avg_blue, action]
# Actions: 0 - Move Forward, 1 - Turn Right, 2 - Move Backward
training_data = [
[150, 30, 30, 1], # Red-like colors prompt turning right.
[30, 30, 150, 2], # Blue-like colors prompt moving backward.
[80, 80, 80, 0], # Neutral colors prompt moving forward.
# Add more samples as needed
]
For simplicity, let's simulate training data. In a real scenario, you'd collect data based on the robot's observations and corresponding actions.
Notes: 6

## Slide 47
Chapter
08
www.midocean.ae
Step 3: Train a Simple Decision Tree Classifier
from sklearn.tree import DecisionTreeClassifier
import numpy as np
# Prepare training data
X = np.array([x[:-1] for x in training_data]) # Color components
y = np.array([x[-1] for x in training_data]) # Actions
# Train the classifier
clf = DecisionTreeClassifier()
clf.fit(X, y)
Notes: 6

## Slide 48
Chapter
08
www.midocean.ae
Step 4: Integrate the Classifier into the Webots Code
# Main simulation loop with ML decision-making
while robot.step(TIME_STEP) != -1:
# Image processing to get the average color...
avg_red, avg_green, avg_blue = get_average_color(camera)
# Predict the action using the trained classifier
action = clf.predict([[avg_red, avg_green, avg_blue]])[0]
# Define robot movements based on the predicted action
if action == 0: # Move Forward
set_velocity(left_motor, right_motor, 5, 5)
elif action == 1: # Turn Right
set_velocity(left_motor, right_motor, 5, -5)
elif action == 2: # Move Backward
set_velocity(left_motor, right_motor, -5, -5)
Notes: 6

## Slide 49
Chapter
08
www.midocean.ae
Understanding Decision Trees
A decision tree is a flowchart-like tree structure where an internal node represents a feature(or attribute), the branch represents a decision rule, and each leaf node represents the outcome. In the context of our robot, the features are the average red, green, and blue (RGB) color values of a 3x3 pixel area in the camera's field of view, and the outcome is the action the robot should take (move forward, turn right, move backward).
Notes: 6

## Slide 50
Chapter
08
www.midocean.ae
Example 2 : Decision Tree Classifier
This example assumes that we have a pretrained decision tree model. The training of the model is conceptually described, but in practice, you would need to collect data, label it, and train the model using a tool like scikit-learn in a Python environment outside of Webots.
Notes: 6

## Slide 51
Chapter
08
www.midocean.ae
Step 1: Simulated Training Data and Model Training
First, you would collect data and train your model. This step is conceptual and would typically happen outside of your Webots project using scikit-learn or a similar library:
# Simulate training data collection
# Features: Average R, G, B values; Label: Action (0=Forward, 1=Right, 2=Backward)
training_data = [
[120, 40, 40, 1], # Red objects mean turn right
[40, 40, 120, 2], # Blue objects mean move backward
[80, 110, 90, 0], # Neutral colors mean move forward
]
# Normally, here you would split your data into features (X) and labels (y),
# train a decision tree model using scikit-learn, and then save the model.
# For this example, assume we have a trained model ready to use.
Notes: 6

## Slide 52
Chapter
08
www.midocean.ae
Step 2: Webots Code Integrating the Trained Model
Now, integrating the model into your Webots controller script. This part simulates loading a pretrained model and using it within the main robot control loop:
Notes: 6

## Slide 53
Chapter
08
www.midocean.ae
from controller import Robot, Camera, Motor
import numpy as np
# Define the robot's actions based on prediction
def robot_action(action, left_motor, right_motor):
speed = 5
if action == 0: # Move forward
left_motor.setVelocity(speed)
right_motor.setVelocity(speed)
elif action == 1: # Turn right
left_motor.setVelocity(speed)
right_motor.setVelocity(-speed)
elif action == 2: # Move backward
left_motor.setVelocity(-speed)
right_motor.setVelocity(-speed)
# Main robot control code
TIME_STEP = 64
robot = Robot()
# Initialize camera
camera = robot.getDevice('camera')
camera.enable(TIME_STEP)
Notes: 6

## Slide 54
Chapter
08
www.midocean.ae
# Initialize motors
left_motor = robot.getDevice('left wheel motor')
right_motor = robot.getDevice('right wheel motor')
left_motor.setPosition(float('inf'))
right_motor.setPosition(float('inf'))
left_motor.setVelocity(0)
right_motor.setVelocity(0)
# Assume 'model' is our pretrained decision tree classifier
# For educational purposes, we will simulate its predictions based on color thresholds
while robot.step(TIME_STEP) != -1:
image = camera.getImage()
width = camera.getWidth()
height = camera.getHeight()
Notes: 6

## Slide 55
Chapter
08
www.midocean.ae
# Center coordinates of the image
centerX = width // 2
centerY = height // 2
# Calculate the average color of the central 3x3 pixels
avg_color = np.zeros(3)
for dx in range(-1, 2):
for dy in range(-1, 2):
# Correcting the method to get RGB components for each pixel
red = camera.imageGetRed(image, width, centerX + dx, centerY + dy)
green = camera.imageGetGreen(image, width, centerX + dx, centerY + dy)
blue = camera.imageGetBlue(image, width, centerX + dx, centerY + dy)
avg_color += np.array([red, green, blue])
avg_color /= 9 # Average RGB values
Notes: 6

## Slide 56
Chapter
08
www.midocean.ae
# Determine action based on average color
# Red detection
if avg_color[0] > 100 and avg_color[1] < 50 and avg_color[2] < 50:
action = 1 # Turn right due to red
# Green detection
elif avg_color[1] > 100 and avg_color[0] < 50 and avg_color[2] < 50:
action = 0 # Move forward due to green
else:
action = 2 # Move backward for any other color as default
# Execute the action
robot_action(action, left_motor, right_motor)
Notes: 6

## Slide 57
Thank You