## Slide 1
Prepared by Dr. Injy Nashaat
Process Selection
and Facility Layout
Lecture 6

## Slide 2: Process Selection
Process selection
  Refers to deciding on the way production of goods or services will be organized
  It has major implications for
    Capacity planning
    Layout of facilities
    Equipment
    Design of work systems

## Slide 3: Process Selection and System Design
Forecasting
Product and Service Design
Technological Change
Capacity Planning
Process Selection
Facilities and Equipment
Layout
Work Design

## Slide 4: Process Strategy
Key aspects of process strategy:
  Capital intensity
    The mix of equipment and labor that will be used by the organization
  Process flexibility
    The degree to which the system can be adjusted to changes in requirements due to such factors as
      Product processing and service design changes
      Volume changes
      Changes in technology

## Slide 5: Process Selection (cont.)
Two key questions in process selection:
How much variety will the process need to be able to handle?
How much volume will the process need to be able to handle?
Job Shop
Repetitive
Batch
Continuous

## Slide 6: Types of Processing
 | Job Shop | Batch | Repetitive/ Assembly | Continuous
Description | Customized goods or services | Semi- standardized goods or services | Standardized goods or services | Highly standardized Goods or services
Advantages | Able to handle a wide variety of work | Flexibility; easy to add or change products or services | Low unit cost, high volume, efficient | Very efficient, very high volume
Disadvantages | Slow, high cost per unit, complex planning and scheduling | Moderate cost per unit, moderate scheduling complexity | Low flexibility, high cost of downtime | Very rigid, lack of variety, costly to change, very high cost of downtime

## Slide 7: Sustainable Production of Goods and Services
There is increasing pressure for organizations to operate sustainable production processes
According to the Lowell Center for Sustainable Production:
  “Sustainable Production is the creation of goods and services using processes and systems that are: non-polluting; conserving of energy and natural resources; economically efficient; safe and healthful for workers, communities, and consumers; and socially and creatively rewarding for all working people.”

## Slide 8: Sustainable Production of Goods and Services (cont.)
Reduce/recycle waste and ecologically incompatible parts and byproducts
Eliminate hazardous chemicals/physical agents
Conserve energy and materials
Redesign workspace to minimize hazards to the workers and the environment

## Slide 9: Process and Information Technology
Process and information technology can have a major impact on costs, productivity and competitiveness:
  Process technology
    Methods, procedures, and equipment used to produce goods and provide services
  Information technology
    The science and use of computers and other electronic equipment to store, process, and send information

## Slide 10: The Need to Manage Technology
Process technology and information technology can have a profound impact on:
  Costs
  Productivity
  Competitiveness

## Slide 11: Automation
Automation
  Machinery that has sensing and control devices that enable it to operate automatically
    Fixed automation
    Programmable automation
    Flexible automation

## Slide 12: Programmable Automation
  Involves the use of high-cost, general-purpose equipment controlled by a computer program that provides both the sequence of operations and specific details about each operation
    Computer-Aided Manufacturing (CAM)
      The use of computers in process control, ranging from robots to automated quality control
    Numerically Controlled (N/C) Machines
      Machines that perform operations by following mathematical processing instructions
    Robot
      A machine consisting of a mechanical arm, a power supply, and a controller

## Slide 13: Various types of Robots
Robots that follow a fixed set of instructions
Programmable robots
  Repeat a set of movements after being led through a sequence
  Follow instructions from a computer
Collaborative robots, also known as cobots

## Slide 14: Flexible Automation
  Evolved from programmable automation. It uses equipment that is more customized than that of programmable automation. A key difference between the two is that flexible automation requires significantly less changeover time.
    FMS (Flexible Manufacturing System)
      A group of machines designed to handle intermittent processing requirements and produce a variety of similar products
    CIM (Computer Integrated Manufacturing)
      A system for linking a broad range of manufacturing activities through an integrated computer system

## Slide 15: Flexible Manufacturing System (FMS)
  A group of machines designed to handle intermittent processing requirements and produce a variety of similar products
    Have some of the benefits of automation and some of the flexibility of individual, or stand-alone, machines
    Includes supervisory computer control, automatic material handling, and robots or other automated processing equipment

## Slide 16: Computer Integrated Manufacturing (CIM)
  A system for linking a broad range of manufacturing activities through an integrated computer system
    Activities include
      Engineering design
      FMS
      Purchasing
      Order processing
      Production planning and control
    The overall goal of CIM is to link various parts of an organization to achieve rapid response to customer orders and/or product changes, to allow rapid production, and to reduce indirect labor costs
    Internet of Things (IoT) further enhances connectivity of devices through internet

## Slide 17: Facilities Layout
Layout
  The configuration of departments, work centers, and equipment, with particular emphasis on movement of work (customers or materials) through the system
  Facilities layout decisions arise when:
    Designing new facilities
    Re-designing existing facilities

## Slide 18: The Need for Layout Planning
Inefficient operations
  High cost
  Bottlenecks
Accidents or safety hazards
Changes in product or service design
Introduction of new products or services
Changes in output volume or product mix
Changes in methods or equipment
Changes in environmental or other legal requirements
Morale problems

## Slide 19: Layout Design Objectives
Basic objective
  Facilitate a smooth flow of work, material, and information through the system
Supporting objectives
  Facilitate product or service quality
  Use workers and space efficiently
  Avoid bottlenecks
  Minimize material handling costs
  Eliminate unnecessary movement of workers or material
  Minimize production time or customer service time
  Design for safety

## Slide 20: Basic Layout Types
Product layouts
Process layouts
Fixed-position layout
Combination layouts

## Slide 21: Repetitive Processing: Product Layouts
Product layout
  Layout that uses standardized processing operations to achieve smooth, rapid, high-volume flow
Used for Repetitive Processing
Repetitive or Continuous
Raw materials
or customer
Finished item
Station
2
Station
3
Station
4
Material
and/or labor
Material
and/or labor
Material
and/or labor
Material
and/or labor
Station
1

## Slide 22: Process Types
A repetitive process
A continuous process
A job shop
A batch process

## Slide 23: Product Layouts: Advantages
Advantages
High rate of output
Low unit cost
Labor specialization
Low material handling cost per unit
High utilization of labor and equipment
Established routing and scheduling
Routine accounting, purchasing, and inventory control

## Slide 24
Disadvantages
Creates dull, repetitive jobs
Poorly skilled workers may not maintain equipment or quality of output
Fairly inflexible to changes in volume or product or process design
Highly susceptible to shutdowns
Preventive maintenance, capacity for quick repair, and spare-parts inventories are necessary expenses
Individual incentive plans are impractical
Right-sized equipment tends to be larger than equipment used in untraditional process layouts
Product Layouts: Disadvantages

## Slide 25: Non-repetitive Processing: Process Layouts
Process layouts
  Layouts that can handle varied processing requirements
Used for Intermittent processing
Job Shop or Batch
Dept. A
Dept. B
Dept. D
Dept. C
Dept. F
Dept. E

## Slide 26: Process Layouts: Advantages (cont.)
Advantages
Can handle a variety of processing requirements
Not particularly vulnerable to equipment failures
General-purpose equipment is often less costly and easier to maintain
It is possible to use individual incentive systems

## Slide 27
In-process inventories can be high
Routing and scheduling pose continual challenges
Equipment utilization rates are low
Material handling is slow and inefficient
Reduced spans of supervision
Special attention necessary for each product or customer
Accounting, inventory control, and purchasing are more involved
Process Layouts: Disadvantages (cont.)

## Slide 28: Fixed Position Layouts
Fixed position layout
  Layout in which the product or project remains stationary, and workers, materials, and equipment are moved as needed
    Large construction projects
    Shipbuilding/aircraft manufacturing
    Space mission

## Slide 29: Combination Layouts
Some operational environments use a combination of the three basic layout types:
  Hospitals
  Supermarket
  Shipyards
Some organizations are moving away from process layouts to capture the benefits of product layouts
  Cellular manufacturing
  Flexible manufacturing systems

## Slide 30: Cellular Layouts
Cellular production
  Layout in which workstations are grouped into a cell that can process items that have similar processing requirements
    Groupings are determined by the operations needed to perform the work for a set of similar items, part families, that require similar processing
    The cells become, in effect, miniature versions of product layouts
    Enables companies to produce a variety of products with very little waste

## Slide 31: Group Technology
  The grouping into part families of items with similar design or manufacturing characteristics
    Design characteristics:
      Size
      Shape
      Function
    Manufacturing or processing characteristics
      Type of operations required
      Sequence of operations required
  Requires a systematic analysis of parts to identify the part families

## Slide 32: Service Layouts
Service layouts can be categorized as: product, process, or fixed position
Service layout requirements are somewhat different due to such factors as:
  Degree of customer contact
  Degree of customization
Common service layouts:
  Warehouse and storage layouts – minimize item movement
  Retail layouts – influence customers into buying more
  Office layouts – increase employee interactions

## Slide 33: Designing Product Layouts: Line Balancing
The goal of a product layout is to arrange workers or machines in the sequence that operations need to be performed

## Slide 34: Line Balancing
  The process of assigning tasks to workstations in such a way that the workstations have approximately equal time requirements
  Goal:
    Obtain task grouping that represents approximately equal time requirements, since this minimizes idle time along the line and results in a high utilization of equipment and labor
  Why is line balancing important?
    It allows us to use labor and equipment more efficiently
    To avoid fairness issues that arise when one workstation must work harder than another

## Slide 35: Cycle Time
Cycle time
  The maximum time allowed at each workstation to complete its set of tasks on a unit
  Cycle time also establishes the output rate of a line

## Slide 36: Precedence Diagram
Precedence diagram
  A diagram that shows elemental tasks and their precedence requirements

## Slide 37: Assigning Tasks to Workstations
Some heuristic (intuitive) rules:
  Assign tasks in order of most following tasks
    Count the number of tasks that follow
  Assign tasks in order of greatest positional weight
    Positional weight is the sum of each task’s time and the times of all following tasks

## Slide 38: Designing Process Layouts
The main issue in designing process layouts concerns the relative placement of the departments
Measuring effectiveness
  A major objective in designing process layouts is to minimize transportation cost, distance, or time

## Slide 39: Information Requirements
In designing process layouts, the following information is required:
  A list of departments to be arranged and their dimensions
  A projection of future workflows between the pairs of work centers
  The distance between locations and the cost per unit of distance to move loads between them
  The amount of money to be invested in the layout
  A list of any special considerations
  The location of key utilities, access and exit points, etc.

## Slide 40
Thank You